Recommended Practices Guide for Geometric Tolerances

December 6, 2004

Note: This is a draft document containing proposals for the recommended usage of the Geometric Tolerances as defined in AIC 519. This document will continue to be refined and extended. Please forward any issues, questions or suggestions to the authors below.

Contacts

David Briggs

Boeing Commercial Airplanes

P.O. Box 2707 M/S 2R-97

Seattle, WA 98124-2207 USA

david.d.briggs@boeing.com

Tom Hendrix

Boeing Commercial Airplanes

P.O. Box 2707 M/S 2R-97

Seattle, WA 98124-2207 USA

thomas.e.hendrix@boeing.com

Table of Contents

1 Introduction	1

2 Scope	1

3 Fundamental Concepts	2

3.1 Associating tolerances with Features	2

3.2 Datum Systems	3

3.2.1 Datums	3

3.2.2 Datums features	4

3.2.3 Datum targets	5

3.2.4 Modified Datum Reference	8

3.3 Modified Tolerance	8

3.4 Multiple Toleranced Features	9

3.5 Composite Tolerances	11

4 Part 21 Example of Typical Tolerance	12

5 Usage	13

5.1 Angularity	14

5.2 Circular runout	14

5.3 Circularity	14

5.4 Coaxiality	15

5.5 Concentricity	15

5.6 Cylindricity	15

5.7 Flatness	15

5.8 Parallelism	15

5.9 Perpendicularity	15

5.10 Position	15

5.11 Profile of a line	15

5.12 Profile of a surface	16

5.13 Roundness	16

5.14 Straightness	16

5.15 Symmetry	16

5.16 Total runout	16

6 Entity Definitions	16

7 Sample Part 21 File	19

# Introduction

Tolerances treat the uncertainty with which the realized shape or measurements of a real manufactured object compare to their design ideals. If all parts could be manufactured perfectly as designed, there would be no need for tolerancing practices. However, it is certain that this cannot be done for finite cost in any but the most trivial cases. In the drawing world, tolerances are noted on the drawing per standard notations such as ANSI Y14.5 or ISO 1101.

There are two main classes of tolerances, dimensional and geometric. Dimensional tolerances are addressed in “Recommended Practices for Dimensions and Dimensional Tolerances” written by Markus Hauser, Mike Strub and Tom Hendrix, dated April 18, 2000.

Geometric tolerances are the more complex of these two types. Geometric tolerances provide more flexible means for controlling shape than do dimensional tolerances.  They achieve this by enabling tolerances to be defined independently of explicit dimensions. This enables tolerances to be specified that are more closely related to the functional requirements of the design, such as strength and fit. These tolerances are the subject of this recommended practices guide.

# Scope

This document covers the recommended usage and implementation of geometric tolerances defined in Application Integrated Construct (AIC) 519. This AIC is the result of a harmonization effort between AP214 and AP224. This AIC is also the basis for the tolerance modules to be included in AP203 Edition 2.

This document is not intended as a primer on geometric tolerancing. The explanations included are only provided to relate common tolerancing techniques to the STEP entity structures. This is not a comprehensive coverage of any existing draughting standard but does provide a capability to exchange a variety of typical models. Future versions of this document will address additional capabilities.

This document covers the application of tolerances to boundary representation solid models. The application of tolerances to wireframe or other geometric models is not covered here.

The tolerances addressed in this document are:

Angularity

Circular runout

Circularity

Coaxiality

Concentricity

Cylindricity

Flatness

Parallelism

Perpendicularity

Position

Profile of a line

Profile of a surface

Roundness

Straightness

Symmetry

Total runout

Tolerance modifiers (Maximum and minimum material condition, regardless of feature size and projected tolerance zone) are also addressed.

# Fundamental Concepts

A geometric tolerance describes a constraint on the acceptable deviation of a manufactured object from the ideal design. Tolerances are applied to the geometric features of a part, such as faces and holes.

The fundamental principles of geometric tolerances can be found in national and international standards such as ANSI Y14.5M-1994 or ISO 5459-1981.

There are several subtypes of the geometric_tolerance entity, which are not mutually exclusive. For example, tolerances that reference datums are of type geometric_tolerance_with_datum_reference. Tolerances that include a modifier such as maximum material condition are of type modified_geometric_tolerance. Many typical engineering tolerances combine these. In these cases, complex entities instances will occur in the Part 21 file.

## Associating tolerances with Features

In STEP, the tolerance entities are associated with a shape_aspect that identifies the toleranced feature. The feature is identified by a shape_aspect which has a representation. In the case of a solid boundary representation model, the feature of the part is represented by one or more topological_representation_items such as advanced_face entities. For example, a through hole in a solid model might be represented by two semi-circular surfaces, each an advanced_face entity. These topological_representation_items are collected together by a shape_representation which is representation of the shape_aspect for the feature. This shape_representation is typically a connected_face_set and shall share the same geometric_representation_context as the solid. See Figure 1 for an example of how the tolerance entities are related to the shape elements of the toleranced feature.

Figure 1 Relating a typical tolerance to a feature's representatation

In the case where the tolerance applies to more than one feature, such as a pattern of holes, the a composite_shape_aspect is used rather than shape_aspect. The composite_shape_aspect is related to the tolerance in the same manner as the shape_aspect.

## Datum Systems

Some types of tolerances refer to one or more datums in order to represent the requirements on the shape. Datum systems are related datums that provide a reference system for describing requirements on the product shape. Datum systems are defined by datum entities and their corresponding datum_feature entities.

### Datums

A datum is a theoretically exact geometric reference, such as an exact point, axis or plane, to which toleranced features are related. A datum is the origin from which the location or geometric characteristics of features of a part are established. A datum may be based on one or more datum features of a part (Definition from ISO 5459-1981).

Since the datum is intended to be the idealized geometry, unbounded geometric entities are used as the representation_item. For a boundary representation solid model, these entities are planes, lines, etc.

### Datums features

Datum features are tangible features of a part, for example a face that provides a reference system for measurements of the actual part. Datum features must lie on the physical boundary of the shape. Consequentially, datum_feature entities are related to topological entities that represent those boundaries in the solid model such as an advanced_face.

Where tolerances contain references to datums, the tolerance entity is considered a subtype of geometric_tolerance_with_datum_reference. It thus inherits the datum_system attribute, which is the mechanism for pointing to the datum_reference entities.

In the figure below, the tolerance entity, e.g., a positional_tolerance uses three datum_reference entities to describe the datum system for the tolerance. The datum_reference points to a datum entity, which in turns points to the geometric elements that represents the datum. The datum_feature, i.e., the feature on the part corresponding to the datum, references the topological elements of the solid model representing that feature, i.e., the advanced_face entities. See Figure 2 for details.

Figure 2 Datums and datum_features

### Datum targets

A datum_target designates a specific point, line or area of contact on a part that is used in establishing a data reference frame (definition from ANSI Y14.5). It differs from a datum_feature in that it identifies a restricted region of a feature, i.e. a point, line or area of a surface rather than a topological feature. Typically, two or more datum_target elements are used to define a  datum

A datum_target is represented by a placed_datum_target_feature. The placed_datum_target_feature is related to datum that it helps establish via the mechanism depicted in Figure 3 below. The point, line or area of the datum_target is represented by a shape_representation_with_parameters containing a measure_representation. See Figure 3.

Figure 3 Datum targets

### Modified Datum Reference

A reference to a datum can contain a modifier that specifies a condition, such as maximum material condition. For example, a control frame whose visual representation is depicted in Figure 4 is represented in a similar manner to an unmodified datum reference except that instead of a datum_reference, the subtype referenced_modified_datum is used. The modifier attribute contains the condition information as a value of type limit_condition.

Figure 4 Modified datum reference

## Modified Tolerance

Certain engineering tolerances are modified by adding conditions. The conditions identified in STEP are defined in the limit_condition enumerated type. The values defined are: maximum_material_condition, least_material_condition and regardless_of_feature_size. These are referred to in tolerance standards as MMC, LMC and RFS respectively.

When the tolerance is modified, the tolerance entity is considered a subtype of modified_geometric_tolerance and thus inherits the modifier attribute. The modifier attribute contains the enumerated value of type condition. The general structure is depicted in Figure 5.

Figure 5 Modified Tolerance

## Toleranced Features with multiple elements

In many cases, a tolerance is applied to a feature of the part that is comprised of multiple shape elements. For example, a tolerance applied to two disjoint, parallel faces of a part that form one of the sides. In these cases, a composite_shape_aspect is used to relate the various features together and the tolerance is applied to the composite_shape_aspect. See Figure 6 for details.

Figure 6 Tolerancing multiple features

## Tolerancing patterns of Features

In addition to tolerancing an individual feature, tolerances can also be applied to a pattern of features. Typical usages include applying the same tolerance to a pattern of holes or slots. See Figure 7 for an example of a typical control frame that applies to a pattern of features .

Figure 7 Pattern Control Frame

In the pattern of features, each individual feature (e.g., hole or slot) is a shape_aspect. A composite_shape_aspect is used to relate the shape_aspects together and the tolerance is applied to the composite_shape_aspect. See Figure 6 for details.

## Composite Tolerances

Some tolerances have multiple requirements as represented by a multiple frame tolerance control frame whose visual representation is shown in Figure 7.

Figure 8 Composite Control Frame

This is implemented by creating the appropriate geometric_tolerance entity for each frame. The geometric_tolerance entities are then related via a geometric_tolerance_relationship. The description attribute of the geometric_tolerance_relationship entity shall contain the value “Composite Tolerance”. See Figure 8 for the structure of the tolerance depicted in Figure 7.

In the geometric_tolerance_relationship entity, the upper frame is the “relating” reference and the lower frame is the “related” reference. For tolerances with more than two frames, multiple geometric_tolerance_relationship entities are used to relate the frames together. For example, a tolerance with three frames would require two geometric_tolerance_relationship entities: one relating the top (“relating”) and middle frames (“related”), the second relating the middle (“relating”) and the bottom (“related”) frames. These relationships will allow the receiver to reconstruct the semantic relationships as well as the visual representation.

Figure 9 Structure of Composite Tolerance

## Tolerances on assemblies (Under construction)

In some engineering situations, tolerances are associated to the assembly level product. The following sections examine different cases of toleranced assemblies.

### Toleranced placement of a component

The placement and/or orientation of a component in an assembly might be controlled by a tolerance. In this case, the tolerance needs to be associated with the instance of the component, i.e., the next_assembly_usage_occurrence (or other usage_occurrance). The tolerance is associated with a shape_aspect which is related to the NAUO through a product_definition_shape. This provides the link to the instance of the component. When the tolerance is associated with a specific feature on the component, this shape_aspect is related to the shape_aspect in the component that defines the shape of the feature. See Figure 10 for details.

Figure 10 Tolerance on component instance

### Assembly features

Another case is a tolerance on a feature that exists in the context of the assembley. An example is a hole drilled on assembly. In this case the shape of the toleranced feature, e.g., the hole, is defined as part of the shape-representation of the assembly. A shape_aspect defining the shape of the feature is associated with the product_definition_shape of the assembly. The tolerance is associated with this shape-aspect. See Figure 11 for details.

Figure 11 Tolerance on Assembly Feature

## Choice of dimensioning standards

Different dimensioning standards define the visual representation and interpretation of the symbology of the tolerances. In order for the receiving system to create the correct visual representation of the tolerance, the dimensioning standard must be known. This information is captured as an applied_document_reference which applies the referenced document, i.e., the dimensioning standard, to the product_definition of the part. This is shown in Figure 9.

Figure 12 Choice of dimensioning standard

The following standard strings should be used for the document identifier:

“ASME Y14.41-2003”

“ASME Y14.5M-1994”

“ISO 5459-1981”

Per the tolerancing harmonization project, the object role for the document has the string value of "dimensioning standard".

# Part 21 Example of Typical Tolerance

Consider an example of a location tolerance on a hole whose visual representation as a control frame is:

Interpreting this in STEP (reading the control frame left to right) the location tolerance is a position_tolerance, locating a cylindrical feature, with a tolerance value of 0.1, with a modifier condition of maximum material condition, referencing datums A, B and C in that order.

Using the AIC 519 schema, this would be a complex entity instance comprising a

geometric_tolerance AND

position_tolerance AND

modified_geometric_tolerance AND

geometric_tolerance_with_datum_reference

In the Part 21 file, this would appear as:

#1000=(GEOMETRIC_TOLERANCE (‘position’, ‘Positional tolerance for hole 1’, 1045, #1008)

GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE ((#1002, #1003, #1004))

MODIFIED_GEOMETRIC_TOLERANCE (.MAXIMUM_MATERIAL_CONDITION.)

POSITIONAL_TOLERANCE ());

The hole feature would be defined by:

#1008=SHAPE_ASPECT('Hole1', 'One inch top hole', #40, .T.);

#1018=PROPERTY_DEFINITION('Feature shape','Shape of feature',#1008);

#1009=SHAPE_DEFINITION_REPRESENTATION(#1018,#1001) ;

#1001=SHAPE_REPRESENTATION('Representation of hole',(#93),#49) ;

where #93 is the ADVANCED_FACE for the inside surface of the hole.

The datum references A, B and C would be referenced by:

#1002=DATUM_REFERENCE(1,#1005);

#1003=DATUM_REFERENCE(2,#1006);

#1004=DATUM_REFERENCE(3,#1007);

The DATUM entities are defined and related to the model geometry via:

#1005=DATUM('Datum A','Datum A',#40,.F.,'A');

#1058=PROPERTY_DEFINITION('Datum geometry','Geometric plane of datum',#1005);

#1059=SHAPE_DEFINITION_REPRESENTATION(#1058,#1061) ;

#1061=SHAPE_REPRESENTATION('Representation of datum plane',(#98),#49) ;

#1006=DATUM('Datum B','Datum B',#40,.F.,'B');

#1068=PROPERTY_DEFINITION('Datum geometry','Geometric plane of datum',#1006);

#1069=SHAPE_DEFINITION_REPRESENTATION(#1068,#1071) ;

#1071=SHAPE_REPRESENTATION('Representation of datum plane',(#214),#49) ;

#1007=DATUM('Datum C','Datum C',#40,.F.,'C');

#1078=PROPERTY_DEFINITION('Datum geometry','Geometric plane of datum',#1007);

#1079=SHAPE_DEFINITION_REPRESENTATION(#1078,#1081) ;

#1081=SHAPE_REPRESENTATION('Representation of datum plane',(#190),#49) ;

where #98, #214 and #190 are the plane entities representing the datum planes in the B-rep solid model.

# Usage

This section contains the recommendation on population of the values for the tolerance entities.

Since the geometric_tolerance entity is the supertype for the tolerance entities, most of the attributes are inherited from it. The recommended values for the geometric_tolerance entity are:

| Name | Explanation |
| --- | --- |
| Geometric_tolerance |  |
| name | One of the following strings: angularity circular runout coaxiality concentricity cylindricity flatness parallelism perpendicularity position linear profile surface profile roundness straightness symmetry total runout |
| description | No requirement defined – instantiate this attribute with an empty string. |
| magnitude | The measure_with_unit that contains the tolerance value.. |
| toleranced_shape_aspect | The shape_aspect the tolerance is associated to. The type of shape_aspect varies depending on the type of tolerance. |

## Angularity

The tolerance is related to the shape_aspect referencing the advanced_face whose underlying geometry is planar that is being toleranced to the datum.

## Circular runout

The tolerance is related to the shape_aspect referencing the advanced_face(s) whose underlying geometry are the cylindrical_surface(s) that are being toleranced.

## Circularity

See Roundness, Section 5.13

## Coaxiality

This is the ISO term for concentricity. See 5.5.

## Concentricity

The tolerance is related to the shape_aspect referencing the advanced_face(s) whose underlying geometry are the cylindrical_surface(s) that are being toleranced.

## Cylindricity

The tolerance is related to the shape_aspect referencing the advanced_face(s) whose underlying geometry are the cylindrical_surface(s) that are being toleranced.

## Flatness

The tolerance is related to the shape_aspect referencing the advanced_face whose underlying geometry is planar that is being toleranced to the datum.

## Parallelism

The tolerance is related to the shape_aspect referencing the advanced_face whose underlying geometry is planar that is being toleranced to the datum.

## Perpendicularity

The tolerance is related to the shape_aspect referencing the advanced_face whose underlying geometry is planar that is being toleranced to the datum.

## Position

Position tolerances can be applied to several types of features. When the feature is a hole, the tolerance is related to the shape_aspect referencing the advanced_face(s) whose underlying geometry is the cylindrical_surface that is being toleranced. For other features, such as tabs, the tolerance is related to the composite_shape_aspect that defines the feature.

## Profile of a line

The tolerance is applied to a shape_aspect that is related to another shape_aspect containing a plane or an intersection_curve. The two shape_aspect entities are related via a shape_aspect_relationship whose name attribute is ’affected plane association’, when the related shape-aspect corresponds to the reference plane, or ’resulting intersection curve association’, when the related shape-aspect corresponds to one of the intersection curves.

## Profile of a surface

The tolerance is applied to a shape_aspect that references an advanced_face whose underlying geometry is planar that is being toleranced.

## Roundness

The tolerance is related to the shape_aspect referencing the advanced_face whose underlying geometry is the cylindrical_surface that is being toleranced. Roundness is the ISO term for what ASME Y14.5 refers to as circularity.

## Straightness

The tolerance is applied to a shape_aspect that references an advanced_face whose underlying geometry is planar that is being toleranced.

## Symmetry

Where the tolerance is applied to a cylinder, the tolerance entity is related to a shape_aspect referencing the advanced_face(s) whose underlying geometry is the cylindrical_surface. Where the tolerance is applied to opposing faces, the tolerance entity is related to a shape_aspect referencing the advanced_faces whose underlying geometry are the opposing planar faces.

## Total runout

The tolerance is applied to a shape_aspect that references an advanced_face whose underlying geometry is the surface that is being toleranced. The surface may be cylindrical or planar.

# Entity Definitions

ENTITY angularity_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) < 3;

END_ENTITY;

ENTITY circular_runout_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 2;

END_ENTITY;

ENTITY coaxiality_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 2;

END_ENTITY;

ENTITY common_datum

SUBTYPE OF (composite_shape_aspect, datum);

WHERE

WR1: SIZEOF (SELF.component_relationships) = 2;

WR2: SIZEOF ( QUERY ( sar <* SELF.component_relationships| NOT (('AIC_GEOMETRIC_TOLERANCES.DATUM' IN TYPEOF (sar.related_shape_aspect)) AND NOT ('AIC_GEOMETRIC_TOLERANCES.COMMON_DATUM' IN TYPEOF (sar.related_shape_aspect))) )) = 0;

END_ENTITY;

ENTITY concentricity_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) = 1;

END_ENTITY;

ENTITY cylindricity_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY flatness_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY geometric_tolerance;

name : label;

description : text;

magnitude : measure_with_unit;

toleranced_shape_aspect : shape_aspect;

WHERE

WR1: ('NUMBER' IN TYPEOF (magnitude\measure_with_unit.value_component)) AND (magnitude\measure_with_unit.value_component >= 0.0);

END_ENTITY;

ENTITY line_profile_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF)) OR ( SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3);

WR2: SIZEOF ( QUERY ( sar <* USEDIN (SELF\geometric_tolerance.toleranced_shape_aspect, 'AIC_GEOMETRIC_TOLERANCES.' + 'SHAPE_ASPECT_RELATIONSHIP.RELATING_SHAPE_ASPECT')| (sar.name IN [ 'affected plane association', 'resulting intersection curve association' ]) )) = 1;

END_ENTITY;

ENTITY parallelism_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) < 3;

END_ENTITY;

ENTITY perpendicularity_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3;

END_ENTITY;

ENTITY position_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF)) OR ( SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3);

END_ENTITY;

ENTITY roundness_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY straightness_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY surface_profile_tolerance

SUBTYPE OF (geometric_tolerance);

WHERE

WR1: NOT ('AIC_GEOMETRIC_TOLERANCES.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF)) OR ( SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3);

END_ENTITY;

ENTITY symmetry_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3;

END_ENTITY;

ENTITY total_runout_tolerance

SUBTYPE OF (geometric_tolerance_with_datum_reference);

WHERE

WR1: SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 2;

END_ENTITY;

# Sample Part 21 File

ISO-10303-21;

HEADER;

FILE_DESCRIPTION(('CATIA V5 STEP Exchange'),'2;1');

FILE_NAME('PatternTol.stp','2004-06-15T21:29:40+00:00',('none'),('none'),'CATIA Version 5 Release 13 (IN-9)','CATIA V5 STEP AP203','none');

FILE_SCHEMA(('Configuration_control_3d_design_ed2_mim_lf'));

ENDSEC;

DATA;

#1=APPLICATION_CONTEXT('configuration controlled 3D design of mechanical parts and assemblies') ;

#2=MECHANICAL_CONTEXT(' ',#1,'mechanical') ;

#3=DESIGN_CONTEXT(' ',#1,'design') ;

#4=APPLICATION_PROTOCOL_DEFINITION('draft international standard','Configuration_control_3d_design_ed2_mim_lf',2004,#1) ;

#5=PRODUCT('Pos Tol','','',(#2)) ;

#7=PRODUCT_CATEGORY('part',$) ;

#9=PRODUCT_CATEGORY_RELATIONSHIP(' ',' ',#7,#8) ;

#6=PRODUCT_DEFINITION_FORMATION_WITH_SPECIFIED_SOURCE('',' ',#5,.NOT_KNOWN.) ;

#8=PRODUCT_RELATED_PRODUCT_CATEGORY('detail',$,(#5)) ;

#10=COORDINATED_UNIVERSAL_TIME_OFFSET(0,0,.AHEAD.) ;

#11=CALENDAR_DATE(2004,15,6) ;

#12=LOCAL_TIME(14,29,39.,#10) ;

#13=DATE_AND_TIME(#11,#12) ;

#14=PRODUCT_DEFINITION(' ',' ',#6,#3) ;

#16=SECURITY_CLASSIFICATION(' ','Because',#15) ;

#15=SECURITY_CLASSIFICATION_LEVEL('unclassified') ;

#17=DATE_TIME_ROLE('classification_date') ;

#18=CC_DESIGN_DATE_AND_TIME_ASSIGNMENT(#13,#17,(#16)) ;

#19=APPROVAL_ROLE('APPROVER') ;

#20=APPROVAL_STATUS('not_yet_approved') ;

#21=APPROVAL(#20,' ') ;

#22=PERSON('Pers1 ','Step ','Joe ',$,$,$) ;

#23=ORGANIZATION('Org1 ','Generic Airplane Company ','Yet another jet manufacturer ') ;

#24=PERSONAL_ADDRESS('Mail Stop 1 ','123 ','Sesame Street','PO Box 101','Anytown','Central','98124','USA','206-555-1234','206-555-5678','help@company.com','206-555-9876',(#22),' ') ;

#25=PERSON_AND_ORGANIZATION(#22,#23) ;

#27=APPLIED_PERSON_AND_ORGANIZATION_ASSIGNMENT(#25,#26,(#16)) ;

#28=DATE_TIME_ROLE('creation_date') ;

#29=APPLIED_DATE_AND_TIME_ASSIGNMENT(#13,#28,(#14)) ;

#30=APPLIED_APPROVAL_ASSIGNMENT(#21,(#6,#14)) ;

#32=APPROVAL_DATE_TIME(#13,#21) ;

#33=APPLIED_PERSON_AND_ORGANIZATION_ASSIGNMENT(#25,#34,(#6)) ;

#35=APPLIED_PERSON_AND_ORGANIZATION_ASSIGNMENT(#25,#36,(#6,#14)) ;

#37=APPLIED_PERSON_AND_ORGANIZATION_ASSIGNMENT(#25,#38,(#5)) ;

#26=PERSON_AND_ORGANIZATION_ROLE('classification_officer') ;

#34=PERSON_AND_ORGANIZATION_ROLE('design_supplier') ;

#36=PERSON_AND_ORGANIZATION_ROLE('creator') ;

#38=PERSON_AND_ORGANIZATION_ROLE('design_owner') ;

#39=APPLIED_SECURITY_CLASSIFICATION_ASSIGNMENT(#16,(#6)) ;

#31=APPROVAL_PERSON_ORGANIZATION(#25,#21,#19) ;

#40=PRODUCT_DEFINITION_SHAPE(' ',' ',#14) ;

#41=(LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.)) ;

#42=(NAMED_UNIT(*)PLANE_ANGLE_UNIT()SI_UNIT($,.RADIAN.)) ;

#44=(NAMED_UNIT(*)SI_UNIT($,.STERADIAN.)SOLID_ANGLE_UNIT()) ;

#48=UNCERTAINTY_MEASURE_WITH_UNIT(LENGTH_MEASURE(0.000196850393701),#47,'TOL_CRV','CONFUSED CURVE UNCERTAINTY') ;

#45=LENGTH_MEASURE_WITH_UNIT(LENGTH_MEASURE(25.4),#41) ;

#47=(CONVERSION_BASED_UNIT('INCH',#45)LENGTH_UNIT()NAMED_UNIT(#46)) ;

#49=(GEOMETRIC_REPRESENTATION_CONTEXT(3)GLOBAL_UNCERTAINTY_ASSIGNED_CONTEXT((#48))GLOBAL_UNIT_ASSIGNED_CONTEXT((#47,#42,#44))REPRESENTATION_CONTEXT(' ',' ')) ;

/* Geometry of Hole 1 */

#55=CARTESIAN_POINT('Axis2P3D Location',(1.,1.,0.99606299213)) ;

#56=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#57=DIRECTION('Axis2P3D XDirection',(0.0345504945626,-0.0188750212049,0.)) ;

#58=AXIS2_PLACEMENT_3D('Cylinder Axis2P3D',#55,#56,#57) ;

#59=CYLINDRICAL_SURFACE('generated cylinder',#58,0.500000000002) ;

/* Geometry of Hole 2 */

#270=CARTESIAN_POINT('Axis2P3D Location',(3.02048023855,0.944704671544,0.99606299213));

#271=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#272=DIRECTION('Axis2P3D XDirection',(0.0345504945626,-0.0188750212049,0.)) ;

#273=AXIS2_PLACEMENT_3D('Cylinder Axis2P3D',#270,#271,#272) ;

#274=CYLINDRICAL_SURFACE('generated cylinder',#273,0.500000000002) ;

#50=CARTESIAN_POINT(' ',(0.,0.,0.)) ;

#60=CARTESIAN_POINT('Line Origine',(0.561208719057,1.23971276931,0.500000000002)) ;

#64=CARTESIAN_POINT('Vertex',(0.561208719057,1.23971276931,0.)) ;

#66=CARTESIAN_POINT('Vertex',(0.561208719057,1.23971276931,1.)) ;

#69=CARTESIAN_POINT('Axis2P3D Location',(1.,1.,0.)) ;

#73=CARTESIAN_POINT('Vertex',(1.43879128095,0.760287230701,0.)) ;

#76=CARTESIAN_POINT('Line Origine',(1.43879128095,0.760287230701,0.500000000002)) ;

#80=CARTESIAN_POINT('Vertex',(1.43879128095,0.760287230701,1.)) ;

#83=CARTESIAN_POINT('Axis2P3D Location',(1.,1.,1.)) ;

#95=CARTESIAN_POINT('Axis2P3D Location',(0.,0.,1.)) ;

#100=CARTESIAN_POINT('Line Origine',(2.00000000001,0.,1.)) ;

#104=CARTESIAN_POINT('Vertex',(0.,0.,1.)) ;

#106=CARTESIAN_POINT('Vertex',(4.00000000002,0.,1.)) ;

#109=CARTESIAN_POINT('Line Origine',(4.00000000002,1.,1.)) ;

#113=CARTESIAN_POINT('Vertex',(4.00000000002,2.00000000001,1.)) ;

#116=CARTESIAN_POINT('Line Origine',(2.00000000001,2.00000000001,1.)) ;

#120=CARTESIAN_POINT('Vertex',(-1.1189649382E-015,2.00000000001,1.)) ;

#123=CARTESIAN_POINT('Line Origine',(0.,1.,1.)) ;

#134=CARTESIAN_POINT('Axis2P3D Location',(3.02048023855,0.944704671544,1.)) ;

#138=CARTESIAN_POINT('Vertex',(2.5816889576,1.18441744085,1.)) ;

#140=CARTESIAN_POINT('Vertex',(3.45927151949,0.704991902241,1.)) ;

#143=CARTESIAN_POINT('Axis2P3D Location',(3.02048023855,0.944704671544,1.)) ;

#152=CARTESIAN_POINT('Axis2P3D Location',(1.,1.,1.)) ;

#162=CARTESIAN_POINT('Axis2P3D Location',(1.,1.,0.)) ;

#174=CARTESIAN_POINT('Axis2P3D Location',(0.,0.,0.)) ;

#179=CARTESIAN_POINT('Line Origine',(0.,0.,0.500000000002)) ;

#183=CARTESIAN_POINT('Vertex',(0.,0.,0.)) ;

#186=CARTESIAN_POINT('Line Origine',(2.00000000001,0.,0.)) ;

#190=CARTESIAN_POINT('Vertex',(4.00000000002,0.,0.)) ;

#193=CARTESIAN_POINT('Line Origine',(4.00000000002,0.,0.500000000002)) ;

#205=CARTESIAN_POINT('Axis2P3D Location',(4.00000000002,-9.1845476537E-016,0.)) ;

#210=CARTESIAN_POINT('Line Origine',(4.00000000002,1.,0.)) ;

#214=CARTESIAN_POINT('Vertex',(4.00000000002,2.00000000001,0.)) ;

#217=CARTESIAN_POINT('Line Origine',(4.00000000002,2.00000000001,0.500000000002)) ;

#229=CARTESIAN_POINT('Axis2P3D Location',(4.00000000002,2.00000000001,0.)) ;

#234=CARTESIAN_POINT('Line Origine',(2.00000000001,2.00000000001,0.)) ;

#238=CARTESIAN_POINT('Vertex',(-1.1189649382E-015,2.00000000001,0.)) ;

#241=CARTESIAN_POINT('Line Origine',(-1.1189649382E-015,2.00000000001,0.500000000002)) ;

#253=CARTESIAN_POINT('Axis2P3D Location',(0.,2.00000000001,0.)) ;

#258=CARTESIAN_POINT('Line Origine',(0.,1.,0.)) ;

#275=CARTESIAN_POINT('Line Origine',(2.5816889576,1.18441744085,0.499999999971)) ;

#279=CARTESIAN_POINT('Vertex',(2.5816889576,1.18441744085,0.)) ;

#282=CARTESIAN_POINT('Axis2P3D Location',(3.02048023855,0.944704671544,0.)) ;

#286=CARTESIAN_POINT('Vertex',(3.45927151949,0.704991902241,0.)) ;

#289=CARTESIAN_POINT('Line Origine',(3.45927151949,0.704991902241,0.499999999971)) ;

#301=CARTESIAN_POINT('Axis2P3D Location',(3.02048023855,0.944704671544,0.)) ;

#313=CARTESIAN_POINT('Axis2P3D Location',(0.,0.,0.)) ;

#61=DIRECTION('Vector Direction',(0.,0.,-0.0393700787402)) ;

#70=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#77=DIRECTION('Vector Direction',(0.,0.,-0.0393700787402)) ;

#84=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#96=DIRECTION('Axis2P3D Direction',(0.,0.,0.0393700787402)) ;

#97=DIRECTION('Axis2P3D XDirection',(0.0393700787402,0.,0.)) ;

#101=DIRECTION('Vector Direction',(0.0393700787402,0.,0.)) ;

#110=DIRECTION('Vector Direction',(0.,0.0393700787402,0.)) ;

#117=DIRECTION('Vector Direction',(-0.0393700787402,0.,0.)) ;

#124=DIRECTION('Vector Direction',(0.,-0.0393700787402,0.)) ;

#135=DIRECTION('Axis2P3D Direction',(0.,0.,0.0393700787402)) ;

#144=DIRECTION('Axis2P3D Direction',(0.,0.,0.0393700787402)) ;

#153=DIRECTION('Axis2P3D Direction',(0.,0.,0.0393700787402)) ;

#163=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#175=DIRECTION('Axis2P3D Direction',(0.,-0.0393700787402,0.)) ;

#176=DIRECTION('Axis2P3D XDirection',(0.0393700787402,0.,0.)) ;

#180=DIRECTION('Vector Direction',(0.,0.,0.0393700787402)) ;

#187=DIRECTION('Vector Direction',(0.0393700787402,0.,0.)) ;

#194=DIRECTION('Vector Direction',(0.,0.,0.0393700787402)) ;

#206=DIRECTION('Axis2P3D Direction',(0.0393700787402,0.,0.)) ;

#207=DIRECTION('Axis2P3D XDirection',(0.,0.0393700787402,0.)) ;

#211=DIRECTION('Vector Direction',(0.,0.0393700787402,0.)) ;

#218=DIRECTION('Vector Direction',(0.,0.,0.0393700787402)) ;

#230=DIRECTION('Axis2P3D Direction',(0.,0.0393700787402,0.)) ;

#231=DIRECTION('Axis2P3D XDirection',(-0.0393700787402,0.,0.)) ;

#235=DIRECTION('Vector Direction',(-0.0393700787402,0.,0.)) ;

#242=DIRECTION('Vector Direction',(0.,0.,0.0393700787402)) ;

#254=DIRECTION('Axis2P3D Direction',(-0.0393700787402,0.,0.)) ;

#255=DIRECTION('Axis2P3D XDirection',(0.,-0.0393700787402,0.)) ;

#259=DIRECTION('Vector Direction',(0.,-0.0393700787402,0.)) ;

#276=DIRECTION('Vector Direction',(0.,0.,-0.0393700787402)) ;

#283=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#290=DIRECTION('Vector Direction',(0.,0.,-0.0393700787402)) ;

#302=DIRECTION('Axis2P3D Direction',(0.,0.,-0.0393700787402)) ;

#314=DIRECTION('Axis2P3D Direction',(0.,0.,0.0393700787402)) ;

#315=DIRECTION('Axis2P3D XDirection',(0.0393700787402,0.,0.)) ;

#51=AXIS2_PLACEMENT_3D(' ',#50,$,$) ;

#71=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#69,#70,$) ;

#85=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#83,#84,$) ;

#98=AXIS2_PLACEMENT_3D('Plane Axis2P3D',#95,#96,#97) ;

#136=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#134,#135,$) ;

#145=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#143,#144,$) ;

#154=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#152,#153,$) ;

#164=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#162,#163,$) ;

#177=AXIS2_PLACEMENT_3D('Plane Axis2P3D',#174,#175,#176) ;

#208=AXIS2_PLACEMENT_3D('Plane Axis2P3D',#205,#206,#207) ;

#232=AXIS2_PLACEMENT_3D('Plane Axis2P3D',#229,#230,#231) ;

#256=AXIS2_PLACEMENT_3D('Plane Axis2P3D',#253,#254,#255) ;

#284=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#282,#283,$) ;

#303=AXIS2_PLACEMENT_3D('Circle Axis2P3D',#301,#302,$) ;

#316=AXIS2_PLACEMENT_3D('Plane Axis2P3D',#313,#314,#315) ;

#89=ORIENTED_EDGE('',*,*,#68,.F.) ;

#90=ORIENTED_EDGE('',*,*,#75,.F.) ;

#91=ORIENTED_EDGE('',*,*,#82,.T.) ;

#92=ORIENTED_EDGE('',*,*,#87,.T.) ;

#129=ORIENTED_EDGE('',*,*,#108,.T.) ;

#130=ORIENTED_EDGE('',*,*,#115,.T.) ;

#131=ORIENTED_EDGE('',*,*,#122,.T.) ;

#132=ORIENTED_EDGE('',*,*,#127,.T.) ;

#149=ORIENTED_EDGE('',*,*,#142,.F.) ;

#150=ORIENTED_EDGE('',*,*,#147,.F.) ;

#158=ORIENTED_EDGE('',*,*,#156,.F.) ;

#159=ORIENTED_EDGE('',*,*,#87,.F.) ;

#168=ORIENTED_EDGE('',*,*,#82,.F.) ;

#169=ORIENTED_EDGE('',*,*,#166,.F.) ;

#170=ORIENTED_EDGE('',*,*,#68,.T.) ;

#171=ORIENTED_EDGE('',*,*,#156,.T.) ;

#199=ORIENTED_EDGE('',*,*,#185,.F.) ;

#200=ORIENTED_EDGE('',*,*,#192,.T.) ;

#201=ORIENTED_EDGE('',*,*,#197,.T.) ;

#202=ORIENTED_EDGE('',*,*,#108,.F.) ;

#223=ORIENTED_EDGE('',*,*,#197,.F.) ;

#224=ORIENTED_EDGE('',*,*,#216,.T.) ;

#225=ORIENTED_EDGE('',*,*,#221,.T.) ;

#226=ORIENTED_EDGE('',*,*,#115,.F.) ;

#247=ORIENTED_EDGE('',*,*,#221,.F.) ;

#248=ORIENTED_EDGE('',*,*,#240,.T.) ;

#249=ORIENTED_EDGE('',*,*,#245,.T.) ;

#250=ORIENTED_EDGE('',*,*,#122,.F.) ;

#264=ORIENTED_EDGE('',*,*,#245,.F.) ;

#265=ORIENTED_EDGE('',*,*,#262,.T.) ;

#266=ORIENTED_EDGE('',*,*,#185,.T.) ;

#267=ORIENTED_EDGE('',*,*,#127,.F.) ;

#295=ORIENTED_EDGE('',*,*,#281,.F.) ;

#296=ORIENTED_EDGE('',*,*,#288,.F.) ;

#297=ORIENTED_EDGE('',*,*,#293,.T.) ;

#298=ORIENTED_EDGE('',*,*,#147,.T.) ;

#307=ORIENTED_EDGE('',*,*,#293,.F.) ;

#308=ORIENTED_EDGE('',*,*,#305,.F.) ;

#309=ORIENTED_EDGE('',*,*,#281,.T.) ;

#310=ORIENTED_EDGE('',*,*,#142,.T.) ;

#319=ORIENTED_EDGE('',*,*,#262,.F.) ;

#320=ORIENTED_EDGE('',*,*,#240,.F.) ;

#321=ORIENTED_EDGE('',*,*,#216,.F.) ;

#322=ORIENTED_EDGE('',*,*,#192,.F.) ;

#325=ORIENTED_EDGE('',*,*,#288,.T.) ;

#326=ORIENTED_EDGE('',*,*,#305,.T.) ;

#329=ORIENTED_EDGE('',*,*,#75,.T.) ;

#330=ORIENTED_EDGE('',*,*,#166,.T.) ;

#151=FACE_BOUND('',#148,.T.) ;

#160=FACE_BOUND('',#157,.T.) ;

#327=FACE_BOUND('',#324,.T.) ;

#331=FACE_BOUND('',#328,.T.) ;

#54=CLOSED_SHELL('Closed Shell',(#94,#161,#173,#204,#228,#252,#269,#300,#312,#332)) ;

#46=DIMENSIONAL_EXPONENTS(1.,0.,0.,0.,0.,0.,0.) ;

#62=VECTOR('Line Direction',#61,0.0393700787402) ;

#78=VECTOR('Line Direction',#77,0.0393700787402) ;

#102=VECTOR('Line Direction',#101,0.0393700787402) ;

#111=VECTOR('Line Direction',#110,0.0393700787402) ;

#118=VECTOR('Line Direction',#117,0.0393700787402) ;

#125=VECTOR('Line Direction',#124,0.0393700787402) ;

#181=VECTOR('Line Direction',#180,0.0393700787402) ;

#188=VECTOR('Line Direction',#187,0.0393700787402) ;

#195=VECTOR('Line Direction',#194,0.0393700787402) ;

#212=VECTOR('Line Direction',#211,0.0393700787402) ;

#219=VECTOR('Line Direction',#218,0.0393700787402) ;

#236=VECTOR('Line Direction',#235,0.0393700787402) ;

#243=VECTOR('Line Direction',#242,0.0393700787402) ;

#260=VECTOR('Line Direction',#259,0.0393700787402) ;

#277=VECTOR('Line Direction',#276,0.0393700787402) ;

#291=VECTOR('Line Direction',#290,0.0393700787402) ;

#334=ADVANCED_BREP_SHAPE_REPRESENTATION('NONE',(#333),#49) ;

#52=SHAPE_REPRESENTATION(' ',(#51),#49) ;

#94=ADVANCED_FACE('',(#93),#59,.F.) ;

#161=ADVANCED_FACE('',(#133,#151,#160),#99,.T.) ;

#173=ADVANCED_FACE('',(#172),#59,.F.) ;

#204=ADVANCED_FACE('',(#203),#178,.T.) ;

#228=ADVANCED_FACE('',(#227),#209,.T.) ;

#252=ADVANCED_FACE('',(#251),#233,.T.) ;

#269=ADVANCED_FACE('',(#268),#257,.T.) ;

#300=ADVANCED_FACE('',(#299),#274,.F.) ;

#312=ADVANCED_FACE('',(#311),#274,.F.) ;

#332=ADVANCED_FACE('',(#323,#327,#331),#317,.F.) ;

#333=MANIFOLD_SOLID_BREP('PartBody',#54) ;

#72=CIRCLE('generated circle',#71,0.500000000002) ;

#86=CIRCLE('generated circle',#85,0.500000000002) ;

#137=CIRCLE('generated circle',#136,0.500000000002) ;

#146=CIRCLE('generated circle',#145,0.500000000002) ;

#155=CIRCLE('generated circle',#154,0.500000000002) ;

#165=CIRCLE('generated circle',#164,0.500000000002) ;

#285=CIRCLE('generated circle',#284,0.500000000002) ;

#304=CIRCLE('generated circle',#303,0.500000000002) ;

#335=SHAPE_REPRESENTATION_RELATIONSHIP(' ',' ',#52,#334) ;

#68=EDGE_CURVE('',#65,#67,#63,.F.) ;

#75=EDGE_CURVE('',#74,#65,#72,.F.) ;

#82=EDGE_CURVE('',#74,#81,#79,.F.) ;

#87=EDGE_CURVE('',#81,#67,#86,.F.) ;

#108=EDGE_CURVE('',#105,#107,#103,.T.) ;

#115=EDGE_CURVE('',#107,#114,#112,.T.) ;

#122=EDGE_CURVE('',#114,#121,#119,.T.) ;

#127=EDGE_CURVE('',#121,#105,#126,.T.) ;

#142=EDGE_CURVE('',#139,#141,#137,.T.) ;

#147=EDGE_CURVE('',#141,#139,#146,.T.) ;

#156=EDGE_CURVE('',#67,#81,#155,.T.) ;

#166=EDGE_CURVE('',#65,#74,#165,.F.) ;

#185=EDGE_CURVE('',#184,#105,#182,.T.) ;

#192=EDGE_CURVE('',#184,#191,#189,.T.) ;

#197=EDGE_CURVE('',#191,#107,#196,.T.) ;

#216=EDGE_CURVE('',#191,#215,#213,.T.) ;

#221=EDGE_CURVE('',#215,#114,#220,.T.) ;

#240=EDGE_CURVE('',#215,#239,#237,.T.) ;

#245=EDGE_CURVE('',#239,#121,#244,.T.) ;

#262=EDGE_CURVE('',#239,#184,#261,.T.) ;

#281=EDGE_CURVE('',#280,#139,#278,.F.) ;

#288=EDGE_CURVE('',#287,#280,#285,.F.) ;

#293=EDGE_CURVE('',#287,#141,#292,.F.) ;

#305=EDGE_CURVE('',#280,#287,#304,.F.) ;

#88=EDGE_LOOP('',(#89,#90,#91,#92)) ;

#128=EDGE_LOOP('',(#129,#130,#131,#132)) ;

#148=EDGE_LOOP('',(#149,#150)) ;

#157=EDGE_LOOP('',(#158,#159)) ;

#167=EDGE_LOOP('',(#168,#169,#170,#171)) ;

#198=EDGE_LOOP('',(#199,#200,#201,#202)) ;

#222=EDGE_LOOP('',(#223,#224,#225,#226)) ;

#246=EDGE_LOOP('',(#247,#248,#249,#250)) ;

#263=EDGE_LOOP('',(#264,#265,#266,#267)) ;

#294=EDGE_LOOP('',(#295,#296,#297,#298)) ;

#306=EDGE_LOOP('',(#307,#308,#309,#310)) ;

#318=EDGE_LOOP('',(#319,#320,#321,#322)) ;

#324=EDGE_LOOP('',(#325,#326)) ;

#328=EDGE_LOOP('',(#329,#330)) ;

#93=FACE_OUTER_BOUND('',#88,.T.) ;

#133=FACE_OUTER_BOUND('',#128,.T.) ;

#172=FACE_OUTER_BOUND('',#167,.T.) ;

#203=FACE_OUTER_BOUND('',#198,.T.) ;

#227=FACE_OUTER_BOUND('',#222,.T.) ;

#251=FACE_OUTER_BOUND('',#246,.T.) ;

#268=FACE_OUTER_BOUND('',#263,.T.) ;

#299=FACE_OUTER_BOUND('',#294,.T.) ;

#311=FACE_OUTER_BOUND('',#306,.T.) ;

#323=FACE_OUTER_BOUND('',#318,.T.) ;

#63=LINE('Line',#60,#62) ;

#79=LINE('Line',#76,#78) ;

#103=LINE('Line',#100,#102) ;

#112=LINE('Line',#109,#111) ;

#119=LINE('Line',#116,#118) ;

#126=LINE('Line',#123,#125) ;

#182=LINE('Line',#179,#181) ;

#189=LINE('Line',#186,#188) ;

#196=LINE('Line',#193,#195) ;

#213=LINE('Line',#210,#212) ;

#220=LINE('Line',#217,#219) ;

#237=LINE('Line',#234,#236) ;

#244=LINE('Line',#241,#243) ;

#261=LINE('Line',#258,#260) ;

#278=LINE('Line',#275,#277) ;

#292=LINE('Line',#289,#291) ;

#99=PLANE('Plane',#98) ;

#178=PLANE('Plane',#177) ;

#209=PLANE('Plane',#208) ;

#233=PLANE('Plane',#232) ;

#257=PLANE('Plane',#256) ;

#317=PLANE('Plane',#316) ;

#43=PLANE_ANGLE_MEASURE_WITH_UNIT(PLANE_ANGLE_MEASURE(0.0174532925199),#42) ;

#53=SHAPE_DEFINITION_REPRESENTATION(#40,#52) ;

#65=VERTEX_POINT('',#64) ;

#67=VERTEX_POINT('',#66) ;

#74=VERTEX_POINT('',#73) ;

#81=VERTEX_POINT('',#80) ;

#105=VERTEX_POINT('',#104) ;

#107=VERTEX_POINT('',#106) ;

#114=VERTEX_POINT('',#113) ;

#121=VERTEX_POINT('',#120) ;

#139=VERTEX_POINT('',#138) ;

#141=VERTEX_POINT('',#140) ;

#184=VERTEX_POINT('',#183) ;

#191=VERTEX_POINT('',#190) ;

#215=VERTEX_POINT('',#214) ;

#239=VERTEX_POINT('',#238) ;

#280=VERTEX_POINT('',#279) ;

#287=VERTEX_POINT('',#286) ;

/* Geometric tolerance entities */

/* Pattern of Position Tolerances */

#1000=(GEOMETRIC_TOLERANCE('Position', 'Pattern of positional tolerances for holes', #1045, #1060)

GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE((#1003, #1004))

MODIFIED_GEOMETRIC_TOLERANCE(.MAXIMUM_MATERIAL_CONDITION.)

POSITION_TOLERANCE());

#1045=LENGTH_MEASURE_WITH_UNIT(LENGTH_MEASURE(0.01),#47) ;

#1008=SHAPE_ASPECT('Hole1', 'One inch top hole', #40, .T.);

#1018=PROPERTY_DEFINITION('Feature shape','Shape of feature',#1008);

#1009=SHAPE_DEFINITION_REPRESENTATION(#1018,#1001) ;

#1001=SHAPE_REPRESENTATION('Representation of hole',(#94),#49) ;

#1028=SHAPE_ASPECT('Hole2', 'One inch top hole', #40, .T.);

#1027=PROPERTY_DEFINITION('Feature shape','Shape of feature',#1028);

#1029=SHAPE_DEFINITION_REPRESENTATION(#1027,#1001) ;

#1001=SHAPE_REPRESENTATION('Representation of hole',(#93),#49) ;

#1060=COMPOSITE_SHAPE_ASPECT('Pattern', 'Hole Pattern', #40, .T.,);

#1062=SHAPE_ASPECT_RELATIONSHIP('Pattern composition', 'Composition of Hole Pattern', #1060, #1008);

#1063=SHAPE_ASPECT_RELATIONSHIP('Pattern composition', 'Composition of Hole Pattern', #1060, #1028);

/* #1002=DATUM_REFERENCE(1,#1005); */

#1003=DATUM_REFERENCE(2,#1006);

#1004=DATUM_REFERENCE(1,#1007);

/* Datum related to geometric plane of datum */

#1005=DATUM('Datum A','Datum A',#40,.F.,'A');

#1058=PROPERTY_DEFINITION('Datum geometry','Geometric plane of datum',#1005);

#1059=SHAPE_DEFINITION_REPRESENTATION(#1058,#1061) ;

#1061=SHAPE_REPRESENTATION('Representation of datum plane',(#98),#49) ;

#1006=DATUM('Datum B','Datum B',#40,.F.,'B');

#1068=PROPERTY_DEFINITION('Datum geometry','Geometric plane of datum',#1006);

#1069=SHAPE_DEFINITION_REPRESENTATION(#1068,#1071) ;

#1071=SHAPE_REPRESENTATION('Representation of datum plane',(#214),#49) ;

#1007=DATUM('Datum C','Datum C',#40,.F.,'C');

#1078=PROPERTY_DEFINITION('Datum geometry','Geometric plane of datum',#1007);

#1079=SHAPE_DEFINITION_REPRESENTATION(#1078,#1081) ;

#1081=SHAPE_REPRESENTATION('Representation of datum plane',(#190),#49) ;

/* Datum Feature is topology of actual solid face representing datum plane */

#1010=DATUM_FEATURE('Datum A','Datum A',#40,.T.);

#1038=PROPERTY_DEFINITION('Datum shape','Shape of datum',#1010);

#1039=SHAPE_DEFINITION_REPRESENTATION(#1038,#1040) ;

#1040=SHAPE_REPRESENTATION('Representation of datum feature',(#142),#49) ;

/* #1041=SHAPE_ASPECT('Datum Feature A', 'Face representing datum feature', #1040, .T.); */

#1011=DATUM_FEATURE('Datum B','Datum B',#40,.T. );

#1048=PROPERTY_DEFINITION('Datum shape','Shape of datum',#1011);

#1049=SHAPE_DEFINITION_REPRESENTATION(#1048,#1050) ;

#1050=SHAPE_REPRESENTATION('Representation of datum feature',(#233),#49) ;

#1012=DATUM_FEATURE('Datum C','Datum C',#40,.T.);

#1098=PROPERTY_DEFINITION('Datum shape','Shape of datum',#1012);

#1099=SHAPE_DEFINITION_REPRESENTATION(#1098,#1100) ;

#1100=SHAPE_REPRESENTATION('Representation of datum feature',(#209),#49);

#1015=SHAPE_ASPECT_RELATIONSHIP('DtoF','Datum to Feature relationship',#1010,#1005);

#1016=SHAPE_ASPECT_RELATIONSHIP('DtoF','Datum to Feature relationship',#1011,#1006);

#1017=SHAPE_ASPECT_RELATIONSHIP('DtoF','Datum to Feature relationship',#1012,#1007);

/* Perpendicularity tolerance */

#2000=PERPENDICULARITY_TOLERANCE('perpendicularity', 'Perpendicularity tolerance for top face', #2045, #2008,(#2003,#2004)) ;

#2045=LENGTH_MEASURE_WITH_UNIT(LENGTH_MEASURE(0.254),#41) ;

#2008=SHAPE_ASPECT('Top face', 'Top face of part', #40, .T.);

#2018=PROPERTY_DEFINITION('Shape','Shape of Feature',#2008);

#2009=SHAPE_DEFINITION_REPRESENTATION(#2018,#2001) ;

#2001=SHAPE_REPRESENTATION('Representation of face',(#142),#49) ;

#2003=DATUM_REFERENCE(1,#1006);

#2004=DATUM_REFERENCE(2,#1012);

/**************************************************************************** *

* Instances #3910-#3956 represent the choioce of dimensioning	              *

* standards per tolerance harmonization effort.                               *

*****************************************************************************/

#3910=APPLIED_DOCUMENT_REFERENCE(#3911, "ASME Y14.41-2003", (#14));

#3911=DOCUMENT("ASME Y14.41-200", "DIGITAL PRODUCT DEFINITION DATA PRACTICES",,"dimensioning standard");

#3912=OBJECT_ROLE("dimensioning standard",);

#3913=ROLE_ASSOCIATION(#3912, #3910);

ENDSEC;

END-ISO-10303-21;

# AP203 Edition 2 Long Form

(*

$Id: mim_lf.exp,v 1.14 2004/12/03 17:18:07 darla Exp $

ISO TC184/SC4/WG3 N1587 - ISO/TS 10303-403 Configuration_control_3d_design_ed2 - EXPRESS MIM

Supersedes ISO TC184/SC4/WG3 N1202

*)

(* ===================================================================================== *)

(* Long form schema generated by The EXPRESS Data Manager  compiler version 9.5B.2004.01.23*)

(* Wed Dec 01 11:06:08 2004                                                                *)

(* The schema is converted from ISO10303 P11-2003 to ISO10303 P11-1994                     *)

(* ===================================================================================== *)

SCHEMA Configuration_control_3d_design_ed2_mim_lf;

CONSTANT

deprecated_constructed_data_types : SET OF STRING :=

['approved_item',

'certified_item',

'change_request_item',

'contracted_item',

'classified_item',

'date_time_item',

'person_organization_item',

'specified_item',

'start_request_item',

'work_item'];

deprecated_entity_data_types : SET OF STRING :=

['cc_design_approval',

'cc_design_certification',

'cc_design_contract',

'cc_design_date_and_time_assignment',

'cc_design_person_and_organization_assignment',

'cc_design_security_classification',

'cc_design_specification_reference',

'change',

'change_request',

'design_context',

'design_make_from_relationship',

'mechanical_context',

'start_request',

'start_work',

'supplied_part_relationship'];

deprecated_interfaced_data_types : SET OF STRING :=

['document_with_class',

'ordinal_date',

'product_definition_formation_with_specified_source',

'week_of_year_and_day_date'];

dummy_gri : geometric_representation_item :=  representation_item('')||

geometric_representation_item();

dummy_tri : topological_representation_item := representation_item('')||

topological_representation_item();

END_CONSTANT;

(* Pruned unused type: action_item_203e2  *)

TYPE action_items = SELECT (

configuration_effectivity,

product_definition,

product_definition_formation,

product_definition_formation_relationship,

product_definition_relationship);

END_TYPE;

TYPE action_request_item = SELECT (

product_definition,

product_definition_formation,

product_definition_formation_relationship,

product_definition_relationship,

property_definition);

END_TYPE;

(* Pruned unused type: action_request_item_203e2  *)

TYPE ahead_or_behind = ENUMERATION OF

(ahead,

exact,

behind);

END_TYPE;

(* Pruned unused type: aliasable_item  *)

TYPE amount_of_substance_measure = REAL;

END_TYPE;

TYPE angle_relator = ENUMERATION OF

(equal,

large,

small);

END_TYPE;

(* Pruned unused type: appearance_representation_identification_item  *)

(* Pruned unused type: appearance_representation_version_item  *)

TYPE approval_item = SELECT (

action,

alternate_product_relationship,

applied_action_assignment,

assembly_component_usage_substitute,

certification,

configuration_effectivity,

contract,

document_file,

executed_action,

product,

product_definition,

product_definition_formation,

product_definition_relationship,

versioned_action_request);

END_TYPE;

(* Pruned unused type: approval_item_203e2  *)

TYPE approved_item = SELECT

(certification,

change,

change_request,

configuration_effectivity,

configuration_item,

contract,

product,

security_classification,

start_request,

start_work);

END_TYPE;

TYPE area_measure = REAL;

END_TYPE;

TYPE area_or_view = SELECT

(presentation_area,

presentation_view);

END_TYPE;

TYPE attribute_language_item = SELECT (

alternate_product_relationship,

application_context,

applied_certification_assignment,

applied_document_reference,

applied_document_usage_constraint_assignment,

applied_external_identification_assignment,

applied_identification_assignment,

applied_organizational_project_assignment,

applied_security_classification_assignment,

approval,

approval_relationship,

approval_status,

assembly_component_usage_substitute,

attribute_value_assignment,

certification,

certification_type,

configuration_design,

configuration_item,

contract,

date_role,

date_time_role,

descriptive_representation_item,

document_relationship,

document_usage_role,

effectivity,

effectivity_relationship,

event_occurrence,

external_source,

general_property,

general_property_relationship,

geometric_representation_item,

geometric_tolerance,

identification_role,

make_from_usage_option,

mapped_item,

multi_language_attribute_assignment,

object_role,

organization_relationship,

organization_role,

organizational_project,

organizational_project_relationship,

organizational_project_role,

person_and_organization,

person_and_organization_role,

product,

product_category,

product_concept,

product_concept_relationship,

product_definition,

product_definition_context,

product_definition_formation,

product_definition_formation_relationship,

product_definition_relationship,

product_definition_shape,

product_related_product_category,

property_definition,

representation,

security_classification,

security_classification_assignment,

shape_aspect,

shape_aspect_relationship,

shape_representation,

time_interval_role,

topological_representation_item,

uncertainty_measure_with_unit,

uncertainty_qualifier);

END_TYPE;

(* Pruned unused type: attribute_language_item_203e2  *)

TYPE attribute_type = SELECT

(label,

text);

END_TYPE;

TYPE axis2_placement = SELECT

(axis2_placement_2d,

axis2_placement_3d);

END_TYPE;

TYPE b_spline_curve_form = ENUMERATION OF

(polyline_form,

circular_arc,

elliptic_arc,

parabolic_arc,

hyperbolic_arc,

unspecified);

END_TYPE;

TYPE b_spline_surface_form = ENUMERATION OF

(plane_surf,

cylindrical_surf,

conical_surf,

spherical_surf,

toroidal_surf,

surf_of_revolution,

ruled_surf,

generalised_cone,

quadric_surf,

surf_of_linear_extrusion,

unspecified);

END_TYPE;

TYPE boolean_operand = SELECT (

solid_model,

half_space_solid,

csg_primitive,

boolean_result);

END_TYPE;

TYPE boolean_operator = ENUMERATION OF

(union,

intersection,

difference);

END_TYPE;

TYPE box_characteristic_select = SELECT

(box_height,

box_width,

box_slant_angle,

box_rotate_angle);

END_TYPE;

TYPE box_height = positive_ratio_measure;

END_TYPE;

TYPE box_rotate_angle = plane_angle_measure;

END_TYPE;

TYPE  box_slant_angle = plane_angle_measure;

END_TYPE;

TYPE box_width = positive_ratio_measure;

END_TYPE;

(* Pruned unused type: cc3dpa_groupable_item  *)

TYPE celsius_temperature_measure = REAL;

END_TYPE;

TYPE central_or_parallel = ENUMERATION OF

(central,

parallel);

END_TYPE;

TYPE certification_item = SELECT (

product_definition_formation_relationship);

END_TYPE;

(* Pruned unused type: certification_item_203e2  *)

TYPE certified_item = SELECT

(supplied_part_relationship);

END_TYPE;

TYPE change_request_item = SELECT

(product_definition_formation);

END_TYPE;

TYPE character_spacing_select = SELECT (

length_measure,

ratio_measure,

measure_with_unit,

descriptive_measure);

END_TYPE;

TYPE character_style_select = SELECT

(character_glyph_style_stroke,

character_glyph_style_outline,

text_style_for_defined_font);

END_TYPE;

TYPE characterized_action_definition = SELECT (

action,

action_method,

action_relationship);

END_TYPE;

TYPE characterized_definition = SELECT

(characterized_object,

characterized_product_definition,

shape_definition);

END_TYPE;

TYPE characterized_product_definition = SELECT

(product_definition,

product_definition_relationship);

END_TYPE;

TYPE classification_item = SELECT (

action,

action_directive,

action_method,

action_property,

action_relationship,

action_request_solution,

action_request_status,

address,

alternate_product_relationship,

applied_action_assignment,

applied_action_request_assignment,

applied_approval_assignment,

applied_certification_assignment,

applied_contract_assignment,

applied_date_and_time_assignment,

applied_date_assignment,

applied_document_reference,

applied_document_usage_constraint_assignment,

applied_effectivity_assignment,

applied_event_occurrence_assignment,

applied_external_identification_assignment,

applied_identification_assignment,

applied_organization_assignment,

applied_organizational_project_assignment,

applied_person_and_organization_assignment,

applied_security_classification_assignment,

approval,

approval_person_organization,

approval_relationship,

approval_status,

assembly_component_usage_substitute,

calendar_date,

certification,

class,

configuration_item,

context_dependent_unit,

contract,

conversion_based_unit,

date_and_time,

date_and_time_assignment,

date_assignment,

derived_unit,

descriptive_representation_item,

directed_action,

document_file,

document_relationship,

effectivity,

event_occurrence,

executed_action,

general_property,

general_property_relationship,

group,

identification_assignment,

language,

measure_representation_item,

measure_with_unit,

multi_language_attribute_assignment,

named_unit,

organization,

organization_relationship,

organizational_address,

organizational_project,

organizational_project_relationship,

person,

person_and_organization_address,

product,

product_category,

product_concept,

product_definition,

product_definition_context,

product_definition_formation,

product_definition_formation_relationship,

product_definition_relationship,

property_definition,

property_definition_representation,

representation,

representation_context,

representation_item,

security_classification,

uncertainty_measure_with_unit,

versioned_action_request);

END_TYPE;

TYPE classified_item = SELECT

(assembly_component_usage,

product_definition_formation);

END_TYPE;

(* Pruned unused type: complete_membership_select  *)

TYPE compound_item_definition = SELECT

(list_representation_item,

set_representation_item);

END_TYPE;

TYPE configuration_design_item = SELECT

(product_definition,

product_definition_formation);

END_TYPE;

TYPE context_dependent_measure = REAL;

END_TYPE;

TYPE contract_item = SELECT (

executed_action,

product_definition_formation);

END_TYPE;

(* Pruned unused type: contract_item_203e2  *)

TYPE contracted_item = SELECT

(product_definition_formation);

END_TYPE;

TYPE count_measure = NUMBER;

END_TYPE;

TYPE csg_primitive = SELECT (

sphere,

block,

right_angular_wedge,

torus,

right_circular_cone,

right_circular_cylinder);

END_TYPE;

TYPE csg_select = SELECT

(boolean_result,

csg_primitive);

END_TYPE;

TYPE curve_font_or_scaled_curve_font_select = SELECT (

curve_style_font_select);

END_TYPE;

TYPE curve_on_surface = SELECT

(pcurve,

surface_curve,

composite_curve_on_surface);

END_TYPE;

TYPE curve_or_annotation_curve_occurrence = SELECT

(curve,

annotation_curve_occurrence);

END_TYPE;

TYPE curve_or_render = SELECT (

curve_style);

END_TYPE;

TYPE curve_style_font_select = SELECT

(curve_style_font,

pre_defined_curve_font,

externally_defined_curve_font);

END_TYPE;

TYPE date_and_time_item = SELECT (

action,

applied_action_assignment,

applied_organization_assignment,

applied_person_and_organization_assignment,

applied_security_classification_assignment,

approval_person_organization,

certification,

contract,

document_file,

event_occurrence,

executed_action,

organizational_project,

product_definition,

product_definition_formation,

product_definition_relationship,

security_classification,

versioned_action_request);

END_TYPE;

(* Pruned unused type: date_and_time_item_203e2  *)

(* Pruned unused type: date_and_time_item_approval  *)

TYPE date_item = SELECT (

action,

applied_action_assignment,

applied_organization_assignment,

applied_person_and_organization_assignment,

applied_security_classification_assignment,

approval_person_organization,

certification,

contract,

document_file,

event_occurrence,

organizational_project,

product_definition,

product_definition_formation,

product_definition_relationship,

security_classification,

versioned_action_request);

END_TYPE;

(* Pruned unused type: date_item_203e2  *)

(* Pruned unused type: date_item_approval  *)

TYPE date_time_item = SELECT

(approval_person_organization,

certification,

change,

change_request,

contract,

product_definition,

security_classification,

start_request,

start_work);

END_TYPE;

TYPE date_time_or_event_occurrence = SELECT

(date_time_select,

event_occurrence);

END_TYPE;

TYPE date_time_select = SELECT

(date,

date_and_time,

local_time);

END_TYPE;

TYPE day_in_month_number = INTEGER;

WHERE

WR1: {1 <= SELF <= 31};

END_TYPE;

TYPE day_in_week_number = INTEGER;

WHERE

WR1: { 1 <= SELF <= 7 };

END_TYPE;

TYPE day_in_year_number = INTEGER;

WHERE

WR1: {1 <= SELF <= 366};

END_TYPE;

TYPE defined_glyph_select = SELECT

(pre_defined_character_glyph,

externally_defined_character_glyph);

END_TYPE;

TYPE defined_symbol_select = SELECT

(pre_defined_symbol,

externally_defined_symbol);

END_TYPE;

TYPE derived_property_select = SELECT (

action_property,

property_definition);

END_TYPE;

TYPE description_attribute_select = SELECT (

action_request_solution,

application_context,

approval_role,

configuration_design,

context_dependent_shape_representation,

date_role,

date_time_role,

effectivity,

external_source,

organization_role,

person_and_organization,

person_and_organization_role,

property_definition_representation,

representation);

END_TYPE;

TYPE descriptive_measure = STRING;

END_TYPE;

TYPE dimension_count = INTEGER;

WHERE

WR1: SELF > 0;

END_TYPE;

TYPE dimension_extent_usage = ENUMERATION OF

(origin,

target);

END_TYPE;

(* Pruned unused type: dimension_identification_item  *)

(* Pruned unused type: dimension_tolerance_document_reference_item  *)

TYPE dimensional_characteristic = SELECT (dimensional_location,

dimensional_size);

END_TYPE;

(* Pruned unused type: dimensioning_standard_document_reference_item  *)

TYPE direction_count_select = SELECT

(u_direction_count,

v_direction_count);

END_TYPE;

(* Pruned unused type: dm_aliasable_item  *)

(* Pruned unused type: dm_approval_item  *)

(* Pruned unused type: dm_attribute_language_item  *)

(* Pruned unused type: dm_contract_item  *)

(* Pruned unused type: dm_date_and_time_item  *)

(* Pruned unused type: dm_date_item  *)

(* Pruned unused type: dm_identification_item  *)

(* Pruned unused type: dm_multi_language_attribute_item  *)

(* Pruned unused type: dm_organization_item  *)

(* Pruned unused type: dm_person_and_organization_item  *)

(* Pruned unused type: dm_security_classification_item  *)

(* Pruned unused type: document_location_select  *)

TYPE document_reference_item = SELECT (

action_method,

dimensional_size,

executed_action,

externally_defined_dimension_definition,

product,

product_definition,

product_definition_formation,

product_definition_formation_relationship,

product_definition_relationship,

shape_aspect,

shape_aspect_relationship,

versioned_action_request);

END_TYPE;

(* Pruned unused type: document_reference_item_203e2  *)

TYPE draughting_callout_element = SELECT

(annotation_text_occurrence,

annotation_symbol_occurrence,

annotation_curve_occurrence);

END_TYPE;

TYPE effectivity_item = SELECT (

assembly_component_usage_substitute,

product,

product_definition,

product_definition_formation,

product_definition_relationship);

END_TYPE;

(* Pruned unused type: effectivity_item_203e2  *)

TYPE electric_current_measure = REAL;

END_TYPE;

(* Pruned unused type: event_occurrence_date_and_time_item  *)

(* Pruned unused type: event_occurrence_date_item  *)

TYPE event_occurrence_item = SELECT (

organizational_project);

END_TYPE;

(* Pruned unused type: event_occurrence_item_203e2  *)

(* Pruned unused type: external_class_name_item  *)

TYPE external_identification_item = SELECT (

document_file,

product_definition);

END_TYPE;

(* Pruned unused type: external_identification_item_203e2  *)

(* Pruned unused type: file_identification_item  *)

(* Pruned unused type: file_location_select  *)

(* Pruned unused type: file_version_item  *)

TYPE fill_area_style_tile_shape_select = SELECT

(fill_area_style_tile_curve_with_style,

fill_area_style_tile_coloured_region,

fill_area_style_tile_symbol_with_style,

pre_defined_tile,

externally_defined_tile);

END_TYPE;

TYPE fill_style_select = SELECT (

fill_area_style_colour,

externally_defined_tile_style,

fill_area_style_tiles,

externally_defined_hatch_style,

fill_area_style_hatching);

END_TYPE;

TYPE font_select = SELECT

(pre_defined_text_font,

externally_defined_text_font);

END_TYPE;

TYPE founded_item_select = SELECT

(founded_item,

representation_item);

END_TYPE;

TYPE geometric_set_select = SELECT

(point,

curve,

surface);

END_TYPE;

TYPE groupable_item = SELECT (

geometric_representation_item,

mapped_item,

representation_relationship_with_transformation,

shape_aspect,

styled_item);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GROUP' IN TYPEOF(SELF));

END_TYPE;

TYPE hour_in_day = INTEGER;

WHERE

WR1: { 0 <= SELF < 24 };

END_TYPE;

TYPE id_attribute_select = SELECT

(action,

address,

application_context,

group,

organizational_project,

product_category,

property_definition,

representation,

shape_aspect,

shape_aspect_relationship);

END_TYPE;

TYPE identification_item = SELECT (

approval_status,

contract,

dimensional_size,

document_file,

draughting_model,

general_property,

mechanical_design_geometric_presentation_representation,

organization,

product,

product_definition,

product_definition_formation,

security_classification,

security_classification_level,

shape_aspect_relationship,

shape_representation);

END_TYPE;

(* Pruned unused type: identification_item_203e2  *)

TYPE identifier = STRING;

END_TYPE;

(* Pruned unused type: idrm_marked_item  *)

TYPE invisibility_context = SELECT (

presentation_representation,

presentation_set);

END_TYPE;

TYPE invisible_item = SELECT

(styled_item,

presentation_layer_assignment,

representation);

END_TYPE;

TYPE knot_type = ENUMERATION OF

(uniform_knots,

quasi_uniform_knots,

piecewise_bezier_knots,

unspecified);

END_TYPE;

TYPE label = STRING;

END_TYPE;

TYPE layered_item = SELECT

(presentation_representation,

representation_item);

END_TYPE;

TYPE length_measure = REAL;

END_TYPE;

TYPE limit_condition = ENUMERATION OF

(maximum_material_condition,

least_material_condition,

regardless_of_feature_size);

END_TYPE;

TYPE list_of_reversible_topology_item =

LIST [0:?] of reversible_topology_item;

END_TYPE;

TYPE list_representation_item = LIST [1:?] OF representation_item;

END_TYPE;

TYPE luminous_intensity_measure = REAL;

END_TYPE;

TYPE marker_select = SELECT

(marker_type,

pre_defined_marker);

END_TYPE;

TYPE marker_type = ENUMERATION OF

(dot,

x,

plus,

asterisk,

ring,

square,

triangle);

END_TYPE;

TYPE mass_measure = REAL;

END_TYPE;

TYPE measure_value = SELECT

(amount_of_substance_measure,

area_measure,

celsius_temperature_measure,

context_dependent_measure,

count_measure,

descriptive_measure,

electric_current_measure,

length_measure,

luminous_intensity_measure,

mass_measure,

numeric_measure,

parameter_value,

plane_angle_measure,

positive_length_measure,

positive_plane_angle_measure,

positive_ratio_measure,

ratio_measure,

solid_angle_measure,

thermodynamic_temperature_measure,

time_measure,

volume_measure);

END_TYPE;

TYPE minute_in_hour = INTEGER;

WHERE

WR1: { 0 <= SELF <= 59 };

END_TYPE;

TYPE month_in_year_number = INTEGER;

WHERE

WR1: { 1 <= SELF <= 12 };

END_TYPE;

(* Pruned unused type: mri_aliasable_item  *)

(* Pruned unused type: mri_approval_item  *)

(* Pruned unused type: mri_attribute_language_item  *)

(* Pruned unused type: mri_date_and_time_item  *)

(* Pruned unused type: mri_date_item  *)

(* Pruned unused type: mri_identification_item  *)

(* Pruned unused type: mri_multi_language_attribute_item  *)

(* Pruned unused type: mri_organization_item  *)

(* Pruned unused type: mri_person_and_organization_item  *)

TYPE multi_language_attribute_item = SELECT (

alternate_product_relationship,

application_context,

applied_certification_assignment,

applied_document_reference,

applied_document_usage_constraint_assignment,

applied_external_identification_assignment,

applied_identification_assignment,

applied_organizational_project_assignment,

approval,

approval_relationship,

approval_status,

assembly_component_usage_substitute,

attribute_value_assignment,

certification,

certification_type,

colour,

configuration_design,

configuration_item,

contract,

date_role,

date_time_role,

descriptive_representation_item,

document_relationship,

document_usage_role,

effectivity,

effectivity_relationship,

event_occurrence,

external_source,

general_property,

general_property_relationship,

geometric_representation_item,

geometric_tolerance,

identification_role,

make_from_usage_option,

mapped_item,

object_role,

organization_relationship,

organization_role,

organizational_project,

organizational_project_relationship,

organizational_project_role,

person_and_organization,

person_and_organization_role,

product,

product_category,

product_concept,

product_concept_relationship,

product_definition,

product_definition_context,

product_definition_formation,

product_definition_formation_relationship,

product_definition_relationship,

product_definition_shape,

product_related_product_category,

property_definition,

representation,

representation_relationship,

security_classification,

security_classification_assignment,

shape_aspect,

shape_aspect_relationship,

shape_representation,

time_interval_role,

topological_representation_item,

uncertainty_measure_with_unit);

END_TYPE;

(* Pruned unused type: multi_language_attribute_item_203e2  *)

TYPE name_attribute_select = SELECT (

action_request_solution,

address,

configuration_design,

context_dependent_shape_representation,

derived_unit,

effectivity,

person_and_organization,

product_definition,

property_definition_representation);

END_TYPE;

TYPE name_item = SELECT (

assembly_component_usage,

external_class_library);

END_TYPE;

TYPE null_style = ENUMERATION OF

(null);

END_TYPE;

TYPE numeric_measure = NUMBER;

END_TYPE;

TYPE organization_item = SELECT (

action,

alternate_product_relationship,

applied_action_assignment,

applied_identification_assignment,

applied_security_classification_assignment,

approval,

assembly_component_usage_substitute,

certification,

configuration_item,

contract,

document_file,

executed_action,

general_property,

organizational_project,

product,

product_definition,

product_definition_formation,

product_definition_formation_relationship,

property_definition,

security_classification,

shape_representation,

versioned_action_request);

END_TYPE;

(* Pruned unused type: organization_item_203e2  *)

(* Pruned unused type: organizational_project_item_203e2  *)

TYPE parameter_value = REAL;

END_TYPE;

TYPE pcurve_or_surface = SELECT

(pcurve,

surface);

END_TYPE;

(* Pruned unused type: pdm_action_items  *)

(* Pruned unused type: pdm_action_request_item  *)

(* Pruned unused type: pdm_approval_item  *)

(* Pruned unused type: pdm_attribute_language_item  *)

(* Pruned unused type: pdm_certification_item  *)

(* Pruned unused type: pdm_classification_item  *)

(* Pruned unused type: pdm_date_and_time_item  *)

(* Pruned unused type: pdm_date_item  *)

(* Pruned unused type: pdm_document_reference_item  *)

(* Pruned unused type: pdm_effectivity_item  *)

(* Pruned unused type: pdm_event_occurrence_item  *)

(* Pruned unused type: pdm_external_class_name_item  *)

(* Pruned unused type: pdm_identification_item  *)

(* Pruned unused type: pdm_multi_language_attribute_item  *)

(* Pruned unused type: pdm_organization_item  *)

(* Pruned unused type: pdm_person_and_organization_item  *)

(* Pruned unused type: pdm_project_item  *)

(* Pruned unused type: pdm_security_classification_item  *)

TYPE person_and_organization_item = SELECT (

action,

alternate_product_relationship,

applied_action_assignment,

applied_identification_assignment,

applied_security_classification_assignment,

approval,

assembly_component_usage_substitute,

certification,

configuration_item,

contract,

document_file,

executed_action,

general_property,

organizational_project,

product,

product_definition,

product_definition_formation,

product_definition_formation_relationship,

property_definition,

security_classification,

shape_representation,

versioned_action_request);

END_TYPE;

(* Pruned unused type: person_and_organization_item_203e2  *)

TYPE person_organization_item = SELECT

(change,

change_request,

configuration_item,

contract,

product,

product_definition,

product_definition_formation,

security_classification,

start_request,

start_work);

END_TYPE;

TYPE person_organization_select = SELECT

(organization,

person,

person_and_organization);

END_TYPE;

TYPE plane_angle_measure = REAL;

END_TYPE;

TYPE positive_length_measure = length_measure;

WHERE

WR1: SELF > 0.0;

END_TYPE;

TYPE positive_plane_angle_measure = plane_angle_measure;

WHERE

WR1: SELF > 0.0;

END_TYPE;

TYPE positive_ratio_measure = ratio_measure;

WHERE

WR1: SELF > 0.0;

END_TYPE;

TYPE preferred_surface_curve_representation = ENUMERATION OF

(curve_3d,

pcurve_s1,

pcurve_s2);

END_TYPE;

TYPE presentable_text = STRING;

END_TYPE;

(* Pruned unused type: presentation_representation_select  *)

TYPE presentation_size_assignment_select = SELECT

(presentation_view,

presentation_area,

area_in_set);

END_TYPE;

TYPE presentation_style_select = SELECT (

point_style,

curve_style,

surface_style_usage,

symbol_style,

fill_area_style,

text_style,

null_style);

END_TYPE;

TYPE product_or_formation_or_definition = SELECT

(product,

product_definition_formation,

product_definition);

END_TYPE;

(* Pruned unused type: project_as_date_and_time_item  *)

(* Pruned unused type: project_as_date_item  *)

TYPE project_item = SELECT (

executed_action,

product_concept);

END_TYPE;

TYPE ratio_measure = REAL;

END_TYPE;

(* Pruned unused type: representation_identification_item  *)

(* Pruned unused type: representation_version_item  *)

TYPE represented_definition = SELECT (

general_property,

property_definition,

shape_aspect,

shape_aspect_relationship);

END_TYPE;

TYPE reversible_topology = SELECT

(reversible_topology_item,

list_of_reversible_topology_item,

set_of_reversible_topology_item);

END_TYPE;

TYPE reversible_topology_item = SELECT

(edge,

path,

face,

face_bound,

closed_shell,

open_shell);

END_TYPE;

TYPE role_select = SELECT (

action_assignment,

action_request_assignment,

approval_assignment,

approval_date_time,

certification_assignment,

contract_assignment,

document_reference,

effectivity_assignment,

group_assignment,

name_assignment,

security_classification_assignment);

END_TYPE;

TYPE second_in_minute = REAL;

WHERE

WR1: { 0 <= SELF <= 60.0 };

END_TYPE;

TYPE security_classification_item = SELECT (

assembly_component_usage,

document_file,

product,

product_definition,

product_definition_formation,

product_definition_usage);

END_TYPE;

(* Pruned unused type: security_classification_item_203e2  *)

TYPE set_of_reversible_topology_item =

SET [0:?] of reversible_topology_item;

END_TYPE;

TYPE set_representation_item = SET [1:?] OF representation_item;

END_TYPE;

TYPE shape_definition = SELECT

(product_definition_shape,

shape_aspect,

shape_aspect_relationship);

END_TYPE;

(* Pruned unused type: shape_tolerance_select  *)

TYPE shell = SELECT

(vertex_shell,

wire_shell,

open_shell,

closed_shell);

END_TYPE;

TYPE si_prefix = ENUMERATION OF

(exa,

peta,

tera,

giga,

mega,

kilo,

hecto,

deca,

deci,

centi,

milli,

micro,

nano,

pico,

femto,

atto);

END_TYPE;

TYPE si_unit_name = ENUMERATION OF

(metre,

gram,

second,

ampere,

kelvin,

mole,

candela,

radian,

steradian,

hertz,

newton,

pascal,

joule,

watt,

coulomb,

volt,

farad,

ohm,

siemens,

weber,

tesla,

henry,

degree_Celsius,

lumen,

lux,

becquerel,

gray,

sievert);

END_TYPE;

TYPE size_select = SELECT (

positive_length_measure,

measure_with_unit,

descriptive_measure);

END_TYPE;

TYPE solid_angle_measure = REAL;

END_TYPE;

TYPE source = ENUMERATION OF

(made,

bought,

not_known);

END_TYPE;

TYPE source_item = SELECT (

identifier);

END_TYPE;

TYPE specified_item = SELECT

(product_definition,

shape_aspect);

END_TYPE;

(* Pruned unused type: spr_document_reference_item  *)

(* Pruned unused type: spr_organization_item  *)

(* Pruned unused type: spr_person_and_organization_item  *)

(* Pruned unused type: start_request_item  *)

TYPE style_context_select = SELECT

(group,

presentation_layer_assignment,

representation,

representation_item,

presentation_set);

END_TYPE;

(* Pruned unused type: supported_item  *)

(* Pruned unused type: surface_boundary  *)

(* Pruned unused type: surface_model  *)

TYPE surface_side = ENUMERATION OF

(positive,

negative,

both);

END_TYPE;

TYPE surface_side_style_select = SELECT (

surface_side_style);

END_TYPE;

TYPE surface_style_element_select = SELECT (

surface_style_fill_area,

surface_style_boundary,

surface_style_silhouette,

surface_style_segmentation_curve,

surface_style_control_grid,

surface_style_parameter_line);

END_TYPE;

TYPE symbol_style_select = SELECT (

symbol_colour);

END_TYPE;

(* Pruned unused type: terminator  *)

TYPE text = STRING;

END_TYPE;

TYPE text_alignment = label;

END_TYPE;

TYPE text_delineation = label;

END_TYPE;

TYPE text_or_character = SELECT

(annotation_text,

annotation_text_character,

defined_character_glyph,

composite_text,

text_literal);

END_TYPE;

TYPE text_path = ENUMERATION OF

(left,

right,

up,

down);

END_TYPE;

TYPE thermodynamic_temperature_measure = REAL;

END_TYPE;

TYPE time_interval_item = SELECT (

time_interval_based_effectivity);

END_TYPE;

(* Pruned unused type: time_interval_item_203e2  *)

TYPE time_measure = REAL;

END_TYPE;

TYPE tolerance_method_definition = SELECT

(tolerance_value,

limits_and_fits);

END_TYPE;

TYPE transformation = SELECT

(item_defined_transformation,

functionally_defined_transformation);

END_TYPE;

TYPE transition_code = ENUMERATION OF

(discontinuous,

continuous,

cont_same_gradient,

cont_same_gradient_same_curvature);

END_TYPE;

TYPE trimming_preference = ENUMERATION OF

(cartesian,

parameter,

unspecified);

END_TYPE;

TYPE trimming_select = SELECT

(cartesian_point,

parameter_value);

END_TYPE;

TYPE u_direction_count = INTEGER;

WHERE

WR1: SELF > 1;

END_TYPE;

TYPE unit = SELECT

(derived_unit,

named_unit);

END_TYPE;

TYPE v_direction_count = INTEGER;

WHERE

WR1: SELF > 1;

END_TYPE;

TYPE value_qualifier = SELECT

(precision_qualifier,

type_qualifier,

uncertainty_qualifier);

END_TYPE;

TYPE vector_or_direction = SELECT

(vector,

direction);

END_TYPE;

(* Pruned unused type: versionable_item  *)

TYPE volume_measure = REAL;

END_TYPE;

TYPE week_in_year_number = INTEGER;

WHERE

WR1: { 1 <= SELF <= 53 };

END_TYPE;

(* Pruned unused type: wireframe_model  *)

TYPE work_item = SELECT

(product_definition_formation);

END_TYPE;

TYPE year_number = INTEGER;

END_TYPE;

ENTITY action;

name : label;

description : OPTIONAL text;

chosen_method : action_method;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY action_assignment

ABSTRACT SUPERTYPE;

assigned_action : action;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY action_directive;

name : label;

description : OPTIONAL text;

analysis : text;

comment : text;

requests : SET[1:?] OF versioned_action_request;

END_ENTITY;

ENTITY action_method;

name : label;

description : OPTIONAL text;

consequence : text;

purpose : text;

END_ENTITY;

ENTITY action_property;

name        : label;

description : text;

definition  : characterized_action_definition;

END_ENTITY;

ENTITY action_property_representation;

name           : label;

description    : text;

property       : action_property;

representation : representation;

END_ENTITY;

ENTITY action_relationship;

name : label;

description : OPTIONAL text;

relating_action : action;

related_action : action;

END_ENTITY;

ENTITY action_request_assignment

ABSTRACT SUPERTYPE;

assigned_action_request : versioned_action_request;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY action_request_solution;

method : action_method;

request : versioned_action_request;

DERIVE

description : text := get_description_value (SELF);

name : label := get_name_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

END_ENTITY;

ENTITY action_request_status;

status : label;

assigned_request : versioned_action_request;

END_ENTITY;

ENTITY action_status;

status : label;

assigned_action : executed_action;

END_ENTITY;

ENTITY address;

internal_location : OPTIONAL label;

street_number : OPTIONAL label;

street : OPTIONAL label;

postal_box : OPTIONAL label;

town : OPTIONAL label;

region : OPTIONAL label;

postal_code : OPTIONAL label;

country : OPTIONAL label;

facsimile_number : OPTIONAL label;

telephone_number : OPTIONAL label;

electronic_mail_address : OPTIONAL label;

telex_number : OPTIONAL label;

DERIVE

name : label := get_name_value(SELF);

url : identifier := get_id_value(SELF);

WHERE

WR1: EXISTS(internal_location) OR EXISTS(street_number) OR EXISTS(street) OR EXISTS(postal_box) OR EXISTS(town) OR EXISTS(region) OR EXISTS(postal_code) OR EXISTS(country) OR EXISTS(facsimile_number) OR EXISTS(telephone_number) OR EXISTS(electronic_mail_address) OR EXISTS(telex_number);

END_ENTITY;

ENTITY advanced_brep_shape_representation

SUBTYPE OF ( shape_representation );

WHERE

WR1 :

SIZEOF (

QUERY ( it <* SELF.items| NOT ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MANIFOLD_SOLID_BREP', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACETED_BREP', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D' ] * TYPEOF (it)) = 1) )) = 0;

WR2 :

SIZEOF (

QUERY ( it <* SELF.items| ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MANIFOLD_SOLID_BREP', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' ] * TYPEOF (it)) = 1) )) > 0;

WR3 :

SIZEOF (

QUERY ( msb <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MANIFOLD_SOLID_BREP' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( csh <* msb_shells(msb)| NOT ( SIZEOF (

QUERY ( fcs <* csh\connected_face_set.cfs_faces| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fcs)) )) = 0) )) = 0) )) = 0;

WR4 :

SIZEOF (

QUERY ( msb <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MANIFOLD_SOLID_BREP' IN TYPEOF (it)) )| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_CLOSED_SHELL' IN TYPEOF (msb\manifold_solid_brep.outer)) )) = 0;

WR5 :

SIZEOF (

QUERY ( brv <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BREP_WITH_VOIDS' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( csh <* brv\brep_with_voids.voids| csh\oriented_closed_shell.orientation )) = 0) )) = 0;

WR6 :

SIZEOF (

QUERY ( mi <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_BREP_SHAPE_REPRESENTATION' IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation)) )) = 0;

END_ENTITY;

ENTITY advanced_face

SUBTYPE OF ( face_surface );

WHERE

WR1 :

SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELEMENTARY_SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SWEPT_SURFACE' ] * TYPEOF (face_geometry)) = 1;

WR2 :

SIZEOF (

QUERY ( elp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) )| NOT ( SIZEOF (

QUERY ( oe <* elp_fbnds.bound\path.edge_list| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_CURVE' IN TYPEOF (oe\oriented_edge.edge_element)) )) = 0) )) = 0;

WR3 :

SIZEOF (

QUERY ( elp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) )| NOT ( SIZEOF (

QUERY ( oe <* elp_fbnds.bound\path.edge_list| NOT ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE' ] * TYPEOF (oe.edge_element\edge_curve.edge_geometry)) = 1) )) = 0) )) = 0;

WR4 :

SIZEOF (

QUERY ( elp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) )| NOT ( SIZEOF (

QUERY ( oe <* elp_fbnds.bound\path.edge_list| NOT ((('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (oe\edge.edge_start)) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF (oe\edge.edge_start\vertex_point.vertex_geometry))) AND (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (oe\edge.edge_end)) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF (oe\edge.edge_end\vertex_point.vertex_geometry)))) )) = 0) )) = 0;

WR5 :

SIZEOF (

QUERY ( elp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) )| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_PATH' IN TYPEOF (elp_fbnds.bound)) )) = 0;

WR6 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SWEPT_SURFACE' IN TYPEOF (face_geometry)) OR ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE' ] * TYPEOF (face_geometry\swept_surface.swept_curve)) = 1);

WR7 :

SIZEOF (

QUERY ( vlp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP' IN TYPEOF (bnds.bound)) )| NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (vlp_fbnds\face_bound.bound\vertex_loop.loop_vertex)) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF (vlp_fbnds\face_bound.bound\vertex_loop.loop_vertex\vertex_point.vertex_geometry))) )) = 0;

WR8 :

SIZEOF (

QUERY ( bnd <* bounds| NOT ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP' ] * TYPEOF (bnd.bound)) = 1) )) = 0;

WR9 :

SIZEOF (

QUERY ( elp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) )| NOT ( SIZEOF (

QUERY ( oe <* elp_fbnds.bound\path.edge_list| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE' IN TYPEOF (oe\oriented_edge.edge_element\edge_curve.edge_geometry)) AND NOT ( SIZEOF (

QUERY ( sc_ag <* oe.edge_element\edge_curve.edge_geometry\surface_curve.associated_geometry| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF (sc_ag)) )) = 0) )) = 0) )) = 0;

WR10 : (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SWEPT_SURFACE' IN TYPEOF (face_geometry)) OR (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF (face_geometry\swept_surface.swept_curve)) OR ( SIZEOF (face_geometry\swept_surface.swept_curve\polyline.points) >= 3))) AND ( SIZEOF (

QUERY ( elp_fbnds <*

QUERY ( bnds <* bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) )| NOT ( SIZEOF (

QUERY ( oe <* elp_fbnds.bound\path.edge_list| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF (oe\oriented_edge.edge_element\edge_curve.edge_geometry)) AND NOT ( SIZEOF (oe\oriented_edge.edge_element\edge_curve.edge_geometry\polyline.points) >= 3) )) = 0) )) = 0);

END_ENTITY;

ENTITY alternate_product_relationship;

name        : label;

definition  : OPTIONAL text;

alternate   : product;

base        : product;

basis       : text;

UNIQUE

UR1: alternate, base;

WHERE

WR1: alternate :<>: base;

END_ENTITY;

ENTITY amount_of_substance_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AMOUNT_OF_SUBSTANCE_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY amount_of_substance_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 1.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY angular_dimension

SUBTYPE OF (dimension_curve_directed_callout);

END_ENTITY;

ENTITY angular_location

SUBTYPE OF (dimensional_location);

angle_selection : angle_relator;

END_ENTITY;

ENTITY angular_size

SUBTYPE OF (dimensional_size);

angle_selection : angle_relator;

END_ENTITY;

ENTITY angularity_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) < 3;

END_ENTITY;

ENTITY annotation_curve_occurrence

SUBTYPE OF (annotation_occurrence);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF (SELF\styled_item.item);

END_ENTITY;

ENTITY annotation_fill_area

SUBTYPE OF (geometric_representation_item);

boundaries : SET [1:?] OF curve;

END_ENTITY;

ENTITY annotation_fill_area_occurrence

SUBTYPE OF (annotation_occurrence);

fill_style_target : point;

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_FILL_AREA' IN

TYPEOF (SELF.item);

END_ENTITY;

ENTITY annotation_occurrence

SUPERTYPE OF (ONEOF (

ANNOTATION_POINT_OCCURRENCE,

ANNOTATION_CURVE_OCCURRENCE,

ANNOTATION_FILL_AREA_OCCURRENCE,

ANNOTATION_TEXT_OCCURRENCE,

ANNOTATION_SYMBOL_OCCURRENCE))

SUBTYPE OF (styled_item);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_ITEM' IN

TYPEOF (SELF);

END_ENTITY;

ENTITY annotation_occurrence_associativity

SUBTYPE OF (annotation_occurrence_relationship);

WHERE

WR1:  SIZEOF (TYPEOF (SELF.related_annotation_occurrence) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_FILL_AREA_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_CURVE']) = 1;

END_ENTITY;

ENTITY annotation_occurrence_relationship;

name                           : label;

description                    : text;

relating_annotation_occurrence : annotation_occurrence;

related_annotation_occurrence  : annotation_occurrence;

END_ENTITY;

ENTITY annotation_point_occurrence

SUBTYPE OF (annotation_occurrence);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT' IN TYPEOF (SELF\styled_item.item);

END_ENTITY;

ENTITY annotation_subfigure_occurrence

SUBTYPE OF (annotation_symbol_occurrence);

WHERE

WR1: SIZEOF (QUERY (sty <* SELF.styles |

NOT (SIZEOF (sty.styles) = 1)

)) = 0;

WR2: SIZEOF (QUERY (sty <* SELF.styles |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.NULL_STYLE'

IN TYPEOF (sty.styles[1]))       ))=0;

WR3: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL'

IN TYPEOF (SELF.item));

WR4: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_SUBFIGURE_REPRESENTATION'

IN TYPEOF

(SELF.item\mapped_item.mapping_source.mapped_representation));

END_ENTITY;

ENTITY annotation_symbol

SUBTYPE OF(mapped_item);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_REPRESENTATION_MAP' IN

TYPEOF (SELF\mapped_item.mapping_source);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_TARGET' IN

TYPEOF (SELF\mapped_item.mapping_target);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_ITEM' IN

TYPEOF (SELF);

END_ENTITY;

ENTITY annotation_symbol_occurrence

SUBTYPE OF (annotation_occurrence);

WHERE

WR1: SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEFINED_SYMBOL'] *

TYPEOF(SELF\styled_item.item)) > 0;

END_ENTITY;

ENTITY annotation_table

SUBTYPE OF(annotation_symbol);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_REPRESENTATION' IN

TYPEOF (SELF\mapped_item.mapping_source.mapped_representation);

END_ENTITY;

ENTITY annotation_table_occurrence

SUBTYPE OF (annotation_symbol_occurrence);

WHERE

WR1: SIZEOF (

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TABLE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEFINED_TABLE'] *

TYPEOF (SELF\styled_item.item)) > 0;

END_ENTITY;

ENTITY annotation_text

SUBTYPE OF (mapped_item);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT' IN

TYPEOF( SELF\mapped_item.mapping_target);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_STRING_REPRESENTATION' IN

TYPEOF( SELF\mapped_item.mapping_source.mapped_representation);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_ITEM' IN

TYPEOF( SELF);

END_ENTITY;

ENTITY annotation_text_character

SUBTYPE OF (mapped_item);

alignment : text_alignment;

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CHARACTER_GLYPH_SYMBOL' IN

TYPEOF (SELF\mapped_item.mapping_source.mapped_representation);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT' IN

TYPEOF (SELF\mapped_item.mapping_target);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_ITEM' IN

TYPEOF (SELF);

END_ENTITY;

ENTITY annotation_text_occurrence

SUBTYPE OF (annotation_occurrence);

WHERE

WR1: SIZEOF (

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_CHARACTER',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEFINED_CHARACTER_GLYPH',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'] *

TYPEOF (SELF\styled_item.item)) > 0;

END_ENTITY;

ENTITY annotation_text_with_associated_curves

SUBTYPE OF (annotation_text);

associated_curves : SET[1:?] of curve;

END_ENTITY;

ENTITY annotation_text_with_blanking_box

SUBTYPE OF (annotation_text);

blanking : planar_box;

END_ENTITY;

ENTITY annotation_text_with_delineation

SUBTYPE OF (annotation_text);

delineation : text_delineation;

END_ENTITY;

ENTITY annotation_text_with_extent

SUBTYPE OF (annotation_text);

extent : planar_extent;

END_ENTITY;

ENTITY apex

SUBTYPE OF (derived_shape_aspect);

END_ENTITY;

ENTITY application_context;

application : label;

DERIVE

description : text := get_description_value (SELF);

id : identifier := get_id_value (SELF);

INVERSE

context_elements : SET[1:?] OF application_context_element FOR frame_of_reference;

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY application_context_element

SUPERTYPE OF (ONEOF (

PRODUCT_CONCEPT_CONTEXT,

PRODUCT_CONTEXT,

PRODUCT_DEFINITION_CONTEXT));

name : label;

frame_of_reference : application_context;

END_ENTITY;

ENTITY application_context_relationship;

name : label;

description : OPTIONAL text;

relating_context : application_context;

related_context : application_context;

END_ENTITY;

ENTITY application_protocol_definition;

status : label;

application_interpreted_model_schema_name : label;

application_protocol_year : year_number;

application : application_context;

END_ENTITY;

ENTITY applied_action_assignment

SUBTYPE OF (action_assignment);

items : SET [1 : ?] OF action_items;

END_ENTITY;

ENTITY applied_action_request_assignment

SUBTYPE OF (action_request_assignment);

items : SET [1 : ?] OF action_request_item;

END_ENTITY;

ENTITY applied_approval_assignment

SUBTYPE OF (approval_assignment);

items : SET[1:?] OF approval_item;

END_ENTITY;

ENTITY applied_certification_assignment

SUBTYPE OF (certification_assignment);

items : SET[1:?] OF certification_item;

END_ENTITY;

ENTITY applied_classification_assignment

SUBTYPE OF (classification_assignment);

items : SET[1:?] OF classification_item;

END_ENTITY;

ENTITY applied_contract_assignment

SUBTYPE OF (contract_assignment);

items : SET [1:?] OF contract_item;

END_ENTITY;

ENTITY applied_date_and_time_assignment

SUBTYPE OF (date_and_time_assignment);

items : SET [1:?] OF date_and_time_item;

END_ENTITY;

ENTITY applied_date_assignment

SUBTYPE OF (date_assignment);

items : SET [1:?] OF date_item;

END_ENTITY;

ENTITY applied_document_reference

SUBTYPE OF (document_reference);

items : SET[1:?] OF document_reference_item;

END_ENTITY;

ENTITY applied_document_usage_constraint_assignment

SUBTYPE OF (document_usage_constraint_assignment);

items : SET[1:?] OF document_reference_item;

END_ENTITY;

ENTITY applied_effectivity_assignment

SUBTYPE OF (effectivity_assignment);

items : SET[1:?] OF effectivity_item;

END_ENTITY;

ENTITY applied_event_occurrence_assignment

SUBTYPE OF (event_occurrence_assignment);

items : SET[1:?] OF event_occurrence_item;

END_ENTITY;

ENTITY applied_external_identification_assignment

SUBTYPE OF (external_identification_assignment);

items : SET [1 : ?] OF external_identification_item;

END_ENTITY;

ENTITY applied_group_assignment

SUBTYPE OF (group_assignment);

items : SET[1:?] OF groupable_item;

END_ENTITY;

ENTITY applied_identification_assignment

SUBTYPE OF (identification_assignment);

items : SET[1:?] OF identification_item;

END_ENTITY;

ENTITY applied_name_assignment

SUBTYPE OF (name_assignment);

item : name_item;

END_ENTITY;

ENTITY applied_organization_assignment

SUBTYPE OF (organization_assignment);

items : SET [1:?] OF organization_item;

END_ENTITY;

ENTITY applied_organizational_project_assignment

SUBTYPE OF (organizational_project_assignment);

items : SET[1:?] OF project_item;

END_ENTITY;

ENTITY applied_person_and_organization_assignment

SUBTYPE OF (person_and_organization_assignment);

items : SET [1:?] OF person_and_organization_item;

END_ENTITY;

ENTITY applied_security_classification_assignment

SUBTYPE OF (security_classification_assignment);

items : SET [1:?] OF security_classification_item;

END_ENTITY;

ENTITY applied_time_interval_assignment

SUBTYPE OF (time_interval_assignment);

items : SET[0:?] OF time_interval_item;

END_ENTITY;

ENTITY approval;

status : approval_status;

level : label;

END_ENTITY;

ENTITY approval_assignment

ABSTRACT SUPERTYPE;

assigned_approval : approval;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY approval_date_time;

date_time : date_time_select;

dated_approval : approval;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY approval_person_organization;

person_organization : person_organization_select;

authorized_approval : approval;

role : approval_role;

END_ENTITY;

ENTITY approval_relationship;

name : label;

description : OPTIONAL text;

relating_approval : approval;

related_approval : approval;

END_ENTITY;

ENTITY approval_role;

role : label;

DERIVE

description : text := get_description_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY approval_status;

name : label;

END_ENTITY;

ENTITY area_in_set;

area   : presentation_area;

in_set : presentation_set;

END_ENTITY;

ENTITY area_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AREA_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY area_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 2.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY assembly_component_usage

SUPERTYPE OF (ONEOF (

NEXT_ASSEMBLY_USAGE_OCCURRENCE,

SPECIFIED_HIGHER_USAGE_OCCURRENCE,

PROMISSORY_USAGE_OCCURRENCE))

SUBTYPE OF (product_definition_usage);

reference_designator : OPTIONAL identifier;

END_ENTITY;

ENTITY assembly_component_usage_substitute;

name              : label;

definition        : OPTIONAL text;

base              : assembly_component_usage;

substitute        : assembly_component_usage;

UNIQUE

UR1: base,substitute;

WHERE

WR1: base.relating_product_definition :=:

substitute.relating_product_definition;

WR2: base :<>: substitute;

END_ENTITY;

ENTITY attribute_classification_assignment

ABSTRACT SUPERTYPE;

assigned_class : group;

attribute_name : label;

role : classification_role;

END_ENTITY;

ENTITY attribute_language_assignment

SUBTYPE OF (attribute_classification_assignment);

SELF\attribute_classification_assignment.assigned_class: language;

items : SET [1:?] OF attribute_language_item;

WHERE

WR1: SELF\attribute_classification_assignment.role.name IN ['primary', 'translated'];

WR2: SELF\attribute_classification_assignment.attribute_name<> '';

END_ENTITY;

ENTITY attribute_value_assignment

ABSTRACT SUPERTYPE;

attribute_name : label;

attribute_value : attribute_type;

role : attribute_value_role;

END_ENTITY;

ENTITY attribute_value_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY axis1_placement

SUBTYPE OF (placement);

axis     : OPTIONAL direction;

DERIVE

z : direction := NVL(normalise(axis), dummy_gri ||

direction([0.0,0.0,1.0]));

WHERE

WR1: SELF\geometric_representation_item.dim  = 3;

END_ENTITY;

ENTITY axis2_placement_2d

SUBTYPE OF (placement);

ref_direction : OPTIONAL direction;

DERIVE

p             : LIST [2:2] OF direction := build_2axes(ref_direction);

WHERE

WR1: SELF\geometric_representation_item.dim = 2;

END_ENTITY;

ENTITY axis2_placement_3d

SUBTYPE OF (placement);

axis          : OPTIONAL direction;

ref_direction : OPTIONAL direction;

DERIVE

p             : LIST [3:3] OF direction := build_axes(axis,ref_direction);

WHERE

WR1: SELF\placement.location.dim = 3;

WR2: (NOT (EXISTS (axis))) OR (axis.dim = 3);

WR3: (NOT (EXISTS (ref_direction))) OR (ref_direction.dim = 3);

WR4: (NOT (EXISTS (axis))) OR (NOT (EXISTS (ref_direction))) OR

(cross_product(axis,ref_direction).magnitude > 0.0);

END_ENTITY;

ENTITY b_spline_curve

SUPERTYPE OF (ONEOF (

UNIFORM_CURVE,

B_SPLINE_CURVE_WITH_KNOTS,

QUASI_UNIFORM_CURVE,

BEZIER_CURVE)

ANDOR

RATIONAL_B_SPLINE_CURVE)

SUBTYPE OF (bounded_curve);

degree               : INTEGER;

control_points_list  : LIST [2:?] OF cartesian_point;

curve_form           : b_spline_curve_form;

closed_curve         : LOGICAL;

self_intersect       : LOGICAL;

DERIVE

upper_index_on_control_points  : INTEGER

:= (SIZEOF(control_points_list) - 1);

control_points       : ARRAY [0:upper_index_on_control_points]

OF cartesian_point

:= list_to_array(control_points_list,0,

upper_index_on_control_points);

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.UNIFORM_CURVE' IN TYPEOF(self)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.QUASI_UNIFORM_CURVE' IN TYPEOF(self)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BEZIER_CURVE' IN TYPEOF(self)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE_WITH_KNOTS' IN TYPEOF(self));

END_ENTITY;

ENTITY b_spline_curve_with_knots

SUBTYPE OF (b_spline_curve);

knot_multiplicities  : LIST [2:?] OF INTEGER;

knots                : LIST [2:?] OF parameter_value;

knot_spec            : knot_type;

DERIVE

upper_index_on_knots : INTEGER := SIZEOF(knots);

WHERE

WR1: constraints_param_b_spline(degree, upper_index_on_knots,

upper_index_on_control_points,

knot_multiplicities, knots);

WR2: SIZEOF(knot_multiplicities) = upper_index_on_knots;

END_ENTITY;

ENTITY b_spline_surface

SUPERTYPE OF (ONEOF (

B_SPLINE_SURFACE_WITH_KNOTS,

UNIFORM_SURFACE,

QUASI_UNIFORM_SURFACE,

BEZIER_SURFACE)

ANDOR

RATIONAL_B_SPLINE_SURFACE)

SUBTYPE OF (bounded_surface);

u_degree             : INTEGER;

v_degree             : INTEGER;

control_points_list  : LIST [2:?] OF

LIST [2:?] OF cartesian_point;

surface_form         : b_spline_surface_form;

u_closed             : LOGICAL;

v_closed             : LOGICAL;

self_intersect       : LOGICAL;

DERIVE

u_upper             : INTEGER := SIZEOF(control_points_list) - 1;

v_upper             : INTEGER := SIZEOF(control_points_list[1]) - 1;

control_points      : ARRAY [0:u_upper] OF ARRAY [0:v_upper] OF

cartesian_point

:= make_array_of_array(control_points_list,

0,u_upper,0,v_upper);

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.UNIFORM_SURFACE' IN TYPEOF(SELF)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.QUASI_UNIFORM_SURFACE' IN TYPEOF(SELF)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BEZIER_SURFACE' IN TYPEOF(SELF)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_SURFACE_WITH_KNOTS' IN TYPEOF(SELF));

END_ENTITY;

ENTITY b_spline_surface_with_knots

SUBTYPE OF (b_spline_surface);

u_multiplicities  : LIST [2:?] OF INTEGER;

v_multiplicities  : LIST [2:?] OF INTEGER;

u_knots           : LIST [2:?] OF parameter_value;

v_knots           : LIST [2:?] OF parameter_value;

knot_spec         : knot_type;

DERIVE

knot_u_upper      : INTEGER := SIZEOF(u_knots);

knot_v_upper      : INTEGER := SIZEOF(v_knots);

WHERE

WR1: constraints_param_b_spline(SELF\b_spline_surface.u_degree,

knot_u_upper, SELF\b_spline_surface.u_upper,

u_multiplicities, u_knots);

WR2: constraints_param_b_spline(SELF\b_spline_surface.v_degree,

knot_v_upper, SELF\b_spline_surface.v_upper,

v_multiplicities, v_knots);

WR3: SIZEOF(u_multiplicities) = knot_u_upper;

WR4: SIZEOF(v_multiplicities) = knot_v_upper;

END_ENTITY;

ENTITY background_colour

SUBTYPE OF (colour);

presentation : area_or_view;

UNIQUE

UR1:  presentation;

END_ENTITY;

ENTITY bezier_curve

SUBTYPE OF (b_spline_curve);

END_ENTITY;

ENTITY bezier_surface

SUBTYPE OF (b_spline_surface);

END_ENTITY;

ENTITY block

SUBTYPE OF (geometric_representation_item);

position : axis2_placement_3d;

x        : positive_length_measure;

y        : positive_length_measure;

z        : positive_length_measure;

END_ENTITY;

ENTITY boolean_result

SUBTYPE OF (geometric_representation_item);

operator        : boolean_operator;

first_operand   :  boolean_operand;

second_operand  :  boolean_operand;

END_ENTITY;

ENTITY boundary_curve

SUBTYPE OF (composite_curve_on_surface);

WHERE

WR1: SELF\composite_curve.closed_curve;

END_ENTITY;

ENTITY bounded_curve

SUPERTYPE OF (ONEOF (

POLYLINE,

B_SPLINE_CURVE,

TRIMMED_CURVE,

BOUNDED_PCURVE,

BOUNDED_SURFACE_CURVE,

COMPOSITE_CURVE))

SUBTYPE OF (curve);

END_ENTITY;

ENTITY bounded_pcurve

SUBTYPE OF (pcurve, bounded_curve);

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOUNDED_CURVE' IN

TYPEOF(SELF\pcurve.reference_to_curve.items[1]));

END_ENTITY;

ENTITY bounded_surface

SUPERTYPE OF (ONEOF (

B_SPLINE_SURFACE,

RECTANGULAR_TRIMMED_SURFACE,

CURVE_BOUNDED_SURFACE,

RECTANGULAR_COMPOSITE_SURFACE))

SUBTYPE OF (surface);

END_ENTITY;

ENTITY bounded_surface_curve

SUBTYPE OF (surface_curve, bounded_curve);

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOUNDED_CURVE' IN

TYPEOF(SELF\surface_curve.curve_3d));

END_ENTITY;

ENTITY box_domain

SUBTYPE OF (founded_item);

corner  : cartesian_point;

xlength : positive_length_measure;

ylength : positive_length_measure;

zlength : positive_length_measure;

WHERE

WR1: SIZEOF(QUERY(item <* USEDIN(SELF,'')|

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOXED_HALF_SPACE'

IN TYPEOF(item)))) = 0;

END_ENTITY;

ENTITY boxed_half_space

SUBTYPE OF(half_space_solid);

enclosure : box_domain;

END_ENTITY;

ENTITY brep_with_voids

SUBTYPE OF (manifold_solid_brep);

voids : SET [1:?] OF oriented_closed_shell;

END_ENTITY;

ENTITY calendar_date

SUBTYPE OF (date);

day_component : day_in_month_number;

month_component : month_in_year_number;

WHERE

WR1: valid_calendar_date (SELF);

END_ENTITY;

ENTITY camera_image

SUBTYPE OF (mapped_item);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CAMERA_USAGE'

IN TYPEOF (SELF\mapped_item.mapping_source);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLANAR_BOX'

IN TYPEOF (SELF\mapped_item.mapping_target);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_ITEM'

IN TYPEOF (SELF);

END_ENTITY;

ENTITY camera_image_3d_with_scale

SUBTYPE OF (camera_image);

DERIVE

scale: positive_ratio_measure := ((SELF\mapped_item.mapping_target\

planar_extent.size_in_x) / (SELF\mapped_item.mapping_source.

mapping_origin\camera_model_d3.perspective_of_volume.view_window.

size_in_x));

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CAMERA_MODEL_D3'

IN TYPEOF (SELF\mapped_item.mapping_source.mapping_origin));

WR2: aspect_ratio(SELF\mapped_item.mapping_target) =

aspect_ratio(SELF\mapped_item.mapping_source.mapping_origin\

camera_model_d3.perspective_of_volume.view_window);

WR3: SELF\mapped_item.mapping_source.mapping_origin\camera_model_d3.

perspective_of_volume.front_plane_clipping

AND

SELF\mapped_item.mapping_source.mapping_origin\camera_model_d3.

perspective_of_volume.view_volume_sides_clipping;

WR4: (SELF\mapped_item.mapping_target\planar_extent.size_in_x > 0)

AND

(SELF\mapped_item.mapping_target\planar_extent.size_in_y > 0);

WR5: (SELF\mapped_item.mapping_source.mapping_origin\camera_model_d3.

perspective_of_volume.view_window.size_in_x > 0)

AND

(SELF\mapped_item.mapping_source.mapping_origin\camera_model_d3.

perspective_of_volume.view_window.size_in_y > 0);

WR6: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AXIS2_PLACEMENT_2D' IN TYPEOF (SELF\mapped_item.

mapping_target\planar_box.placement))

AND NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AXIS2_PLACEMENT_3D' IN TYPEOF (SELF\mapped_item.

mapping_target\planar_box.placement));

END_ENTITY;

ENTITY camera_model

SUBTYPE OF (geometric_representation_item);

WHERE

WR1: (SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'ITEM_DEFINED_TRANSFORMATION.' +

'TRANSFORM_ITEM_1')) +

SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'REPRESENTATION_MAP.MAPPING_ORIGIN'))

) > 0;

WR2: SIZEOF(USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'STYLED_ITEM.ITEM')) = 0;

END_ENTITY;

ENTITY camera_model_d3

SUBTYPE OF (camera_model);

view_reference_system : axis2_placement_3d;

perspective_of_volume : view_volume;

WHERE

WR1: (dot_product (SELF.view_reference_system.p[3],

SELF.perspective_of_volume.view_window.placement.p[3]) = 1.0)

AND

(SELF.view_reference_system.location.coordinates[3] =

SELF.perspective_of_volume.view_window.

placement.location.coordinates[3]);

WR2: SELF\geometric_representation_item.dim = 3;

END_ENTITY;

ENTITY camera_usage

SUBTYPE OF (representation_map);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_REPRESENTATION'

IN TYPEOF(SELF\representation_map.mapped_representation));

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CAMERA_MODEL'

IN TYPEOF (SELF\representation_map.mapping_origin);

END_ENTITY;

ENTITY cartesian_point

SUBTYPE OF (point);

coordinates  : LIST [1:3] OF length_measure;

END_ENTITY;

ENTITY cartesian_transformation_operator

SUPERTYPE OF (ONEOF (

CARTESIAN_TRANSFORMATION_OPERATOR_2D,

CARTESIAN_TRANSFORMATION_OPERATOR_3D))

SUBTYPE OF (geometric_representation_item,

functionally_defined_transformation);

axis1        : OPTIONAL direction;

axis2        : OPTIONAL direction;

local_origin : cartesian_point;

scale        : OPTIONAL REAL;

DERIVE

scl          : REAL := NVL(scale, 1.0);

WHERE

WR1: scl > 0.0;

END_ENTITY;

ENTITY cartesian_transformation_operator_2d

SUBTYPE OF (cartesian_transformation_operator);

DERIVE

u : LIST[2:2] OF direction :=

base_axis(2,SELF\cartesian_transformation_operator.axis1,

SELF\cartesian_transformation_operator.axis2,?);

WHERE

WR1: SELF\geometric_representation_item.dim = 2;

END_ENTITY;

ENTITY cartesian_transformation_operator_3d

SUBTYPE OF (cartesian_transformation_operator);

axis3 : OPTIONAL direction;

DERIVE

u     : LIST[3:3] OF direction

:= base_axis(3,SELF\cartesian_transformation_operator.axis1,

SELF\cartesian_transformation_operator.axis2,axis3);

WHERE

WR1: SELF\geometric_representation_item.dim = 3;

END_ENTITY;

ENTITY cc_design_approval

SUBTYPE OF (approval_assignment);

items : SET[1:?] OF approved_item;

END_ENTITY;

ENTITY cc_design_certification

SUBTYPE OF (certification_assignment);

items : SET[1:?] OF certified_item;

END_ENTITY;

ENTITY cc_design_contract

SUBTYPE OF (contract_assignment);

items : SET[1:?] OF contracted_item;

END_ENTITY;

ENTITY cc_design_date_and_time_assignment

SUBTYPE OF (date_and_time_assignment);

items : SET[1:?] OF date_time_item;

END_ENTITY;

ENTITY cc_design_person_and_organization_assignment

SUBTYPE OF (person_and_organization_assignment);

items : SET[1:?] OF person_organization_item;

WHERE

WR1: cc_design_person_and_organization_correlation(SELF);

END_ENTITY;

ENTITY cc_design_security_classification

SUBTYPE OF (security_classification_assignment);

items : SET[1:?] OF classified_item;

END_ENTITY;

ENTITY cc_design_specification_reference

SUBTYPE OF (document_reference);

items : SET[1:?] OF specified_item;

END_ENTITY;

ENTITY celsius_temperature_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.THERMODYNAMIC_TEMPERATURE_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY centre_of_symmetry

SUBTYPE OF (derived_shape_aspect);

WHERE

WR1: SIZEOF

(QUERY(sadr<*SELF\derived_shape_aspect.deriving_relationships|

NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMMETRIC_SHAPE_ASPECT'

IN TYPEOF

(sadr\shape_aspect_relationship.related_shape_aspect))))=0;

END_ENTITY;

ENTITY certification;

name : label;

purpose : text;

kind : certification_type;

END_ENTITY;

ENTITY certification_assignment

ABSTRACT SUPERTYPE;

assigned_certification : certification;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY certification_type;

description : label;

END_ENTITY;

ENTITY change

SUBTYPE OF (action_assignment);

items : SET[1:?] OF work_item;

END_ENTITY;

ENTITY change_request

SUBTYPE OF (action_request_assignment);

items : SET[1:?] OF change_request_item;

END_ENTITY;

ENTITY character_glyph_style_outline;

outline_style : curve_style;

END_ENTITY;

ENTITY character_glyph_style_stroke;

stroke_style : curve_style;

END_ENTITY;

ENTITY characterized_object;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY circle

SUBTYPE OF (conic);

radius   : positive_length_measure;

END_ENTITY;

ENTITY circular_runout_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 2;

END_ENTITY;

ENTITY class

SUBTYPE OF (group);

END_ENTITY;

ENTITY class_by_extension

SUBTYPE OF (class);

END_ENTITY;

ENTITY class_by_intension

SUBTYPE OF (class);

END_ENTITY;

ENTITY classification_assignment

ABSTRACT SUPERTYPE;

assigned_class : group;

role : classification_role;

END_ENTITY;

ENTITY classification_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY closed_shell

SUBTYPE OF (connected_face_set);

END_ENTITY;

ENTITY coaxiality_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 2;

END_ENTITY;

ENTITY colour;

END_ENTITY;

ENTITY colour_rgb

SUBTYPE OF (colour_specification);

red   : REAL;

green : REAL;

blue  : REAL;

WHERE

WR1: {0.0 <= red <= 1.0};

WR2: {0.0 <= green <= 1.0};

WR3: {0.0 <= blue <= 1.0};

END_ENTITY;

ENTITY colour_specification

SUBTYPE OF (colour);

name : label;

END_ENTITY;

ENTITY common_datum

SUBTYPE OF ( composite_shape_aspect , datum );

WHERE

WR1 :

SIZEOF (SELF.component_relationships) = 2;

WR2 :

SIZEOF (

QUERY ( sar <* SELF.component_relationships| NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM' IN TYPEOF (sar.related_shape_aspect)) AND NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMMON_DATUM' IN TYPEOF (sar.related_shape_aspect))) )) = 0;

END_ENTITY;

ENTITY composite_curve

SUBTYPE OF (bounded_curve);

segments       : LIST [1:?] OF composite_curve_segment;

self_intersect : LOGICAL;

DERIVE

n_segments     : INTEGER := SIZEOF(segments);

closed_curve   : LOGICAL

:= segments[n_segments].transition <> discontinuous;

WHERE

WR1: ((NOT closed_curve) AND (SIZEOF(QUERY(temp <* segments |

temp.transition = discontinuous)) = 1)) OR

((closed_curve) AND (SIZEOF(QUERY(temp <* segments |

temp.transition = discontinuous)) = 0));

END_ENTITY;

ENTITY composite_curve_on_surface

SUPERTYPE OF (

BOUNDARY_CURVE)

SUBTYPE OF (composite_curve);

DERIVE

basis_surface : SET[0:2] OF surface :=

get_basis_surface(SELF);

WHERE

WR1: SIZEOF(basis_surface) > 0;

WR2: constraints_composite_curve_on_surface(SELF);

END_ENTITY;

ENTITY composite_curve_segment

SUBTYPE OF (founded_item);

transition    : transition_code;

same_sense    : BOOLEAN;

parent_curve  : curve;

INVERSE

using_curves  : BAG[1:?] OF composite_curve FOR segments;

WHERE

WR1 : ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOUNDED_CURVE' IN TYPEOF(parent_curve));

END_ENTITY;

ENTITY composite_shape_aspect

SUBTYPE OF (shape_aspect);

INVERSE

component_relationships : SET [2:?] OF shape_aspect_relationship

FOR relating_shape_aspect;

END_ENTITY;

ENTITY composite_text

SUBTYPE OF (geometric_representation_item);

collected_text : SET[2:?] of text_or_character;

WHERE

WR1: acyclic_composite_text( SELF, SELF.collected_text);

END_ENTITY;

ENTITY composite_text_with_associated_curves

SUBTYPE OF (composite_text);

associated_curves : SET[1:?] of curve;

END_ENTITY;

ENTITY composite_text_with_blanking_box

SUBTYPE OF (composite_text);

blanking : planar_box;

END_ENTITY;

ENTITY composite_text_with_delineation

SUBTYPE OF (composite_text);

delineation : text_delineation;

END_ENTITY;

ENTITY composite_text_with_extent

SUBTYPE OF (composite_text);

extent : planar_extent;

END_ENTITY;

ENTITY compound_representation_item

SUBTYPE OF (representation_item);

item_element : compound_item_definition;

END_ENTITY;

ENTITY concentricity_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) = 1;

END_ENTITY;

ENTITY configuration_design;

configuration : configuration_item;

design        : configuration_design_item;

DERIVE

name          : label := get_name_value (SELF);

description   : text := get_description_value (SELF);

UNIQUE

UR1: configuration, design;

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY configuration_effectivity

SUBTYPE OF (product_definition_effectivity);

configuration : configuration_design;

UNIQUE

UR1: configuration,

usage,

id;

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION_USAGE' IN

TYPEOF (SELF\product_definition_effectivity.usage);

END_ENTITY;

ENTITY configuration_item;

id                  :  identifier;

name                :  label;

description         :  OPTIONAL text;

item_concept        :  product_concept;

purpose             :  OPTIONAL label;

END_ENTITY;

ENTITY conic

SUPERTYPE OF (ONEOF (

CIRCLE,

ELLIPSE,

HYPERBOLA,

PARABOLA))

SUBTYPE OF (curve);

position: axis2_placement;

END_ENTITY;

ENTITY

conical_surface

SUBTYPE OF (elementary_surface);

radius     : length_measure;

semi_angle : plane_angle_measure;

WHERE

WR1: radius >= 0.0;

END_ENTITY;

ENTITY connected_edge_set

SUBTYPE OF (topological_representation_item);

ces_edges : SET [1:?] OF edge;

END_ENTITY;

ENTITY connected_face_set

SUPERTYPE OF (ONEOF (

CLOSED_SHELL,

OPEN_SHELL))

SUBTYPE OF (topological_representation_item);

cfs_faces : SET [1:?] OF face;

END_ENTITY;

ENTITY constructive_geometry_representation

SUBTYPE OF (representation);

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_CONTEXT' IN TYPEOF(SELF.context_of_items)) AND ({2 <= SELF.context_of_items\geometric_representation_context. coordinate_space_dimension <= 3});

WR2: SIZEOF( QUERY( cgr_i <* SELF.items | SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLACEMENT', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT'] * TYPEOF(cgr_i)) <> 1 )) = 0;

WR3: SIZEOF( USEDIN( SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION_RELATIONSHIP.REP_2') ) > 0;

WR4: SIZEOF( USEDIN( SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION_MAP.MAPPED_REPRESENTATION') ) = 0;

END_ENTITY;

ENTITY constructive_geometry_representation_relationship

SUBTYPE OF (representation_relationship);

WHERE

WR1: (SELF.rep_1.context_of_items :=: SELF.rep_2.context_of_items) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_CONTEXT' IN TYPEOF(SELF.rep_1.context_of_items));

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONSTRUCTIVE_GEOMETRY_REPRESENTATION' IN TYPEOF(SELF.rep_2);

WR3: SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONSTRUCTIVE_GEOMETRY_REPRESENTATION'] * TYPEOF(SELF.rep_1)) = 1;

WR4: NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION_RELATIONSHIP_WITH_TRANSFORMATION' IN TYPEOF(SELF));

END_ENTITY;

ENTITY context_dependent_invisibility

SUBTYPE OF (invisibility);

presentation_context : invisibility_context;

END_ENTITY;

ENTITY context_dependent_shape_representation;

representation_relation : shape_representation_relationship;

represented_product_relation : product_definition_shape;

DERIVE

description : text := get_description_value (SELF);

name : label := get_name_value (SELF);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION_RELATIONSHIP' IN TYPEOF (SELF.represented_product_relation.definition);

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

WR3: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

END_ENTITY;

ENTITY context_dependent_unit

SUBTYPE OF (named_unit);

name : label;

END_ENTITY;

ENTITY contract;

name : label;

purpose : text;

kind : contract_type;

END_ENTITY;

ENTITY contract_assignment

ABSTRACT SUPERTYPE;

assigned_contract : contract;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY contract_type;

description : label;

END_ENTITY;

ENTITY conversion_based_unit

SUBTYPE OF (named_unit);

name : label;

conversion_factor : measure_with_unit;

END_ENTITY;

ENTITY coordinated_universal_time_offset;

hour_offset : INTEGER;

minute_offset : OPTIONAL INTEGER;

sense : ahead_or_behind;

DERIVE

actual_minute_offset : INTEGER := NVL(minute_offset,0);

WHERE

WR1: { 0 <= hour_offset < 24 };

WR2: { 0 <= actual_minute_offset <= 59 };

WR3: NOT (((hour_offset <> 0) OR (actual_minute_offset <>0)) AND (sense = exact));

END_ENTITY;

ENTITY csg_shape_representation

SUBTYPE OF ( shape_representation );

WHERE

WR1 : SELF.context_of_items\geometric_representation_context.coordinate_space_dimension = 3;

WR2 :

SIZEOF (

QUERY ( it <* SELF.items| ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CSG_SOLID', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SOLID_REPLICA', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REVOLVED_FACE_SOLID', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EXTRUDED_FACE_SOLID' ] * TYPEOF (it)) <> 1) )) = 0;

WR3 :

SIZEOF (

QUERY ( mi <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CSG_SHAPE_REPRESENTATION' IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation)) )) = 0;

WR4 :

SIZEOF (

QUERY ( sr <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SOLID_REPLICA' IN TYPEOF (it)) )| ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CSG_SOLID', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REVOLVED_FACE_SOLID', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EXTRUDED_FACE_SOLID' ] * TYPEOF (sr\solid_replica.parent_solid)) = 0) )) = 0;

WR5 :

SIZEOF (

QUERY ( it <* SELF.items| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D' IN TYPEOF (it)) )) > 0;

END_ENTITY;

ENTITY csg_solid

SUBTYPE OF (solid_model);

tree_root_expression : csg_select;

END_ENTITY;

ENTITY curve

SUPERTYPE OF (ONEOF (

LINE,

CONIC,

PCURVE,

SURFACE_CURVE,

OFFSET_CURVE_2D,

OFFSET_CURVE_3D,

CURVE_REPLICA))

SUBTYPE OF (geometric_representation_item);

END_ENTITY;

ENTITY curve_bounded_surface

SUBTYPE OF (bounded_surface);

basis_surface    : surface;

boundaries       : SET [1:?] OF boundary_curve;

implicit_outer   : BOOLEAN;

WHERE

WR1: (NOT implicit_outer) OR

(SIZEOF (QUERY (temp <* boundaries |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OUTER_BOUNDARY_CURVE' IN TYPEOF(temp))) = 0);

WR2: (NOT(implicit_outer)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOUNDED_SURFACE' IN TYPEOF(basis_surface));

WR3: SIZEOF(QUERY(temp <* boundaries |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OUTER_BOUNDARY_CURVE' IN

TYPEOF(temp))) <= 1;

WR4: SIZEOF(QUERY(temp <* boundaries |

(temp\composite_curve_on_surface.basis_surface [1] <>

SELF.basis_surface))) = 0;

END_ENTITY;

ENTITY curve_dimension

SUBTYPE OF (dimension_curve_directed_callout);

END_ENTITY;

ENTITY curve_replica

SUBTYPE OF (curve);

parent_curve   : curve;

transformation : cartesian_transformation_operator;

WHERE

WR1: transformation.dim = parent_curve.dim;

WR2: acyclic_curve_replica (SELF, parent_curve);

END_ENTITY;

ENTITY curve_style;

name         : label;

curve_font   : curve_font_or_scaled_curve_font_select;

curve_width  : size_select;

curve_colour : colour;

END_ENTITY;

ENTITY curve_style_font;

name         : label;

pattern_list : LIST [1:?] OF curve_style_font_pattern;

END_ENTITY;

ENTITY curve_style_font_pattern;

visible_segment_length   : positive_length_measure;

invisible_segment_length : positive_length_measure;

END_ENTITY;

ENTITY cylindrical_surface

SUBTYPE OF (elementary_surface);

radius : positive_length_measure;

END_ENTITY;

ENTITY cylindricity_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY date

SUPERTYPE OF (ONEOF (

CALENDAR_DATE,

ORDINAL_DATE,

WEEK_OF_YEAR_AND_DAY_DATE));

year_component : year_number;

END_ENTITY;

ENTITY date_and_time;

date_component : date;

time_component : local_time;

END_ENTITY;

ENTITY date_and_time_assignment

ABSTRACT SUPERTYPE;

assigned_date_and_time : date_and_time;

role : date_time_role;

END_ENTITY;

ENTITY date_assignment

ABSTRACT SUPERTYPE;

assigned_date : date;

role : date_role;

END_ENTITY;

ENTITY date_role;

name : label;

DERIVE

description : text := get_description_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY date_time_role;

name : label;

DERIVE

description : text := get_description_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY dated_effectivity

SUBTYPE OF (effectivity);

effectivity_end_date : OPTIONAL date_time_or_event_occurrence;

effectivity_start_date : date_time_or_event_occurrence;

END_ENTITY;

ENTITY datum

SUBTYPE OF (shape_aspect);

identification               :identifier;

INVERSE

established_by_relationships : SET [1:?] OF shape_aspect_relationship

FOR related_shape_aspect;

WHERE

WR1: SIZEOF (QUERY (x<*SELF\datum.established_by_relationships |

SIZEOF (TYPEOF(x\shape_aspect_relationship.relating_shape_aspect)*

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM_FEATURE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM_TARGET']) <> 1))=0;

END_ENTITY;

ENTITY datum_feature

SUBTYPE OF (shape_aspect);

INVERSE

feature_basis_relationship : shape_aspect_relationship

FOR relating_shape_aspect;

WHERE

WR1: SIZEOF (QUERY (sar<* bag_to_set (USEDIN (SELF,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_ASPECT_RELATIONSHIP.'+

'RELATING_SHAPE_ASPECT'))

| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM' IN TYPEOF

(sar\shape_aspect_relationship.related_shape_aspect))))=0;

WR2: SELF\shape_aspect.product_definitional = TRUE;

END_ENTITY;

ENTITY datum_feature_callout

SUBTYPE OF (draughting_callout);

END_ENTITY;

ENTITY datum_reference;

precedence       : INTEGER;

referenced_datum : datum;

WHERE

WR1: precedence > 0;

END_ENTITY;

ENTITY datum_target

SUBTYPE OF (shape_aspect);

target_id             : identifier;

INVERSE

target_basis_relationship : shape_aspect_relationship FOR

relating_shape_aspect;

WHERE

WR1: SIZEOF (QUERY (sar<* bag_to_set (USEDIN (SELF,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_ASPECT_RELATIONSHIP.' +

'RELATING_SHAPE_ASPECT'))

| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM' IN TYPEOF

(sar\shape_aspect_relationship.related_shape_aspect))))=0;

WR2: SELF\shape_aspect.product_definitional = TRUE;

END_ENTITY;

ENTITY datum_target_callout

SUBTYPE OF (draughting_callout);

END_ENTITY;

ENTITY default_tolerance_table

SUBTYPE OF (representation);

WHERE

WR1: SIZEOF( QUERY( i <* SELF.items | NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEFAULT_TOLERANCE_TABLE_CELL' IN TYPEOF(i)) )) = 0;

WR2: (SIZEOF( QUERY( rr <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION_RELATIONSHIP.REP_1') | rr.name < 'general tolerance definition' )) = 0) AND (SIZEOF( QUERY( rr <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION_RELATIONSHIP.REP_1') | (rr.name = 'general tolerance definition') AND (rr.rep_2.name < 'default tolerance') )) = 0) AND (SIZEOF( USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION_RELATIONSHIP.REP_2') ) = 0);

END_ENTITY;

ENTITY default_tolerance_table_cell

SUBTYPE OF (compound_representation_item);

WHERE

WR1: SIZEOF(QUERY( x <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'REPRESENTATION.ITEMS') | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DEFAULT_TOLERANCE_TABLE' IN TYPEOF(x)))=1 ;

WR2: default_tolerance_table_cell_wr2(SELF\compound_representation_item.item_element);

WR3: default_tolerance_table_cell_wr3(SELF\compound_representation_item.item_element);

WR4: default_tolerance_table_cell_wr4(SELF\compound_representation_item.item_element);

WR5: default_tolerance_table_cell_wr5(SELF\compound_representation_item.item_element);

END_ENTITY;

ENTITY defined_character_glyph

SUBTYPE OF(geometric_representation_item);

definition : defined_glyph_select;

placement  : axis2_placement;

END_ENTITY;

ENTITY defined_symbol

SUBTYPE OF(geometric_representation_item);

definition : defined_symbol_select;

target     : symbol_target;

END_ENTITY;

ENTITY defined_table

SUBTYPE OF(defined_symbol);

END_ENTITY;

ENTITY definitional_representation

SUBTYPE OF (representation);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PARAMETRIC_REPRESENTATION_CONTEXT' IN

TYPEOF (SELF\representation.context_of_items );

END_ENTITY;

ENTITY degenerate_pcurve

SUBTYPE OF (point);

basis_surface:  surface;

reference_to_curve : definitional_representation;

WHERE

WR1: SIZEOF(reference_to_curve\representation.items) = 1;

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF

(reference_to_curve\representation.items[1]);

WR3: reference_to_curve\representation.

items[1]\geometric_representation_item.dim =2;

END_ENTITY;

ENTITY degenerate_toroidal_surface

SUBTYPE OF (toroidal_surface);

select_outer : BOOLEAN;

WHERE

WR1: major_radius <   minor_radius;

END_ENTITY;

ENTITY derived_shape_aspect

SUPERTYPE OF (ONEOF (

APEX,

CENTRE_OF_SYMMETRY,

GEOMETRIC_ALIGNMENT,

GEOMETRIC_INTERSECTION,

PARALLEL_OFFSET,

PERPENDICULAR_TO,

EXTENSION,

TANGENT))

SUBTYPE OF (shape_aspect);

INVERSE

deriving_relationships : SET [1:?] OF

shape_aspect_relationship FOR relating_shape_aspect;

WHERE

WR1: SIZEOF (QUERY (dr <*

SELF\derived_shape_aspect.deriving_relationships |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SHAPE_ASPECT_DERIVING_RELATIONSHIP'

IN TYPEOF (dr)))) = 0;

END_ENTITY;

ENTITY derived_unit;

elements : SET[1:?] OF derived_unit_element;

DERIVE

name : label := get_name_value (SELF);

WHERE

WR1: (SIZEOF (elements) > 1) OR ((SIZEOF (elements) = 1) AND (elements[1].exponent <> 1.0));

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

END_ENTITY;

ENTITY derived_unit_element;

unit : named_unit;

exponent : REAL;

END_ENTITY;

ENTITY description_attribute;

attribute_value : text;

described_item : description_attribute_select;

END_ENTITY;

ENTITY descriptive_representation_item

SUBTYPE OF (representation_item);

description : text;

END_ENTITY;

ENTITY design_context

SUBTYPE OF (product_definition_context);

WHERE

WR1: SELF.life_cycle_stage = 'design';

END_ENTITY;

ENTITY design_make_from_relationship

SUBTYPE OF (product_definition_relationship);

END_ENTITY;

ENTITY diameter_dimension

SUBTYPE OF (dimension_curve_directed_callout);

END_ENTITY;

ENTITY dimension_callout_component_relationship

SUBTYPE OF (draughting_callout_relationship);

WHERE

WR1: SELF.name IN ['prefix', 'suffix'];

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STRUCTURED_DIMENSION_CALLOUT'

IN TYPEOF (SELF.relating_draughting_callout);

WR3: SIZEOF (TYPEOF (SELF.related_draughting_callout) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIMENSION_CURVE_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STRUCTURED_DIMENSION_CALLOUT']) = 0;

WR4: SELF.related_draughting_callout.contents *

SELF.relating_draughting_callout.contents =

SELF.related_draughting_callout.contents;

WR5: ((SELF.name = 'prefix') AND

(SIZEOF (QUERY (ato <* QUERY (con <*

SELF.related_draughting_callout.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(con))) |

NOT (ato.name = 'prefix text')

)) = 0));

WR6: ((SELF.name = 'suffix') AND

(SIZEOF (QUERY (ato <* QUERY (con <*

SELF.related_draughting_callout.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(con))) |

NOT (ato.name = 'suffix text')

)) = 0));

END_ENTITY;

ENTITY dimension_callout_relationship

SUBTYPE OF (draughting_callout_relationship);

WHERE

WR1: SELF.name IN ['primary', 'secondary'];

WR2: SIZEOF (TYPEOF (SELF.relating_draughting_callout) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANGULAR_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIAMETER_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_DIRECTED_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINEAR_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORDINATE_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RADIUS_DIMENSION'])>=1;

WR3: SIZEOF (TYPEOF (SELF.related_draughting_callout) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIMENSION_CURVE_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_DIRECTED_CALLOUT']) = 0;

WR4: SELF.related_draughting_callout.contents *

SELF.relating_draughting_callout.contents =

SELF.related_draughting_callout.contents;

END_ENTITY;

ENTITY dimension_curve

SUBTYPE OF (annotation_curve_occurrence);

WHERE

wr1: (SIZEOF(

QUERY(dct <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'TERMINATOR_SYMBOL.ANNOTATED_CURVE')

| (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'DIMENSION_CURVE_TERMINATOR' IN TYPEOF(dct))

))

) <= 2);

wr2:  SIZEOF(

QUERY( dcdc <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT.CONTENTS') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'DIMENSION_CURVE_DIRECTED_CALLOUT' IN TYPEOF(dcdc)))

)>= 1;

wr3: (SIZEOF(

QUERY(dct1 <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'TERMINATOR_SYMBOL.ANNOTATED_CURVE')

| (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'DIMENSION_CURVE_TERMINATOR' IN TYPEOF(dct1))

AND (dct1.role = origin)))

) <= 1)

AND

(SIZEOF(

QUERY (dct2 <* USEDIN(SELF,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'TERMINATOR_SYMBOL.ANNOTATED_CURVE')

| (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'DIMENSION_CURVE_TERMINATOR' IN TYPEOF(dct2))

AND (dct2.role = target)))

) <= 1);

END_ENTITY;

ENTITY dimension_curve_directed_callout

SUBTYPE OF (draughting_callout);

WHERE

WR1: SIZEOF(QUERY(d_c<*SELF\draughting_callout.contents |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIMENSION_CURVE' IN (TYPEOF(d_c))))=1;

WR2: SIZEOF(SELF\draughting_callout.contents) >= 2;

END_ENTITY;

ENTITY dimension_curve_terminator

SUBTYPE OF (terminator_symbol);

role  : dimension_extent_usage;

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIMENSION_CURVE' IN TYPEOF

(SELF\terminator_symbol.annotated_curve);

END_ENTITY;

ENTITY dimension_pair

SUBTYPE OF (draughting_callout_relationship);

WHERE

WR1: SELF.name IN ['chained', 'parallel'];

WR2: SIZEOF (TYPEOF (SELF.relating_draughting_callout) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANGULAR_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIAMETER_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINEAR_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORDINATE_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RADIUS_DIMENSION'])=1;

WR3: SIZEOF (TYPEOF (SELF.related_draughting_callout) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANGULAR_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIAMETER_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINEAR_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORDINATE_DIMENSION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RADIUS_DIMENSION'])=1;

END_ENTITY;

ENTITY dimension_related_tolerance_zone_element;

related_dimension : dimensional_location;

related_element   : tolerance_zone_definition;

END_ENTITY;

ENTITY dimension_text_associativity

SUBTYPE OF (text_literal, mapped_item);

WHERE

WR1:  ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_DIMENSION_REPRESENTATION'

IN TYPEOF (SELF\mapped_item.

mapping_source.mapped_representation));

WR2:  ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT'

IN TYPEOF (SELF\mapped_item.mapping_target));

WR3:  SIZEOF (QUERY (ato <* QUERY (si <*

USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM.ITEM') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(si))) |

NOT (SIZEOF( QUERY (dc <*

USEDIN (ato, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT.CONTENTS') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT'

IN TYPEOF (dc)))

* [SELF\mapped_item.mapping_target]) = 1)

)) = 0;

END_ENTITY;

ENTITY dimensional_characteristic_representation;

dimension      : dimensional_characteristic;

representation : shape_dimension_representation;

END_ENTITY;

ENTITY dimensional_exponents;

length_exponent : REAL;

mass_exponent : REAL;

time_exponent : REAL;

electric_current_exponent : REAL;

thermodynamic_temperature_exponent : REAL;

amount_of_substance_exponent : REAL;

luminous_intensity_exponent : REAL;

END_ENTITY;

ENTITY dimensional_location

SUPERTYPE OF (ONEOF (

ANGULAR_LOCATION,

DIMENSIONAL_LOCATION_WITH_PATH))

SUBTYPE OF (shape_aspect_relationship);

END_ENTITY;

ENTITY dimensional_location_with_path

SUBTYPE OF (dimensional_location);

path : shape_aspect;

END_ENTITY;

ENTITY dimensional_size

SUPERTYPE OF (ONEOF (

ANGULAR_SIZE,

DIMENSIONAL_SIZE_WITH_PATH));

applies_to : shape_aspect;

name       : label;

WHERE

WR1: applies_to.product_definitional = TRUE;

END_ENTITY;

ENTITY dimensional_size_with_path

SUBTYPE OF (dimensional_size);

path : shape_aspect;

END_ENTITY;

ENTITY directed_action

SUBTYPE OF (executed_action);

directive : action_directive;

END_ENTITY;

ENTITY directed_dimensional_location

SUBTYPE OF (dimensional_location);

END_ENTITY;

ENTITY direction

SUBTYPE OF (geometric_representation_item);

direction_ratios : LIST [2:3] OF REAL;

WHERE

WR1: SIZEOF(QUERY(tmp <* direction_ratios | tmp <> 0.0)) > 0;

END_ENTITY;

ENTITY document;

id : identifier;

name : label;

description : OPTIONAL text;

kind : document_type;

INVERSE

representation_types : SET[0:?] OF document_representation_type FOR represented_document;

END_ENTITY;

ENTITY document_file

SUBTYPE OF (document, characterized_object);

WHERE

WR1: SELF\characterized_object.name = '';

WR2: NOT EXISTS(SELF\characterized_object.description);

WR3: SIZEOF( QUERY( drt <* SELF\document.representation_types |

drt.name IN ['digital','physical'])) = 1;

END_ENTITY;

ENTITY document_product_association;

name : label;

description : OPTIONAL text;

relating_document : document;

related_product : product_or_formation_or_definition;

END_ENTITY;

ENTITY document_product_equivalence

SUBTYPE OF (document_product_association);

WHERE

WR1: SELF\document_product_association.name = 'equivalence';

WR2: NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT' IN TYPEOF(SELF\document_product_association.related_product)) OR ((SELF\document_product_association.relating_document.kind. product_data_type = 'configuration controlled document') AND (SIZEOF( QUERY( prpc <* USEDIN(SELF\document_product_association.related_product,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'PRODUCT_RELATED_PRODUCT_CATEGORY.PRODUCTS') | prpc.name = 'document' )) = 1));

WR3: NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION_FORMATION' IN TYPEOF(SELF.related_product)) OR ((SELF\document_product_association.relating_document.kind.product_data_type = 'configuration controlled document version') AND (SIZEOF( QUERY( prpc <* USEDIN(SELF.related_product\product_definition_formation.of_product, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_RELATED_PRODUCT_CATEGORY.PRODUCTS') | prpc.name = 'document')) = 1));

WR4: NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION' IN TYPEOF(SELF.related_product)) OR ((SELF\document_product_association.relating_document.kind.product_data_type = 'configuration controlled document definition') AND (SIZEOF( QUERY( prpc <* USEDIN(SELF\document_product_association.related_product\product_definition.formation.of_product, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_RELATED_PRODUCT_CATEGORY.PRODUCTS') | prpc.name = 'document' )) = 1));

END_ENTITY;

ENTITY document_reference

ABSTRACT SUPERTYPE;

assigned_document : document;

source : label;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY document_relationship;

name : label;

description : OPTIONAL text;

relating_document : document;

related_document : document;

END_ENTITY;

ENTITY document_representation_type;

name : label;

represented_document : document;

END_ENTITY;

ENTITY document_type;

product_data_type : label;

END_ENTITY;

ENTITY document_usage_constraint;

source : document;

subject_element : label;

subject_element_value : text;

END_ENTITY;

ENTITY document_usage_constraint_assignment

ABSTRACT SUPERTYPE;

assigned_document_usage : document_usage_constraint;

role : document_usage_role;

END_ENTITY;

ENTITY document_usage_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY document_with_class

SUBTYPE OF (document);

class : identifier;

END_ENTITY;

ENTITY draughting_annotation_occurrence

SUBTYPE OF (annotation_occurrence);

WHERE

WR1:	-- curve_has_curve_style:

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_CURVE_OCCURRENCE'

IN TYPEOF (SELF))) OR

(SIZEOF (QUERY (sty <* SELF.styles |

NOT ((SIZEOF (sty.styles) = 1)

AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF (sty.styles[1]))) )) = 0);

WR2:	-- fill_area_has_fill_style:

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_FILL_AREA_OCCURRENCE'

IN TYPEOF (SELF))) OR    (SIZEOF (QUERY (sty <* SELF.styles |

NOT ((SIZEOF (sty.styles) = 1)

AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FILL_AREA_STYLE'

IN TYPEOF (sty.styles[1]))) )) = 0);

WR3:	-- styled_fill_boundaries:

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_FILL_AREA_OCCURRENCE'

IN TYPEOF (SELF))) OR    (SIZEOF (QUERY (bound <*

SELF.item\annotation_fill_area.boundaries |

NOT (SIZEOF (QUERY (si <*

USEDIN (bound, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'STYLED_ITEM.ITEM') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'ANNOTATION_CURVE_OCCURRENCE' IN TYPEOF (si)))) > 0))) = 0);

WR4:	-- symbol_has_symbol_style:

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL_OCCURRENCE'

IN TYPEOF (SELF))) OR    (SIZEOF (QUERY (sty <* SELF.styles |

NOT ((SIZEOF (sty.styles) = 1)           AND

(SIZEOF (TYPEOF (sty.styles[1]) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_STYLE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.NULL_STYLE']) = 1)) )) = 0);

WR5:	-- allowable_symbol_representations:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL_OCCURRENCE'

IN TYPEOF (SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL'

IN TYPEOF(SELF.item)))) OR

(SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_SYMBOL_REPRESENTATION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_SUBFIGURE_REPRESENTATION'] *

TYPEOF (SELF.item\mapped_item.mapping_source.

mapped_representation)) = 1);

WR6:	-- text_has_text_style:

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF))) OR

(SIZEOF (QUERY (sty <* SELF.styles |

NOT ((SIZEOF (sty.styles) = 1)

AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_STYLE'

IN TYPEOF (sty.styles[1]))) )) = 0);

WR7:	-- allowable_text:

(('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF))) OR

(SIZEOF (TYPEOF(SELF.item) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL']) = 1);

WR8:	-- text_not_nested:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'

IN TYPEOF (SELF.item)))) OR    (SIZEOF (QUERY (tl <*

SELF.item\composite_text.collected_text |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL'

IN TYPEOF (tl)) )) = 0);

WR9:	-- text_alignment_literals:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL'

IN TYPEOF (SELF.item)))) OR (SELF.item\text_literal.alignment

IN ['baseline left', 'baseline centre', 'baseline right']);

WR10:	-- text_alignment_composites:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'

IN TYPEOF (SELF.item)))) OR

(SIZEOF (QUERY (tl <* QUERY (text <* SELF.

item\composite_text.collected_text

|('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL' IN TYPEOF(text))) |

NOT (tl\text_literal.alignment IN

['baseline left', 'baseline centre', 'baseline right']) )) = 0);

WR11:	-- single_text_alignment:

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'

IN TYPEOF (SELF.item))) OR check_text_alignment(SELF.item);

WR12:	-- single_text_font:

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'

IN TYPEOF (SELF.item))) OR check_text_font(SELF.item);

WR13:	-- allowable_text_literals:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'

IN TYPEOF (SELF.item)))) OR

(SIZEOF (QUERY (tl <* QUERY (text <*

SELF.item\composite_text.collected_text |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL' IN TYPEOF (text))) |

NOT (SIZEOF (TYPEOF(tl) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'TEXT_LITERAL_WITH_BLANKING_BOX',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'TEXT_LITERAL_WITH_ASSOCIATED_CURVES']) = 0) )) = 0);

WR14:	-- styled_text_literal_curves:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL_WITH_ASSOCIATED_CURVES'

IN TYPEOF (SELF.item)))) OR

(SIZEOF (QUERY (crv <*

SELF.item\text_literal_with_associated_curves.

associated_curves |

NOT (SIZEOF (QUERY (si <*  USEDIN (crv,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM.ITEM') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_CURVE_OCCURRENCE'

IN TYPEOF (si)) )) > 0) )) = 0);

WR15:	-- styled_composite_text_curves:

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT_WITH_ASSOCIATED_CURVES'

IN TYPEOF (SELF.item)))) OR

(SIZEOF (QUERY (crv <*

SELF.item\composite_text_with_associated_curves.

associated_curves |

NOT (SIZEOF (QUERY (si <*  USEDIN (crv,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM.ITEM') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_CURVE_OCCURRENCE'

IN TYPEOF (si)) )) > 0) )) = 0);

WR16:	-- curve_style_has_width:

SIZEOF (QUERY (cs <* QUERY (sty <* SELF.styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE' IN TYPEOF (sty.styles[1])))

| NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_MEASURE_WITH_UNIT'

IN TYPEOF (cs.styles[1]\curve_style.curve_width)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POSITIVE_LENGTH_MEASURE'

IN TYPEOF (cs.styles[1]\curve_style.

curve_width\measure_with_unit.value_component))))) = 0;

WR17:	-- tiling_constraints:

SIZEOF (QUERY (fas <* QUERY (sty <* SELF.styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FILL_AREA_STYLE'

IN TYPEOF (sty.styles[1]))) |

NOT ((SIZEOF (QUERY (fs <* fas.styles[1]\fill_area_style.fill_styles

| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FILL_AREA_STYLE_TILES'

IN TYPEOF (fs)))) <= 1)

AND (SIZEOF (QUERY (fst <* QUERY (fs <*

fas.styles[1]\fill_area_style.fill_styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FILL_AREA_STYLE_TILES'

IN TYPEOF (fs))) |

NOT (SIZEOF (fst\fill_area_style_tiles.tiles) = 1)

)) = 0))

)) = 0;

WR18:	-- hatching_constraints:

SIZEOF (QUERY (fas <* QUERY (sty <* SELF.styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FILL_AREA_STYLE'

IN TYPEOF (sty.styles[1]))) |

NOT (SIZEOF (QUERY (fsh <* QUERY (fs <*

fas.styles[1]\fill_area_style.fill_styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FILL_AREA_STYLE_HATCHING'

IN TYPEOF (fs))) |

NOT (fsh\fill_area_style_hatching.point_of_reference_hatch_line :=:

fsh\fill_area_style_hatching.pattern_start)  )) = 0)  )) = 0;

WR19:	-- text_style_constraint:

SIZEOF (QUERY (ts <* QUERY (sty <* SELF.styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_STYLE'

IN TYPEOF(sty.styles[1]))) |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'TEXT_STYLE_WITH_BOX_CHARACTERISTICS'

IN TYPEOF (ts.styles[1])))) = 0;

WR20:	-- text_style_characteristics:

SIZEOF (QUERY (ts <* QUERY (sty <* SELF.styles |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_STYLE_WITH_BOX_CHARACTERISTICS'

IN TYPEOF (sty.styles[1]))) |

NOT (SIZEOF (ts.styles[1]\text_style_with_box_characteristics.

characteristics) = 4) )) = 0;

END_ENTITY;

ENTITY draughting_callout

SUBTYPE OF (geometric_representation_item);

contents : SET [1:?] OF draughting_callout_element;

END_ENTITY;

ENTITY draughting_callout_relationship;

name : label;

description : text;

relating_draughting_callout : draughting_callout;

related_draughting_callout : draughting_callout;

END_ENTITY;

ENTITY draughting_elements

SUBTYPE OF (draughting_callout);

WHERE

WR1: SIZEOF (QUERY (l_c <* QUERY (con <* SELF.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_CURVE' IN TYPEOF(con))) |

NOT (SIZEOF (QUERY (ldc <* USEDIN (l_c,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DRAUGHTING_CALLOUT.CONTENTS') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_DIRECTED_CALLOUT'

IN TYPEOF (ldc)))) <= 1)))=0;

WR2: NOT    ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIMENSION_CURVE_DIRECTED_CALLOUT'

IN TYPEOF(SELF)) OR

(SIZEOF (QUERY (con <* SELF.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_CURVE' IN

TYPEOF (con)))) <= 2);

WR3: SIZEOF (QUERY (rc <* USEDIN (SELF,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT_' +

'RELATIONSHIP.RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_RELATIONSHIP' IN TYPEOF (rc)) AND

(rc.name = 'primary') )) <= 1;

WR4: SIZEOF (QUERY (rc <* USEDIN (SELF,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT_' +

'RELATIONSHIP.RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_RELATIONSHIP' IN TYPEOF (rc)) AND

(rc.name = 'secondary') )) <= 1;

WR5: SIZEOF (QUERY (sec <* QUERY (rc <* USEDIN (SELF,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT_' +

'RELATIONSHIP.RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_RELATIONSHIP' IN TYPEOF (rc)) AND

(rc.name = 'secondary') ) |

NOT (SIZEOF (QUERY (prim <* USEDIN (SELF,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT_' +

'RELATIONSHIP.RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_RELATIONSHIP' IN TYPEOF (prim)) AND

(prim.name = 'primary') )) = 1))) = 0;

END_ENTITY;

ENTITY draughting_model

SUBTYPE OF (representation);

UNIQUE

UR1:  SELF\representation.name;

WHERE

WR1:  SIZEOF (QUERY (it <* SELF.items |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CAMERA_MODEL'] *

TYPEOF (it)) = 1

))) = 0;

WR2:  SIZEOF (QUERY (mi <* QUERY (it <* SELF.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF(it))) |

NOT (

SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_MODEL'] *

TYPEOF (mi\mapped_item.mapping_source.

mapped_representation)) = 1

))) = 0;

WR3:  SIZEOF (QUERY (smi <* QUERY (si <* QUERY (it <* SELF.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM' IN TYPEOF(it))) |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN

TYPEOF(si\styled_item.item))) |

(NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION' IN

TYPEOF(smi\styled_item.item\mapped_item.

mapping_source.mapped_representation))

AND

(SIZEOF (QUERY (sty <* smi\styled_item.styles |

(NOT (SIZEOF (QUERY (psa <* sty.styles |

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF(psa))))) = 1

)))) = 1)))

)) = 0;

END_ENTITY;

ENTITY draughting_pre_defined_colour

SUBTYPE OF (pre_defined_colour);

WHERE

WR1: SELF.name IN

['red',

'green',

'blue',

'yellow',

'magenta',

'cyan',

'black',

'white'];

END_ENTITY;

ENTITY draughting_pre_defined_curve_font

SUBTYPE OF (pre_defined_curve_font);

WHERE

WR1: SELF.name IN

['continuous',

'chain',

'chain double dash',

'dashed',

'dotted'];

END_ENTITY;

ENTITY draughting_subfigure_representation

SUBTYPE OF (symbol_representation);

WHERE

WR1: SIZEOF (QUERY (item <* SELF\representation.items |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT']

* TYPEOF (item)) = 1))) = 0;

WR2: SIZEOF (QUERY (item <* SELF\representation.items |

SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_CALLOUT'] *

TYPEOF (item)) = 1)) >= 1;

WR3: SIZEOF (QUERY (srm <* QUERY (rm <*

USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'REPRESENTATION_MAP.MAPPED_REPRESENTATION') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_REPRESENTATION_MAP'

IN TYPEOF(rm))) |

NOT (SIZEOF (QUERY (a_s <* QUERY (mi <* srm.map_usage |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL' IN TYPEOF(mi)))

| NOT (SIZEOF (QUERY (aso <*

USEDIN (a_s, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'STYLED_ITEM.ITEM') |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SUBFIGURE_OCCURRENCE'

IN TYPEOF(aso)))) = 0))) = 0))) > 0;

WR4: NOT (acyclic_mapped_item_usage (SELF));

WR5: SIZEOF (SELF.context_of_items.representations_in_context) = 1;

END_ENTITY;

ENTITY draughting_symbol_representation

SUBTYPE of (symbol_representation);

UNIQUE

UR1: SELF\representation.name;

WHERE

WR1:

SIZEOF (QUERY (item <* SELF\representation.items |

NOT (SIZEOF (TYPEOF (item) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_CURVE_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_FILL_AREA_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT']) = 1)

)) = 0;

WR2:

SIZEOF (QUERY (item <* SELF\representation.items |

(SIZEOF (TYPEOF (item) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_CURVE_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_FILL_AREA_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE']) = 1)

)) >= 1;

WR3:

SIZEOF (QUERY (item <* SELF\representation.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SUBFIGURE_OCCURRENCE'

IN TYPEOF (item))) = 0;

WR4:

SIZEOF (QUERY (srm <* QUERY (rm <*

USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'REPRESENTATION_MAP.MAPPED_REPRESENTATION') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_REPRESENTATION_MAP'

IN TYPEOF(rm))) |

NOT (SIZEOF (QUERY (a_s <* QUERY (mi <* srm.map_usage |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL' IN TYPEOF(mi))) |

NOT (SIZEOF (QUERY(aso <*

USEDIN(a_s, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'STYLED_ITEM.ITEM') |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_SYMBOL_OCCURRENCE'

IN TYPEOF(aso))

)) = 0) )) = 0) )) > 0;

WR5:

NOT (acyclic_mapped_item_usage (SELF));

WR6:

SIZEOF (SELF.context_of_items.representations_in_context) = 1;

END_ENTITY;

ENTITY draughting_text_literal_with_delineation

SUBTYPE OF (text_literal_with_delineation);

WHERE

WR1: SELF.delineation IN ['underline', 'overline'];

END_ENTITY;

ENTITY edge

SUPERTYPE OF (ONEOF (

EDGE_CURVE,

ORIENTED_EDGE))

SUBTYPE OF (topological_representation_item);

edge_start : vertex;

edge_end   : vertex;

END_ENTITY;

ENTITY edge_based_wireframe_model

SUBTYPE OF (geometric_representation_item);

ebwm_boundary  : SET [1:?] OF connected_edge_set;

END_ENTITY;

ENTITY edge_based_wireframe_shape_representation

SUBTYPE OF ( shape_representation );

WHERE

WR1 :

SIZEOF (

QUERY ( it <* SELF.items| NOT ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D' ] * TYPEOF (it)) = 1) )) = 0;

WR2 :

SIZEOF (

QUERY ( it <* SELF.items| ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' ] * TYPEOF (it)) = 1) )) >= 1;

WR3 :

SIZEOF (

QUERY ( ebwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( eb <* ebwm\edge_based_wireframe_model.ebwm_boundary| NOT ( SIZEOF (

QUERY ( edges <* eb.ces_edges| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_CURVE' IN TYPEOF (edges)) )) = 0) )) = 0) )) = 0;

WR4 :

SIZEOF (

QUERY ( ebwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( eb <* ebwm\edge_based_wireframe_model.ebwm_boundary| NOT ( SIZEOF (

QUERY ( pline_edges <*

QUERY ( edges <* eb.ces_edges| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF (edges\edge_curve.edge_geometry)) )| NOT ( SIZEOF (pline_edges\edge_curve.edge_geometry\polyline.points) > 2) )) = 0) )) = 0) )) = 0;

WR5 :

SIZEOF (

QUERY ( ebwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( eb <* ebwm\edge_based_wireframe_model.ebwm_boundary| NOT ( SIZEOF (

QUERY ( edges <* eb.ces_edges| NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (edges.edge_start)) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (edges.edge_end))) )) = 0) )) = 0) )) = 0;

WR6 :

SIZEOF (

QUERY ( ebwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( eb <* ebwm\edge_based_wireframe_model.ebwm_boundary| NOT ( SIZEOF (

QUERY ( edges <* eb.ces_edges| NOT valid_wireframe_edge_curve(edges\edge_curve.edge_geometry) )) = 0) )) = 0) )) = 0;

WR7 :

SIZEOF (

QUERY ( ebwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( eb <* ebwm\edge_based_wireframe_model.ebwm_boundary| NOT ( SIZEOF (

QUERY ( edges <* eb.ces_edges| NOT (valid_wireframe_vertex_point(edges.edge_start\vertex_point.vertex_geometry) AND valid_wireframe_vertex_point(edges.edge_end\vertex_point.vertex_geometry)) )) = 0) )) = 0) )) = 0;

WR8 :

SIZEOF (

QUERY ( mi <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'EDGE_BASED_WIREFRAME_SHAPE_REPRESENTATION' IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation)) )) = 0;

WR9 : SELF.context_of_items\geometric_representation_context.coordinate_space_dimension = 3;

END_ENTITY;

ENTITY edge_curve

SUBTYPE OF(edge,geometric_representation_item);

edge_geometry : curve;

same_sense    : BOOLEAN;

END_ENTITY;

ENTITY edge_loop

SUBTYPE OF (loop,path);

DERIVE

ne : INTEGER := SIZEOF(SELF\path.edge_list);

WHERE

WR1: (SELF\path.edge_list[1].edge_start) :=:

(SELF\path.edge_list[ne].edge_end);

END_ENTITY;

ENTITY effectivity

SUPERTYPE OF (ONEOF (

SERIAL_NUMBERED_EFFECTIVITY,

DATED_EFFECTIVITY,

LOT_EFFECTIVITY,

TIME_INTERVAL_BASED_EFFECTIVITY));

id : identifier;

DERIVE

name : label := get_name_value(SELF);

description : text := get_description_value(SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

WR2: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY effectivity_assignment

ABSTRACT SUPERTYPE;

assigned_effectivity : effectivity;

DERIVE

role : object_role := get_role(SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY effectivity_relationship;

name : label;

description : OPTIONAL text;

related_effectivity : effectivity;

relating_effectivity : effectivity;

END_ENTITY;

ENTITY electric_current_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELECTRIC_CURRENT_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY electric_current_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 1.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY elementary_surface

SUPERTYPE OF (ONEOF (

PLANE,

CYLINDRICAL_SURFACE,

CONICAL_SURFACE,

SPHERICAL_SURFACE,

TOROIDAL_SURFACE))

SUBTYPE OF (surface);

position : axis2_placement_3d;

END_ENTITY;

ENTITY ellipse

SUBTYPE OF (conic);

semi_axis_1 : positive_length_measure;

semi_axis_2 : positive_length_measure;

END_ENTITY;

ENTITY evaluated_degenerate_pcurve

SUBTYPE OF (degenerate_pcurve);

equivalent_point : cartesian_point;

END_ENTITY;

ENTITY event_occurrence;

id : identifier;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY event_occurrence_assignment

ABSTRACT SUPERTYPE;

assigned_event_occurrence : event_occurrence;

role : event_occurrence_role;

END_ENTITY;

ENTITY event_occurrence_relationship;

name : label;

description : OPTIONAL text;

relating_event : event_occurrence;

related_event : event_occurrence;

END_ENTITY;

ENTITY event_occurrence_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY executed_action

SUBTYPE OF (action);

END_ENTITY;

ENTITY extension

SUBTYPE OF (derived_shape_aspect);

WHERE

WR1: SIZEOF (SELF\derived_shape_aspect.deriving_relationships)= 1;

END_ENTITY;

ENTITY external_class_library

SUBTYPE OF (external_source);

END_ENTITY;

ENTITY external_identification_assignment

ABSTRACT SUPERTYPE

SUBTYPE OF (identification_assignment);

source : external_source;

END_ENTITY;

ENTITY external_source;

source_id : source_item;

DERIVE

description : text := get_description_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY externally_defined_character_glyph

SUBTYPE OF (externally_defined_item);

END_ENTITY;

ENTITY externally_defined_class

SUBTYPE OF (class, externally_defined_item);

END_ENTITY;

ENTITY externally_defined_colour

SUBTYPE OF (colour_specification,externally_defined_item);

END_ENTITY;

ENTITY externally_defined_curve_font

SUBTYPE OF (externally_defined_item);

END_ENTITY;

ENTITY externally_defined_dimension_definition

SUBTYPE OF (dimensional_size, externally_defined_item);

WHERE

WR1: (SELF\externally_defined_item.item_id = 'external size dimension') AND (SELF\externally_defined_item.source.source_id = 'external size dimension specification');

WR2: 1 >= SIZEOF(QUERY ( adr <* USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.APPLIED_DOCUMENT_REFERENCE.ITEMS')| (adr.assigned_document.description = 'external size dimension specification') ));

END_ENTITY;

ENTITY externally_defined_hatch_style

SUBTYPE OF (externally_defined_item, geometric_representation_item);

END_ENTITY;

ENTITY externally_defined_item;

item_id : source_item;

source : external_source;

END_ENTITY;

ENTITY externally_defined_marker

SUBTYPE OF (externally_defined_symbol, pre_defined_marker);

END_ENTITY;

ENTITY externally_defined_symbol

SUBTYPE OF (externally_defined_item);

END_ENTITY;

ENTITY externally_defined_terminator_symbol

SUBTYPE OF (externally_defined_symbol);

END_ENTITY;

ENTITY externally_defined_text_font

SUBTYPE OF (externally_defined_item);

END_ENTITY;

ENTITY externally_defined_tile

SUBTYPE OF (externally_defined_item);

END_ENTITY;

ENTITY externally_defined_tile_style

SUBTYPE OF (externally_defined_item, geometric_representation_item);

END_ENTITY;

ENTITY extruded_face_solid

SUBTYPE OF (swept_face_solid);

extruded_direction : direction;

depth              : positive_length_measure;

WHERE

WR1: dot_product(

(SELF\swept_face_solid.swept_face.face_geometry\

elementary_surface.position.p[3]), extruded_direction) <> 0.0;

END_ENTITY;

ENTITY face

SUPERTYPE OF (ONEOF (

FACE_SURFACE,

ORIENTED_FACE))

SUBTYPE OF (topological_representation_item);

bounds : SET[1:?] OF face_bound;

WHERE

WR1: NOT (mixed_loop_type_set(list_to_set(list_face_loops(SELF))));

WR2: SIZEOF(QUERY(temp <* bounds | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_OUTER_BOUND' IN

TYPEOF(temp))) <= 1;

END_ENTITY;

ENTITY face_bound

SUBTYPE OF(topological_representation_item);

bound       :  loop;

orientation :  BOOLEAN;

END_ENTITY;

ENTITY face_outer_bound

SUBTYPE OF (face_bound);

END_ENTITY;

ENTITY face_surface

SUBTYPE OF(face,geometric_representation_item);

face_geometry :  surface;

same_sense    :  BOOLEAN;

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_SURFACE' IN TYPEOF(face_geometry));

END_ENTITY;

ENTITY faceted_brep

SUBTYPE OF (manifold_solid_brep);

END_ENTITY;

ENTITY faceted_brep_shape_representation

SUBTYPE OF ( shape_representation );

WHERE

WR1 :

SIZEOF (

QUERY ( it <* items| NOT ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACETED_BREP', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D' ] * TYPEOF (it)) = 1) )) = 0;

WR2 :

SIZEOF (

QUERY ( it <* items| ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACETED_BREP', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' ] * TYPEOF (it)) = 1) )) > 0;

WR3 :

SIZEOF (

QUERY ( fbrep <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACETED_BREP' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( csh <* msb_shells(fbrep)| NOT ( SIZEOF (

QUERY ( fcs <* csh\connected_face_set.cfs_faces| NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_SURFACE' IN TYPEOF (fcs)) AND (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLANE' IN TYPEOF (fcs\face_surface.face_geometry)) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF (fcs\face_surface.face_geometry\elementary_surface.position.location)))) )) = 0) )) = 0) )) = 0;

WR4 :

SIZEOF (

QUERY ( fbrep <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACETED_BREP' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( csh <* msb_shells(fbrep)| NOT ( SIZEOF (

QUERY ( fcs <* csh\connected_face_set.cfs_faces| NOT ( SIZEOF (

QUERY ( bnds <* fcs.bounds| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_OUTER_BOUND' IN TYPEOF (bnds)) )) = 1) )) = 0) )) = 0) )) = 0;

WR5 :

SIZEOF (

QUERY ( msb <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MANIFOLD_SOLID_BREP' IN TYPEOF (it)) )| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_CLOSED_SHELL' IN TYPEOF (msb\manifold_solid_brep.outer)) )) = 0;

WR6 :

SIZEOF (

QUERY ( brv <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BREP_WITH_VOIDS' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( csh <* brv\brep_with_voids.voids| csh\oriented_closed_shell.orientation )) = 0) )) = 0;

WR7 :

SIZEOF (

QUERY ( mi <*

QUERY ( it <* items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACETED_BREP_SHAPE_REPRESENTATION' IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation)) )) = 0;

END_ENTITY;

ENTITY fill_area_style;

name       : label;

fill_styles : SET [1:?] OF fill_style_select;

WHERE

WR1: SIZEOF(QUERY(fill_style <* SELF.fill_styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'FILL_AREA_STYLE_COLOUR' IN

TYPEOF(fill_style)

)) <= 1;

END_ENTITY;

ENTITY fill_area_style_colour;

name        : label;

fill_colour : colour;

END_ENTITY;

ENTITY fill_area_style_hatching

SUBTYPE OF (geometric_representation_item);

hatch_line_appearance         : curve_style;

start_of_next_hatch_line      : one_direction_repeat_factor;

point_of_reference_hatch_line : cartesian_point;

pattern_start                 : cartesian_point;

hatch_line_angle              : plane_angle_measure;

END_ENTITY;

ENTITY fill_area_style_tile_coloured_region

SUBTYPE OF (geometric_representation_item);

closed_curve  : curve_or_annotation_curve_occurrence;

region_colour : colour;

END_ENTITY;

ENTITY fill_area_style_tile_curve_with_style

SUBTYPE OF (geometric_representation_item);

styled_curve : annotation_curve_occurrence;

END_ENTITY;

ENTITY fill_area_style_tile_symbol_with_style

SUBTYPE OF (geometric_representation_item);

symbol : annotation_symbol_occurrence;

END_ENTITY;

ENTITY fill_area_style_tiles

SUBTYPE OF (geometric_representation_item);

tiling_pattern : two_direction_repeat_factor;

tiles          : SET [1:?] OF fill_area_style_tile_shape_select;

tiling_scale   : positive_ratio_measure;

END_ENTITY;

ENTITY flatness_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY founded_item;

END_ENTITY;

ENTITY functionally_defined_transformation;

name        : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY general_property;

id : identifier;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY general_property_association;

name : label;

description : OPTIONAL text;

base_definition : general_property;

derived_definition : derived_property_select;

WHERE

WR1: SIZEOF( USEDIN( derived_definition, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GENERAL_PROPERTY_ASSOCIATION.' + 'DERIVED_DEFINITION')) = 1;

WR2: derived_definition.name = base_definition.name;

END_ENTITY;

ENTITY general_property_relationship;

name : label;

description : OPTIONAL text;

relating_property : general_property;

related_property : general_property;

END_ENTITY;

ENTITY geometric_alignment

SUBTYPE OF (derived_shape_aspect);

WHERE

WR1: SIZEOF (SELF\derived_shape_aspect.deriving_relationships)> 1;

END_ENTITY;

ENTITY geometric_curve_set

SUBTYPE OF (geometric_set);

WHERE

WR1: SIZEOF(QUERY(temp <* SELF\geometric_set.elements |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE' IN TYPEOF(temp))) = 0;

END_ENTITY;

ENTITY geometric_intersection

SUBTYPE OF (derived_shape_aspect);

WHERE

WR1: SIZEOF (SELF\derived_shape_aspect.deriving_relationships)> 1;

END_ENTITY;

ENTITY geometric_representation_context

SUBTYPE OF (representation_context);

coordinate_space_dimension : dimension_count;

END_ENTITY;

ENTITY geometric_representation_item

SUPERTYPE OF (ONEOF (

POINT,

DIRECTION,

VECTOR,

PLACEMENT,

CARTESIAN_TRANSFORMATION_OPERATOR,

CURVE,

SURFACE,

EDGE_CURVE,

FACE_SURFACE,

POLY_LOOP,

VERTEX_POINT,

SOLID_MODEL,

BOOLEAN_RESULT,

SPHERE,

RIGHT_CIRCULAR_CONE,

RIGHT_CIRCULAR_CYLINDER,

TORUS,

BLOCK,

RIGHT_ANGULAR_WEDGE,

HALF_SPACE_SOLID,

SHELL_BASED_SURFACE_MODEL,

SHELL_BASED_WIREFRAME_MODEL,

EDGE_BASED_WIREFRAME_MODEL,

GEOMETRIC_SET))

SUBTYPE OF (representation_item);

DERIVE

dim : dimension_count := dimension_of(SELF);

WHERE

WR1: SIZEOF (QUERY (using_rep <* using_representations (SELF) |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_CONTEXT' IN

TYPEOF (using_rep.context_of_items)))) = 0;

END_ENTITY;

ENTITY geometric_set

SUBTYPE OF (geometric_representation_item);

elements :  SET [1:?] OF geometric_set_select;

END_ENTITY;

ENTITY geometric_tolerance;

name                    : label;

description             : text;

magnitude               : measure_with_unit;

toleranced_shape_aspect : shape_aspect;

WHERE

WR1: ('NUMBER' IN TYPEOF

(magnitude\measure_with_unit.value_component)) AND

(magnitude\measure_with_unit.value_component >= 0.0);

END_ENTITY;

ENTITY geometric_tolerance_relationship;

name                         :label;

description                  :text;

relating_geometric_tolerance : geometric_tolerance;

related_geometric_tolerance  : geometric_tolerance;

END_ENTITY;

ENTITY geometric_tolerance_with_datum_reference

SUBTYPE OF (geometric_tolerance);

datum_system : SET [1:?] OF  datum_reference;

END_ENTITY;

ENTITY geometric_tolerance_with_defined_unit

SUBTYPE OF (geometric_tolerance);

unit_size : measure_with_unit;

WHERE

WR1: ('NUMBER' IN TYPEOF

(unit_size\measure_with_unit.value_component)) AND

(unit_size\measure_with_unit.value_component > 0.0);

END_ENTITY;

ENTITY geometrical_tolerance_callout

SUBTYPE OF (draughting_callout);

END_ENTITY;

ENTITY geometrically_bounded_surface_shape_representation

SUBTYPE OF (shape_representation);

WHERE

WR1: SIZEOF(QUERY(it <* SELF.items | NOT (SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D'] * TYPEOF(it)) = 1))) = 0;

WR2: SIZEOF(QUERY(it <* SELF.items | SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'] * TYPEOF(it)) = 1)) > 0;

WR3: SIZEOF(QUERY(mi <* QUERY(it <* SELF.items | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF(it)) | NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRICALLY_BOUNDED_SURFACE_SHAPE_REPRESENTATION' IN TYPEOF(mi\mapped_item.mapping_source.mapped_representation)) AND (SIZEOF(QUERY(mr_it <* mi\mapped_item.mapping_source.mapped_representation.items | ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET' IN TYPEOF(mr_it)))) > 0)))) = 0;

WR4: SIZEOF(QUERY(gs <* QUERY(it <* SELF.items | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET' IN TYPEOF(it)) | NOT (SIZEOF(QUERY(pnt <* QUERY(gsel <* gs\geometric_set.elements | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT' IN TYPEOF(gsel)) | NOT (gbsf_check_point(pnt)))) = 0))) = 0;

WR5: SIZEOF(QUERY(gs <* QUERY(it <* SELF.items | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET' IN TYPEOF(it)) | NOT (SIZEOF(QUERY(cv <* QUERY(gsel <* gs\geometric_set.elements | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF(gsel)) | NOT (gbsf_check_curve(cv)))) = 0))) = 0;

WR6: SIZEOF(QUERY(gs <* QUERY(it <* SELF.items | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET' IN TYPEOF(it)) | NOT (SIZEOF(QUERY(sf <* QUERY(gsel <* gs\geometric_set.elements | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE' IN TYPEOF(gsel)) | NOT (gbsf_check_surface(sf)))) = 0))) = 0;

WR7: SIZEOF(QUERY(gs <* QUERY(it <* SELF.items | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_SET' IN TYPEOF(it)) | SIZEOF(QUERY(gsel <* gs\geometric_set.elements | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE' IN TYPEOF(gsel))) > 0)) > 0;

END_ENTITY;

ENTITY geometrically_bounded_wireframe_shape_representation

SUBTYPE OF ( shape_representation );

WHERE

WR1 :

SIZEOF (

QUERY ( it <* SELF.items| NOT ( SIZEOF ( TYPEOF (it) * [ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_CURVE_SET', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' ]) = 1) )) = 0;

WR2 :

SIZEOF (

QUERY ( it <* SELF.items| ( SIZEOF ( TYPEOF (it) * [ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_CURVE_SET', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' ]) = 1) )) >= 1;

WR3 :

SIZEOF (

QUERY ( gcs <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_CURVE_SET' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( crv <*

QUERY ( elem <* gcs\geometric_set.elements| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF (elem)) )| NOT valid_geometrically_bounded_wf_curve(crv) )) = 0) )) = 0;

WR4 :

SIZEOF (

QUERY ( gcs <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_CURVE_SET' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( pnts <*

QUERY ( elem <* gcs\geometric_set.elements| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT' IN TYPEOF (elem)) )| NOT valid_geometrically_bounded_wf_point(pnts) )) = 0) )) = 0;

WR5 :

SIZEOF (

QUERY ( gcs <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_CURVE_SET' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( cnc <*

QUERY ( elem <* gcs\geometric_set.elements| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC' IN TYPEOF (elem)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D' IN TYPEOF (cnc\conic.position)) )) = 0) )) = 0;

WR6 :

SIZEOF (

QUERY ( gcs <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_CURVE_SET' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( pline <*

QUERY ( elem <* gcs\geometric_set.elements| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF (elem)) )| NOT ( SIZEOF (pline\polyline.points) > 2) )) = 0) )) = 0;

WR7 :

SIZEOF (

QUERY ( mi <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRICALLY_BOUNDED_WIREFRAME_SHAPE_REPRESENTATION' IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation)) )) = 0;

END_ENTITY;

ENTITY global_uncertainty_assigned_context

SUBTYPE OF (representation_context);

uncertainty : SET [1:?] OF uncertainty_measure_with_unit;

END_ENTITY;

ENTITY global_unit_assigned_context

SUBTYPE OF (representation_context);

units : SET[1:?] OF unit;

END_ENTITY;

ENTITY group;

name : label;

description : OPTIONAL text;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY group_assignment

ABSTRACT SUPERTYPE;

assigned_group : group;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY group_relationship;

name : label;

description : OPTIONAL text;

relating_group : group;

related_group : group;

END_ENTITY;

ENTITY half_space_solid

SUBTYPE OF(geometric_representation_item);

base_surface   : surface;

agreement_flag : BOOLEAN;

END_ENTITY;

ENTITY hyperbola

SUBTYPE OF (conic);

semi_axis      : positive_length_measure;

semi_imag_axis : positive_length_measure;

END_ENTITY;

ENTITY id_attribute;

attribute_value : identifier;

identified_item : id_attribute_select;

END_ENTITY;

ENTITY identification_assignment

ABSTRACT SUPERTYPE;

assigned_id : identifier;

role : identification_role;

END_ENTITY;

ENTITY identification_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY intersection_curve

SUBTYPE OF (surface_curve);

WHERE

WR1: SIZEOF(SELF\surface_curve.associated_geometry) = 2;

WR2: associated_surface(SELF\surface_curve.associated_geometry[1]) <>

associated_surface(SELF\surface_curve.associated_geometry[2]);

END_ENTITY;

ENTITY invisibility;

invisible_items : SET [1:?] OF invisible_item;

END_ENTITY;

ENTITY item_defined_transformation;

name             : label;

description      : OPTIONAL text;

transform_item_1 : representation_item;

transform_item_2 : representation_item;

END_ENTITY;

ENTITY language

SUBTYPE OF (group);

WHERE

WR1: SELF\group.name <> '';

END_ENTITY;

ENTITY leader_curve

SUBTYPE OF (annotation_curve_occurrence);

WHERE

WR1: SIZEOF(

QUERY(ldc <* USEDIN( SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT.CONTENTS')

|   'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'LEADER_DIRECTED_CALLOUT'  IN TYPEOF(ldc))) >= 1;

END_ENTITY;

ENTITY leader_directed_callout

SUBTYPE OF (draughting_callout);

WHERE

WR1: SIZEOF (QUERY (l_1 <* SELF\draughting_callout.contents |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_CURVE' IN (TYPEOF(l_1)))) >= 1;

WR2: SIZEOF(SELF\draughting_callout.contents) >=2;

END_ENTITY;

ENTITY leader_directed_dimension

SUBTYPE OF (leader_directed_callout);

WHERE

WR1: SIZEOF (QUERY (con <* SELF.contents |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_CURVE' IN TYPEOF (con)))=1;

END_ENTITY;

ENTITY leader_terminator

SUBTYPE OF (terminator_symbol);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_CURVE' IN TYPEOF

(SELF\terminator_symbol.annotated_curve);

END_ENTITY;

ENTITY length_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY length_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 1.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY limits_and_fits;

form_variance   : label;

zone_variance   : label;

grade           : label;

source          : text;

END_ENTITY;

ENTITY line

SUBTYPE OF (curve);

pnt : cartesian_point;

dir : vector;

WHERE

WR1: dir.dim  = pnt.dim;

END_ENTITY;

ENTITY line_profile_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF)) OR ( SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3);

WR2 :

SIZEOF (

QUERY ( sar <* USEDIN (SELF\geometric_tolerance.toleranced_shape_aspect, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'SHAPE_ASPECT_RELATIONSHIP.RELATING_SHAPE_ASPECT')| (sar.name IN [ 'affected plane association', 'resulting intersection curve association' ]) )) = 1;

END_ENTITY;

ENTITY linear_dimension

SUBTYPE OF (dimension_curve_directed_callout);

END_ENTITY;

ENTITY local_time;

hour_component : hour_in_day;

minute_component : OPTIONAL minute_in_hour;

second_component : OPTIONAL second_in_minute;

zone : coordinated_universal_time_offset;

WHERE

WR1: valid_time (SELF);

END_ENTITY;

ENTITY loop

SUPERTYPE OF (ONEOF (

VERTEX_LOOP,

EDGE_LOOP,

POLY_LOOP))

SUBTYPE OF (topological_representation_item);

END_ENTITY;

ENTITY lot_effectivity

SUBTYPE OF (effectivity);

effectivity_lot_id : identifier;

effectivity_lot_size : measure_with_unit;

END_ENTITY;

ENTITY luminous_intensity_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LUMINOUS_INTENSITY_UNIT' IN TYPEOF(SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY luminous_intensity_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 1.0);

END_ENTITY;

ENTITY make_from_usage_option

SUBTYPE OF (product_definition_usage);

ranking           : INTEGER;

ranking_rationale : text;

quantity          : measure_with_unit;

WHERE

WR1: (NOT ('NUMBER' IN TYPEOF(quantity.value_component)))

OR (quantity.value_component > 0);

END_ENTITY;

ENTITY manifold_solid_brep

SUBTYPE OF (solid_model);

outer : closed_shell;

END_ENTITY;

ENTITY manifold_surface_shape_representation

SUBTYPE OF (shape_representation);

WHERE

WR1: SIZEOF (QUERY (it <* SELF.items |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D'] * TYPEOF (it)) = 1))) = 0;

WR2: SIZEOF (QUERY (it <* SELF.items |

SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'] * TYPEOF (it)) = 1)) > 0;

WR3: SIZEOF (QUERY (mi <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MANIFOLD_SURFACE_SHAPE_REPRESENTATION'

IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation))

AND

(SIZEOF(QUERY (mr_it <*

mi\mapped_item.mapping_source.mapped_representation.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL'

IN TYPEOF (mr_it)))) > 0 )))) = 0;

WR4: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (sh <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OPEN_SHELL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_CLOSED_SHELL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CLOSED_SHELL']

* TYPEOF (sh)) = 1))) = 0))) = 0;

WR5: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_SURFACE' IN TYPEOF (fa)) )) = 0)))

= 0))) = 0;

WR6: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(msf_surface_check(fa\face_surface.face_geometry))))) = 0)))

= 0))) = 0;

WR7: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (bnds <* fa.bounds |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP']

* TYPEOF (bnds.bound)) = 1))) = 0)))) = 0))) = 0))) = 0;

WR8: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items|

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (elp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) |

NOT (SIZEOF (QUERY (oe <* elp_fbnds\path.edge_list |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_CURVE' IN TYPEOF

(oe.edge_element)))) = 0))) = 0)))) = 0))) = 0))) = 0;

WR9: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (elp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) |

NOT (SIZEOF (QUERY (oe_cv <* QUERY (oe <*

elp_fbnds\path.edge_list |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_CURVE' IN TYPEOF (oe.edge_element)) |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE'] *

TYPEOF (oe_cv.edge_element\edge_curve.edge_geometry))

= 1))) = 0))) = 0)))) = 0))) = 0))) = 0;

WR10: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (elp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) |

NOT (SIZEOF (QUERY (oe <* elp_fbnds\path.edge_list |

NOT (msf_curve_check (oe.edge_element\edge_curve.edge_geometry))))

= 0))) = 0)))) = 0))) = 0))) = 0;

WR11: SIZEOF (QUERY(sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (elp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) |

NOT (SIZEOF (QUERY (oe <* elp_fbnds\path.edge_list|

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF

(oe.edge_element.edge_start))

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN

TYPEOF (oe.edge_element.edge_end)))))

= 0))) = 0)))) = 0))) = 0))) = 0;

WR12: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (elp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (bnds.bound)) |

NOT (SIZEOF (QUERY (oe <* elp_fbnds\path.edge_list |

NOT ((SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEGENERATE_PCURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_SURFACE'] * TYPEOF

(oe.edge_element.edge_start\vertex_point.vertex_geometry)) = 1)

AND

(SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEGENERATE_PCURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_SURFACE'] * TYPEOF

(oe.edge_element.edge_end\vertex_point.vertex_geometry)) = 1

)))) = 0))) = 0)))) = 0))) = 0))) = 0;

WR13: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (vlp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP' IN TYPEOF (bnds.bound)) |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF

(vlp_fbnds\vertex_loop.loop_vertex)))) = 0)))) = 0)))

= 0))) = 0;

WR14: SIZEOF (QUERY (sbsm <* QUERY (it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_SURFACE_MODEL' IN TYPEOF (it)) |

NOT (SIZEOF (QUERY (cfs <*

sbsm\shell_based_surface_model.sbsm_boundary |

NOT (SIZEOF (QUERY (fa <* cfs\connected_face_set.cfs_faces |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ADVANCED_FACE' IN TYPEOF (fa))

OR

(SIZEOF (QUERY (vlp_fbnds <* QUERY (bnds <* fa.bounds |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP' IN TYPEOF (bnds.bound)) |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEGENERATE_PCURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_SURFACE'] * TYPEOF

(vlp_fbnds\vertex_loop.loop_vertex\vertex_point.vertex_geometry))

= 1))) = 0)))) = 0))) = 0))) = 0;

END_ENTITY;

ENTITY mapped_item

SUBTYPE OF (representation_item);

mapping_source : representation_map;

mapping_target : representation_item;

WHERE

WR1: acyclic_mapped_representation(using_representations(SELF), [SELF]);

END_ENTITY;

ENTITY mass_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MASS_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY mass_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 1.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY measure_qualification;

name : label;

description : text;

qualified_measure : measure_with_unit;

qualifiers : SET [1:?] OF value_qualifier;

WHERE

WR1: SIZEOF(QUERY(temp <* qualifiers |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRECISION_QUALIFIER'

IN TYPEOF(temp))) < 2;

END_ENTITY;

ENTITY measure_representation_item

SUBTYPE OF (representation_item, measure_with_unit);

END_ENTITY;

ENTITY measure_with_unit

SUPERTYPE OF (ONEOF (

LENGTH_MEASURE_WITH_UNIT,

MASS_MEASURE_WITH_UNIT,

TIME_MEASURE_WITH_UNIT,

ELECTRIC_CURRENT_MEASURE_WITH_UNIT,

THERMODYNAMIC_TEMPERATURE_MEASURE_WITH_UNIT,

CELSIUS_TEMPERATURE_MEASURE_WITH_UNIT,

AMOUNT_OF_SUBSTANCE_MEASURE_WITH_UNIT,

LUMINOUS_INTENSITY_MEASURE_WITH_UNIT,

PLANE_ANGLE_MEASURE_WITH_UNIT,

SOLID_ANGLE_MEASURE_WITH_UNIT,

AREA_MEASURE_WITH_UNIT,

VOLUME_MEASURE_WITH_UNIT,

RATIO_MEASURE_WITH_UNIT));

value_component : measure_value;

unit_component : unit;

WHERE

WR1: valid_units (SELF);

END_ENTITY;

ENTITY mechanical_context

SUBTYPE OF (product_context);

WHERE

WR1: SELF.discipline_type = 'mechanical';

END_ENTITY;

ENTITY mechanical_design_geometric_presentation_area

SUBTYPE OF (presentation_area);

WHERE

WR1:  -- only presentation_views or axis2_placements in

-- mechanical_design_geometric_presentation_area

SIZEOF(QUERY(it1 <* SELF.items |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT'

IN TYPEOF(it1))

OR

(('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'

IN TYPEOF(it1)) AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_VIEW'

IN TYPEOF

(it1\mapped_item.mapping_source.mapped_representation)))))) = 0;

WR2:  -- only mechanical_design_geometric_presentation_representation

-- via camera_image_3d_with_scale or axis2_placements in

-- presentation_views

SIZEOF(QUERY(pv <* QUERY(mi1 <* QUERY(it1 <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'

IN TYPEOF(it1)) |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_VIEW'

IN TYPEOF

(mi1\mapped_item.mapping_source.mapped_representation)) |

-- search in all presentation_views for axis2_placements and

-- mapped_items and for the subtype of mapped_item

-- camera_image_3d_with_scale; the latter shall reference

-- a mechanical_design_geometric_presentation_representation;

-- the supertype mapped_item shall reference presentation_view.

NOT (SIZEOF(QUERY(it2 <* pv\mapped_item.mapping_source.

mapped_representation\representation.items |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT'

IN TYPEOF(it2))

OR

(('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'

IN TYPEOF(it2)) AND NOT

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'CAMERA_IMAGE_3D_WITH_SCALE' IN TYPEOF(it2))) AND NOT (

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_VIEW'

IN TYPEOF

(it2\mapped_item.mapping_source.mapped_representation)))

OR

(('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'CAMERA_IMAGE_3D_WITH_SCALE' IN TYPEOF(it2))

AND NOT (

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'MECHANICAL_DESIGN_GEOMETRIC_PRESENTATION_REPRESENTATION'

IN TYPEOF (it2\mapped_item.mapping_source.mapped_representation) ))

))) = 0))) = 0;

WR3:  (SIZEOF(QUERY(ps <* USEDIN (SELF\presentation_area,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT') | ((ps.size\planar_extent.size_in_x <= 0)

OR

(ps.size\planar_extent.size_in_y <= 0)))) = 0)

AND

(SIZEOF(QUERY(ais <* USEDIN (SELF\presentation_area,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AREA_IN_SET.AREA') |

(SIZEOF(QUERY(ps <* USEDIN (ais,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT') |

((ps.size\planar_extent.size_in_x <= 0)

OR

(ps.size\planar_extent.size_in_y <= 0)))) > 0))) = 0);

WR4:  (SIZEOF(QUERY(ps <* USEDIN (SELF\presentation_area,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AXIS2_PLACEMENT_2D' IN TYPEOF (ps.size.placement)))) = 1)

AND

(SIZEOF(QUERY(ps <* USEDIN (SELF\presentation_area,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AXIS2_PLACEMENT_3D' IN TYPEOF (ps.size.placement)))) = 0)

OR

((SIZEOF(QUERY(ais <* USEDIN (SELF\presentation_area,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AREA_IN_SET.AREA') |

(SIZEOF(QUERY(ps <* USEDIN (ais,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AXIS2_PLACEMENT_2D' IN TYPEOF (ps.size.placement)))) = 1))) = 1)

AND

(SIZEOF(QUERY(ais <* USEDIN (SELF\presentation_area,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AREA_IN_SET.AREA') |

(SIZEOF(QUERY(ps <* USEDIN (ais,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AXIS2_PLACEMENT_3D' IN TYPEOF (ps.size.placement)))) = 0))) = 1));

END_ENTITY;

ENTITY mechanical_design_geometric_presentation_representation

SUBTYPE OF (representation);

WHERE

WR1:  SIZEOF(QUERY(it <* SELF.items |

NOT (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CAMERA_MODEL_D3']

* TYPEOF(it)) = 1))) = 0;

WR2:  -- only shape_representations and

-- mechanical_design_geometric_presentation_representations

-- shall be referenced from mapped_items

SIZEOF(QUERY(mi <* QUERY(it <* SELF.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'

IN TYPEOF(it))) | NOT (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SHAPE_REPRESENTATION',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'MECHANICAL_DESIGN_GEOMETRIC_PRESENTATION_REPRESENTATION']

* TYPEOF(mi\mapped_item.mapping_source.mapped_representation))

= 1))) = 0;

WR3:  -- a mapped_item that is styled shall reference a

-- shape_representation

SIZEOF(QUERY(smi <* QUERY(si <* QUERY(it <* SELF.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it))) |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'

IN TYPEOF(si\styled_item.item))) | NOT (

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SHAPE_REPRESENTATION' IN TYPEOF (smi\styled_item.

item\mapped_item.mapping_source.mapped_representation))) )) = 0;

WR4:  SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(pss <* psa.styles | NOT (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_STYLE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE']

* TYPEOF(pss)) = 1))) = 0))) = 0))) = 0;

WR5:  SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) |

NOT (SIZEOF(QUERY(psbc <* QUERY(psa <* si\styled_item.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_STYLE_BY_CONTEXT' IN TYPEOF(psa)) | NOT (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'REPRESENTATION_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION']

* TYPEOF(psbc\presentation_style_by_context.style_context))

= 1))) = 0))) = 0;

WR6:  SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ps <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_STYLE'

IN TYPEOF(pss)) | NOT

(('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF (ps\point_style.marker_size))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(ps\point_style.marker_colour))

= 1)))) = 0))) = 0))) = 0;

WR7:  SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(cs <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF(pss)) | NOT((SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(cs\curve_style.curve_colour)) = 1)

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF (cs\curve_style.curve_width))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE_FONT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_CURVE_FONT']

* TYPEOF(cs\curve_style.curve_font)) = 1)))) = 0))) = 0))) = 0;

WR8:  SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_SIDE_STYLE' IN TYPEOF

(ssu\surface_style_usage.style)))) = 0))) = 0))) = 0;

WR9:  SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) | NOT (SIZEOF(QUERY(sses <*

ssu\surface_style_usage.style\surface_side_style.styles |

NOT (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_PARAMETER_LINE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_CONTROL_GRID',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_SILHOUETTE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_SEGMENTATION_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_FILL_AREA',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_BOUNDARY']

* TYPEOF(sses)) = 1))) = 0))) = 0))) = 0))) = 0;

WR10: SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) | NOT (SIZEOF(QUERY(sspl <* QUERY(sses <*

ssu\surface_style_usage.style\surface_side_style.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_PARAMETER_LINE' IN TYPEOF(sses)) |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF

(sspl\surface_style_parameter_line.style_of_parameter_lines))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(sspl\surface_style_parameter_line.

style_of_parameter_lines\curve_style.curve_colour)) = 1)

AND (

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF

(sspl\surface_style_parameter_line.

style_of_parameter_lines\curve_style.curve_width))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE_FONT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'DRAUGHTING_PRE_DEFINED_CURVE_FONT']

* TYPEOF(sspl\surface_style_parameter_line.

style_of_parameter_lines\curve_style.curve_font)) = 1))))

= 0))) = 0))) = 0))) = 0;

WR11: SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) | NOT (SIZEOF(QUERY(sscg <* QUERY(sses <*

ssu\surface_style_usage.style\surface_side_style.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_CONTROL_GRID' IN TYPEOF(sses)) |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF (sscg\surface_style_control_grid.style_of_control_grid))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(sscg\surface_style_control_grid.

style_of_control_grid\curve_style.curve_colour)) = 1)

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF

(sscg\surface_style_control_grid.

style_of_control_grid\curve_style.curve_width))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE_FONT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_CURVE_FONT']

* TYPEOF(sscg\surface_style_control_grid.

style_of_control_grid\curve_style.curve_font)) = 1))))

= 0))) = 0))) = 0))) = 0;

WR12: SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) |

NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) | NOT (SIZEOF(QUERY(sssh <* QUERY(sses <*

ssu\surface_style_usage.style\surface_side_style.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_SILHOUETTE' IN TYPEOF(sses)) |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF (sssh\surface_style_silhouette.style_of_silhouette))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(sssh\surface_style_silhouette.

style_of_silhouette\curve_style.curve_colour)) = 1)

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF

(sssh\surface_style_silhouette.style_of_silhouette\curve_style.

curve_width))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE_FONT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_CURVE_FONT']

* TYPEOF(sssh\surface_style_silhouette.

style_of_silhouette\curve_style.curve_font)) = 1))))

= 0))) = 0))) = 0))) = 0;

WR13: SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) | NOT (SIZEOF(QUERY(sssc <* QUERY(sses <*

ssu\surface_style_usage.style\surface_side_style.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_SEGMENTATION_CURVE' IN TYPEOF(sses)) |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF

(sssc\surface_style_segmentation_curve.style_of_segmentation_curve))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(sssc\surface_style_segmentation_curve.

style_of_segmentation_curve\curve_style.curve_colour)) = 1)

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF

(sssc\surface_style_segmentation_curve.

style_of_segmentation_curve\curve_style.curve_width))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE_FONT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_CURVE_FONT']

* TYPEOF(sssc\surface_style_segmentation_curve.

style_of_segmentation_curve\curve_style.curve_font)) = 1))))

= 0))) = 0))) = 0))) = 0;

WR14: SIZEOF(QUERY(si <* QUERY(it <* SELF.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM'

IN TYPEOF(it)) | NOT (SIZEOF(QUERY(psa <* si\styled_item.styles |

NOT (SIZEOF(QUERY(ssu <* QUERY(pss <* psa.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE'

IN TYPEOF(pss)) | NOT (SIZEOF(QUERY(ssbd <* QUERY(sses <*

ssu\surface_style_usage.style\surface_side_style.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_BOUNDARY' IN TYPEOF(sses)) |

NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE'

IN TYPEOF (ssbd\surface_style_boundary.style_of_boundary))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COLOUR_RGB',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_COLOUR']

* TYPEOF(ssbd\surface_style_boundary.

style_of_boundary\curve_style.curve_colour)) = 1)

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'POSITIVE_LENGTH_MEASURE' IN TYPEOF (ssbd\surface_style_boundary.

style_of_boundary\curve_style.curve_width))

AND (SIZEOF(

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE_FONT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_PRE_DEFINED_CURVE_FONT']

* TYPEOF(ssbd\surface_style_boundary.

style_of_boundary\curve_style.curve_font)) = 1)))) = 0)))

= 0))) = 0))) = 0;

END_ENTITY;

ENTITY modified_geometric_tolerance

SUBTYPE OF (geometric_tolerance);

modifier : limit_condition;

END_ENTITY;

ENTITY multi_language_attribute_assignment

SUBTYPE OF (attribute_value_assignment);

items : SET [1:?] OF multi_language_attribute_item;

DERIVE

translation_language : language := language_indication[1]\attribute_classification_assignment.assigned_class;

INVERSE

language_indication: SET[1:1] OF attribute_language_assignment FOR items;

WHERE

WR1: (SELF\attribute_value_assignment.role.name = 'alternate language');

WR2: SIZEOF( QUERY( ala <* language_indication |

(ala\attribute_classification_assignment.attribute_name = 'attribute_value') AND

(ala\attribute_classification_assignment.role.name='translated') )) = 1 ;

WR3: SELF\attribute_value_assignment.attribute_name <> '' ;

WR4: SIZEOF(QUERY(ci <* items |

SIZEOF(QUERY(ata <* USEDIN(ci, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MULTI_LANGUAGE_ATTRIBUTE_ASSIGNMENT.ITEMS') |

(ata\attribute_value_assignment.attribute_name = SELF\attribute_value_assignment.attribute_name) AND

(ata.translation_language :=: translation_language) ))>1 )) =0;

WR5: SIZEOF(QUERY(ci <* items |

SIZEOF(QUERY(ata <* USEDIN(ci, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ATTRIBUTE_LANGUAGE_ASSIGNMENT.ITEMS') |

(ata\attribute_classification_assignment.role.name='primary') AND

(ata\attribute_classification_assignment.attribute_name= SELF\attribute_value_assignment.attribute_name) AND

(ata\attribute_classification_assignment.assigned_class :=: translation_language) ))>0 )) =0;

END_ENTITY;

ENTITY name_assignment

ABSTRACT SUPERTYPE;

assigned_name : label;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1 ;

END_ENTITY;

ENTITY name_attribute;

attribute_value : label;

named_item : name_attribute_select;

END_ENTITY;

ENTITY named_unit

SUPERTYPE OF (ONEOF (

SI_UNIT,

CONVERSION_BASED_UNIT,

CONTEXT_DEPENDENT_UNIT)

ANDOR ONEOF (

LENGTH_UNIT,

MASS_UNIT,

TIME_UNIT,

ELECTRIC_CURRENT_UNIT,

THERMODYNAMIC_TEMPERATURE_UNIT,

AMOUNT_OF_SUBSTANCE_UNIT,

LUMINOUS_INTENSITY_UNIT,

PLANE_ANGLE_UNIT,

SOLID_ANGLE_UNIT,

AREA_UNIT,

VOLUME_UNIT,

RATIO_UNIT));

dimensions : dimensional_exponents;

END_ENTITY;

ENTITY next_assembly_usage_occurrence

SUBTYPE OF (assembly_component_usage);

END_ENTITY;

ENTITY object_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY offset_curve_2d

SUBTYPE OF (curve);

basis_curve    : curve;

distance       : length_measure;

self_intersect : LOGICAL;

WHERE

WR1: basis_curve.dim = 2;

END_ENTITY;

ENTITY offset_curve_3d

SUBTYPE OF (curve);

basis_curve    : curve;

distance       : length_measure;

self_intersect : LOGICAL;

ref_direction  : direction;

WHERE

WR1 : (basis_curve.dim = 3) AND (ref_direction.dim = 3);

END_ENTITY;

ENTITY offset_surface

SUBTYPE OF (surface);

basis_surface  : surface;

distance       : length_measure;

self_intersect : LOGICAL;

END_ENTITY;

ENTITY one_direction_repeat_factor

SUBTYPE OF (geometric_representation_item);

repeat_factor : vector;

END_ENTITY;

ENTITY open_shell

SUBTYPE OF (connected_face_set);

END_ENTITY;

ENTITY ordinal_date

SUBTYPE OF (date);

day_component : day_in_year_number;

WHERE

WR1: (NOT leap_year(SELF.year_component) AND { 1 <= day_component <= 365 }) OR (leap_year(SELF.year_component) AND { 1 <= day_component <= 366 });

END_ENTITY;

ENTITY ordinate_dimension

SUBTYPE OF (projection_directed_callout);

END_ENTITY;

ENTITY organization;

id : OPTIONAL identifier;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY organization_assignment

ABSTRACT SUPERTYPE;

assigned_organization : organization;

role : organization_role;

END_ENTITY;

ENTITY organization_relationship;

name : label;

description : OPTIONAL text;

relating_organization : organization;

related_organization : organization;

END_ENTITY;

ENTITY organization_role;

name : label;

DERIVE

description : text := get_description_value(SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY organizational_address

SUBTYPE OF (address);

organizations : SET[1:?] OF organization;

description : OPTIONAL text;

END_ENTITY;

ENTITY organizational_project;

name : label;

description : OPTIONAL text;

responsible_organizations : SET[1:?] OF organization;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY organizational_project_assignment

ABSTRACT SUPERTYPE;

assigned_organizational_project : organizational_project;

role : organizational_project_role;

END_ENTITY;

ENTITY organizational_project_relationship;

name : label;

description : OPTIONAL text;

relating_organizational_project : organizational_project;

related_organizational_project : organizational_project;

END_ENTITY;

ENTITY organizational_project_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY oriented_closed_shell

SUBTYPE OF (closed_shell);

closed_shell_element : closed_shell;

orientation          : BOOLEAN;

DERIVE

SELF\connected_face_set.cfs_faces : SET [1:?] OF face

:= conditional_reverse(SELF.orientation,

SELF.closed_shell_element.cfs_faces);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_CLOSED_SHELL'

IN TYPEOF (SELF.closed_shell_element));

END_ENTITY;

ENTITY oriented_edge

SUBTYPE OF (edge);

edge_element : edge;

orientation  : BOOLEAN;

DERIVE

SELF\edge.edge_start : vertex := boolean_choose (SELF.orientation,

SELF.edge_element.edge_start,

SELF.edge_element.edge_end);

SELF\edge.edge_end   : vertex := boolean_choose (SELF.orientation,

SELF.edge_element.edge_end,

SELF.edge_element.edge_start);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_EDGE' IN TYPEOF (SELF.edge_element));

END_ENTITY;

ENTITY oriented_face

SUBTYPE OF (face);

face_element : face;

orientation  : BOOLEAN;

DERIVE

SELF\face.bounds : SET[1:?] OF face_bound

:= conditional_reverse(SELF.orientation,SELF.face_element.bounds);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_FACE' IN TYPEOF (SELF.face_element));

END_ENTITY;

ENTITY oriented_open_shell

SUBTYPE OF (open_shell);

open_shell_element : open_shell;

orientation        : BOOLEAN;

DERIVE

SELF\connected_face_set.cfs_faces : SET [1:?] OF face

:= conditional_reverse(SELF.orientation,

SELF.open_shell_element.cfs_faces);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_OPEN_SHELL'

IN TYPEOF (SELF.open_shell_element));

END_ENTITY;

ENTITY oriented_path

SUBTYPE OF (path);

path_element : path;

orientation  : BOOLEAN;

DERIVE

SELF\path.edge_list : LIST [1:?] OF UNIQUE oriented_edge

:= conditional_reverse(SELF.orientation,

SELF.path_element.edge_list);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_PATH' IN TYPEOF (SELF.path_element));

END_ENTITY;

ENTITY oriented_surface

SUBTYPE OF (surface);

orientation : BOOLEAN;

END_ENTITY;

ENTITY outer_boundary_curve

SUBTYPE OF (boundary_curve);

END_ENTITY;

ENTITY over_riding_styled_item

SUBTYPE OF (styled_item);

over_ridden_style : styled_item;

END_ENTITY;

ENTITY parabola

SUBTYPE OF (conic);

focal_dist : length_measure;

WHERE

WR1: focal_dist <> 0.0;

END_ENTITY;

ENTITY parallel_offset

SUBTYPE OF (derived_shape_aspect);

offset               : measure_with_unit;

WHERE

WR1: SIZEOF (SELF\derived_shape_aspect.deriving_relationships)= 1;

END_ENTITY;

ENTITY parallelism_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) < 3;

END_ENTITY;

ENTITY parametric_representation_context

SUBTYPE OF (representation_context);

END_ENTITY;

ENTITY path

SUPERTYPE OF (ONEOF (

EDGE_LOOP,

ORIENTED_PATH))

SUBTYPE OF (topological_representation_item);

edge_list  : LIST [1:?] OF UNIQUE oriented_edge;

WHERE

WR1: path_head_to_tail(SELF);

END_ENTITY;

ENTITY pcurve

SUBTYPE OF (curve);

basis_surface      : surface;

reference_to_curve : definitional_representation;

WHERE

WR1: SIZEOF(reference_to_curve\representation.items) = 1;

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF

(reference_to_curve\representation.items[1]);

WR3: reference_to_curve\representation.items[1]\

geometric_representation_item.dim =2;

END_ENTITY;

ENTITY perpendicular_to

SUBTYPE OF (derived_shape_aspect);

WHERE

WR1: SIZEOF (SELF\derived_shape_aspect.deriving_relationships)= 1;

END_ENTITY;

ENTITY perpendicularity_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3;

END_ENTITY;

ENTITY person;

id : identifier;

last_name : OPTIONAL label;

first_name : OPTIONAL label;

middle_names : OPTIONAL LIST[1:?] OF label;

prefix_titles : OPTIONAL LIST[1:?] OF label;

suffix_titles : OPTIONAL LIST[1:?] OF label;

WHERE

WR1: EXISTS(last_name) OR EXISTS(first_name);

END_ENTITY;

ENTITY person_and_organization;

the_person : person;

the_organization : organization;

DERIVE

name : label := get_name_value (SELF);

description : text := get_description_value(SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY person_and_organization_address

SUBTYPE OF (organizational_address, personal_address);

SELF\organizational_address.organizations : SET[1:1] OF organization;

SELF\personal_address.people : SET[1:1] OF person;

WHERE

WR1: SIZEOF(QUERY(pao <* USEDIN (SELF\personal_address.people[1], 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PERSON_AND_ORGANIZATION.THE_PERSON') | pao.the_organization :=: SELF\organizational_address.organizations[1])) = 1;

END_ENTITY;

ENTITY person_and_organization_assignment

ABSTRACT SUPERTYPE;

assigned_person_and_organization : person_and_organization;

role : person_and_organization_role;

END_ENTITY;

ENTITY person_and_organization_role;

name : label;

DERIVE

description : text := get_description_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

END_ENTITY;

ENTITY personal_address

SUBTYPE OF (address);

people : SET[1:?] OF person;

description : OPTIONAL text;

END_ENTITY;

ENTITY placed_datum_target_feature

SUBTYPE OF (datum_target);

DERIVE

representation_associations : SET[0:?] OF property_definition_representation := get_shape_aspect_property_definition_representations(SELF);

WHERE

WR1: SELF.description IN ['point','line','rectangle','circle', 'circular line'];

WR2: SIZEOF (QUERY (pdr <* representation_associations | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION_WITH_PARAMETERS' IN TYPEOF (pdr.used_representation) )) = 1;

WR3: valid_datum_target_parameters(SELF);

END_ENTITY;

ENTITY placement

SUPERTYPE OF (ONEOF (

AXIS1_PLACEMENT,

AXIS2_PLACEMENT_2D,

AXIS2_PLACEMENT_3D))

SUBTYPE OF (geometric_representation_item);

location : cartesian_point;

END_ENTITY;

ENTITY planar_box

SUBTYPE OF (planar_extent);

placement:  axis2_placement;

END_ENTITY;

ENTITY planar_extent

SUBTYPE OF (geometric_representation_item);

size_in_x : length_measure;

size_in_y : length_measure;

END_ENTITY;

ENTITY plane

SUBTYPE OF (elementary_surface);

END_ENTITY;

ENTITY plane_angle_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLANE_ANGLE_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY plane_angle_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY  plus_minus_tolerance;

range                : tolerance_method_definition;

toleranced_dimension : dimensional_characteristic;

UNIQUE

UR1: toleranced_dimension;

END_ENTITY;

ENTITY point

SUPERTYPE OF (ONEOF (

CARTESIAN_POINT,

POINT_ON_CURVE,

POINT_ON_SURFACE,

POINT_REPLICA,

DEGENERATE_PCURVE))

SUBTYPE OF (geometric_representation_item);

END_ENTITY;

ENTITY point_on_curve

SUBTYPE OF (point);

basis_curve     : curve;

point_parameter : parameter_value;

END_ENTITY;

ENTITY point_on_surface

SUBTYPE OF (point);

basis_surface     : surface;

point_parameter_u : parameter_value;

point_parameter_v : parameter_value;

END_ENTITY;

ENTITY point_replica

SUBTYPE OF (point);

parent_pt      : point;

transformation : cartesian_transformation_operator;

WHERE

WR1: transformation.dim = parent_pt.dim;

WR2: acyclic_point_replica (SELF,parent_pt);

END_ENTITY;

ENTITY point_style;

name          : label;

marker        : marker_select;

marker_size   : size_select;

marker_colour : colour;

END_ENTITY;

ENTITY poly_loop

SUBTYPE OF (loop,geometric_representation_item);

polygon : LIST [3:?] OF UNIQUE cartesian_point;

END_ENTITY;

ENTITY polyline

SUBTYPE OF (bounded_curve);

points : LIST [2:?] OF cartesian_point;

END_ENTITY;

ENTITY position_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF)) OR ( SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3);

END_ENTITY;

ENTITY pre_defined_character_glyph

SUBTYPE OF (pre_defined_item);

END_ENTITY;

ENTITY pre_defined_colour

SUBTYPE OF (pre_defined_item, colour);

END_ENTITY;

ENTITY pre_defined_curve_font

SUBTYPE OF (pre_defined_item);

END_ENTITY;

ENTITY pre_defined_item;

name : label;

END_ENTITY;

ENTITY pre_defined_marker

SUBTYPE OF (pre_defined_item);

END_ENTITY;

ENTITY pre_defined_symbol

SUBTYPE OF (pre_defined_item);

END_ENTITY;

ENTITY pre_defined_terminator_symbol

SUBTYPE OF (pre_defined_symbol);

WHERE

WR1: SELF.name IN ['blanked arrow', 'blanked box', 'blanked dot', 'dimension origin', 'filled arrow', 'filled box', 'filled dot', 'integral symbol', 'open arrow', 'slash', 'unfilled arrow'];

END_ENTITY;

ENTITY pre_defined_text_font

SUBTYPE OF (pre_defined_item);

END_ENTITY;

ENTITY pre_defined_tile

SUBTYPE OF (pre_defined_item);

END_ENTITY;

ENTITY precision_qualifier;

precision_value : INTEGER;

END_ENTITY;

ENTITY presentation_area

SUBTYPE OF (presentation_representation);

WHERE

WR1: ((SIZEOF (QUERY (ais <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'AREA_IN_SET.AREA') |

SIZEOF (USEDIN (ais, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT')) =1)) > 0) OR

(SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_SIZE.UNIT')) =1));

END_ENTITY;

ENTITY presentation_layer_assignment;

name           : label;

description    : text;

assigned_items : SET [1:?] OF layered_item;

END_ENTITY;

ENTITY presentation_representation

SUBTYPE OF (representation);

WHERE

WR1: SELF\representation.

context_of_items\geometric_representation_context.

coordinate_space_dimension = 2;

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRIC_REPRESENTATION_CONTEXT'

IN TYPEOF (SELF\representation.context_of_items);

END_ENTITY;

ENTITY presentation_set;

INVERSE

areas : SET [1:?] OF area_in_set FOR in_set;

END_ENTITY;

ENTITY presentation_size;

unit : presentation_size_assignment_select;

size : planar_box;

WHERE

WR1: (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_REPRESENTATION'

IN TYPEOF (SELF.unit)) AND

item_in_context (SELF.size,

SELF.unit\representation.context_of_items)

)

OR

(

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AREA_IN_SET'

IN TYPEOF (SELF.unit)) AND

(SIZEOF (QUERY ( ais <* SELF.unit\area_in_set.in_set.areas |

NOT item_in_context (SELF.size, ais.area\representation.

context_of_items) )) = 0)

);

END_ENTITY;

ENTITY presentation_style_assignment;

styles : SET [1:?] OF presentation_style_select;

WHERE

WR1: SIZEOF (QUERY (style1 <* SELF.styles |

NOT (SIZEOF (QUERY (style2 <* (SELF.styles - style1) |

NOT ((TYPEOF (style1) <> TYPEOF (style2)) OR

(SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SURFACE_STYLE_USAGE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'EXTERNALLY_DEFINED_STYLE'] *

TYPEOF (style1)) = 1)

))) = 0

))) = 0;

WR2: SIZEOF (QUERY (style1 <* SELF.styles |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_STYLE_USAGE' IN

TYPEOF(style1)

)) <= 2;

END_ENTITY;

ENTITY presentation_style_by_context

SUBTYPE OF (presentation_style_assignment);

style_context : style_context_select;

END_ENTITY;

ENTITY presentation_view

SUBTYPE OF (presentation_representation);

END_ENTITY;

ENTITY product;

id : identifier;

name : label;

description : OPTIONAL text;

frame_of_reference : SET[1:?] OF product_context;

END_ENTITY;

ENTITY product_category;

name : label;

description : OPTIONAL text;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY product_category_relationship;

name : label;

description : OPTIONAL text;

category : product_category;

sub_category : product_category;

WHERE

WR1: acyclic_product_category_relationship (SELF, [SELF.sub_category]);

END_ENTITY;

ENTITY product_concept;

id                  : identifier;

name                : label;

description         : OPTIONAL text;

market_context      : product_concept_context;

UNIQUE

UR1: id;

END_ENTITY;

ENTITY product_concept_context

SUBTYPE OF (application_context_element);

market_segment_type : label;

END_ENTITY;

ENTITY product_concept_relationship;

name                     : label;

description              : OPTIONAL text;

relating_product_concept : product_concept;

related_product_concept  : product_concept;

END_ENTITY;

ENTITY product_context

SUBTYPE OF (application_context_element);

discipline_type : label;

END_ENTITY;

ENTITY product_definition;

id : identifier;

description : OPTIONAL text;

formation : product_definition_formation;

frame_of_reference : product_definition_context;

DERIVE

name : label := get_name_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

END_ENTITY;

ENTITY product_definition_context

SUBTYPE OF (application_context_element);

life_cycle_stage : label;

END_ENTITY;

ENTITY product_definition_context_association;

definition : product_definition;

frame_of_reference : product_definition_context;

role : product_definition_context_role;

END_ENTITY;

ENTITY product_definition_context_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY product_definition_effectivity

SUBTYPE OF (effectivity);

usage : product_definition_relationship;

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'EFFECTIVITY_ASSIGNMENT.ASSIGNED_EFFECTIVITY')) = 0;

END_ENTITY;

ENTITY product_definition_formation;

id : identifier;

description : OPTIONAL text;

of_product : product;

UNIQUE

UR1: id, of_product;

END_ENTITY;

ENTITY product_definition_formation_relationship;

id : identifier;

name : label;

description : OPTIONAL text;

relating_product_definition_formation : product_definition_formation;

related_product_definition_formation : product_definition_formation;

END_ENTITY;

ENTITY product_definition_formation_with_specified_source

SUBTYPE OF (product_definition_formation);

make_or_buy : source;

END_ENTITY;

ENTITY product_definition_relationship;

id : identifier;

name : label;

description : OPTIONAL text;

relating_product_definition : product_definition;

related_product_definition : product_definition;

END_ENTITY;

ENTITY product_definition_shape

SUBTYPE OF (property_definition);

UNIQUE

UR1: SELF\property_definition.definition;

WHERE

WR1: SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CHARACTERIZED_PRODUCT_DEFINITION', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CHARACTERIZED_OBJECT'] * TYPEOF(SELF\property_definition.definition)) > 0;

END_ENTITY;

ENTITY product_definition_usage

SUPERTYPE OF (ONEOF (

MAKE_FROM_USAGE_OPTION,

ASSEMBLY_COMPONENT_USAGE))

SUBTYPE OF (product_definition_relationship);

UNIQUE

UR1: SELF\product_definition_relationship.id,

SELF\product_definition_relationship.relating_product_definition,

SELF\product_definition_relationship.related_product_definition;

WHERE

WR1:  acyclic_product_definition_relationship

(SELF,

[SELF\product_definition_relationship.related_product_definition],

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION_USAGE');

END_ENTITY;

ENTITY product_definition_with_associated_documents

SUBTYPE OF (product_definition);

documentation_ids : SET[1:?] OF document;

END_ENTITY;

ENTITY product_related_product_category

SUBTYPE OF (product_category);

products : SET[1:?] OF product;

END_ENTITY;

ENTITY projected_zone_definition

SUBTYPE OF (tolerance_zone_definition);

projection_end   : shape_aspect;

projected_length : measure_with_unit;

WHERE

WR1: ('NUMBER' IN TYPEOF

(projected_length\measure_with_unit.value_component)) AND

(projected_length\measure_with_unit.value_component > 0.0);

WR2: (derive_dimensional_exponents

(projected_length\measure_with_unit.unit_component)=

dimensional_exponents(1,0,0,0,0,0,0));

END_ENTITY;

ENTITY projection_curve

SUBTYPE OF (annotation_curve_occurrence);

END_ENTITY;

ENTITY projection_directed_callout

SUBTYPE OF (draughting_callout);

WHERE

WR1: SIZEOF(QUERY(p_1<*SELF\draughting_callout.contents |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_CURVE' IN (TYPEOF(p_1))))=1;

WR2: SIZEOF(SELF\draughting_callout.contents) >=2;

END_ENTITY;

ENTITY promissory_usage_occurrence

SUBTYPE OF (assembly_component_usage);

END_ENTITY;

ENTITY property_definition;

name : label;

description : OPTIONAL text;

definition : characterized_definition;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY property_definition_representation;

definition : represented_definition;

used_representation : representation;

DERIVE

description : text := get_description_value (SELF);

name : label := get_name_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM')) <= 1;

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.NAMED_ITEM')) <= 1;

END_ENTITY;

ENTITY qualified_representation_item

SUBTYPE OF (representation_item);

qualifiers : SET [1:?] OF value_qualifier;

WHERE

WR1: SIZEOF(QUERY(temp <* qualifiers |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRECISION_QUALIFIER'

IN TYPEOF(temp))) < 2;

END_ENTITY;

ENTITY quantified_assembly_component_usage

SUBTYPE OF (assembly_component_usage);

quantity   : measure_with_unit;

WHERE

WR1: (NOT ('NUMBER' IN TYPEOF(quantity.value_component)))

OR (quantity.value_component > 0);

END_ENTITY;

ENTITY quasi_uniform_curve

SUBTYPE OF (b_spline_curve);

END_ENTITY;

ENTITY quasi_uniform_surface

SUBTYPE OF (b_spline_surface);

END_ENTITY;

ENTITY radius_dimension

SUBTYPE OF (dimension_curve_directed_callout);

WHERE

WR1: SIZEOF (QUERY (con <* SELF.contents |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_CURVE' IN TYPEOF (con)))<=1;

END_ENTITY;

ENTITY ratio_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RATIO_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY ratio_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY rational_b_spline_curve

SUBTYPE OF (b_spline_curve);

weights_data : LIST [2:?] OF REAL;

DERIVE

weights           : ARRAY [0:upper_index_on_control_points] OF REAL

:= list_to_array(weights_data,0,

upper_index_on_control_points);

WHERE

WR1:  SIZEOF(weights_data) = SIZEOF(SELF\b_spline_curve.

control_points_list);

WR2:  curve_weights_positive(SELF);

END_ENTITY;

ENTITY rational_b_spline_surface

SUBTYPE OF (b_spline_surface);

weights_data : LIST [2:?] OF

LIST [2:?] OF REAL;

DERIVE

weights       : ARRAY [0:u_upper] OF

ARRAY [0:v_upper] OF REAL

:= make_array_of_array(weights_data,0,u_upper,0,v_upper);

WHERE

WR1: (SIZEOF(weights_data) =

SIZEOF(SELF\b_spline_surface.control_points_list))

AND (SIZEOF(weights_data[1]) =

SIZEOF(SELF\b_spline_surface.control_points_list[1]));

WR2: surface_weights_positive(SELF);

END_ENTITY;

ENTITY rectangular_composite_surface

SUBTYPE OF (bounded_surface);

segments      : LIST [1:?] OF LIST [1:?] OF surface_patch;

DERIVE

n_u : INTEGER := SIZEOF(segments);

n_v : INTEGER := SIZEOF(segments[1]);

WHERE

WR1: SIZEOF(QUERY (s <* segments | n_v <> SIZEOF (s))) = 0;

WR2: constraints_rectangular_composite_surface(SELF);

END_ENTITY;

ENTITY rectangular_trimmed_surface

SUBTYPE OF (bounded_surface);

basis_surface : surface;

u1            : parameter_value;

u2            : parameter_value;

v1            : parameter_value;

v2            : parameter_value;

usense        : BOOLEAN;

vsense        : BOOLEAN;

WHERE

WR1: u1 <> u2;

WR2: v1 <> v2;

WR3: (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELEMENTARY_SURFACE' IN TYPEOF(basis_surface))

AND  (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLANE' IN TYPEOF(basis_surface)))) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_OF_REVOLUTION' IN TYPEOF(basis_surface))

OR (usense = (u2 > u1));

WR4: (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SPHERICAL_SURFACE' IN TYPEOF(basis_surface))

OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TOROIDAL_SURFACE' IN TYPEOF(basis_surface)))

OR (vsense = (v2 > v1));

END_ENTITY;

ENTITY referenced_modified_datum

SUBTYPE OF (datum_reference);

modifier : limit_condition;

END_ENTITY;

ENTITY relative_event_occurrence

SUBTYPE OF (event_occurrence);

base_event : event_occurrence;

offset : time_measure_with_unit;

END_ENTITY;

ENTITY reparametrised_composite_curve_segment

SUBTYPE OF (composite_curve_segment);

param_length : parameter_value;

WHERE

WR1: param_length > 0.0;

END_ENTITY;

ENTITY representation;

name             : label;

items            : SET[1:?] OF representation_item;

context_of_items : representation_context;

DERIVE

id               : identifier := get_id_value (SELF);

description      : text := get_description_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'ID_ATTRIBUTE.IDENTIFIED_ITEM'))

<= 1;

WR2: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DESCRIPTION_ATTRIBUTE.DESCRIBED_ITEM'))

<= 1;

END_ENTITY;

ENTITY representation_context;

context_identifier : identifier;

context_type       : text;

INVERSE

representations_in_context : SET [1:?] OF representation

FOR context_of_items;

END_ENTITY;

ENTITY representation_item;

name : label;

WHERE

WR1: SIZEOF(using_representations(SELF)) > 0;

END_ENTITY;

ENTITY representation_map;

mapping_origin        : representation_item;

mapped_representation : representation;

INVERSE

map_usage : SET[1:?] OF mapped_item FOR mapping_source;

WHERE

WR1: item_in_context(SELF.mapping_origin,

SELF.mapped_representation.context_of_items);

END_ENTITY;

ENTITY representation_relationship;

name        : label;

description : OPTIONAL text;

rep_1       : representation;

rep_2       : representation;

END_ENTITY;

ENTITY representation_relationship_with_transformation

SUBTYPE OF (representation_relationship);

transformation_operator : transformation;

WHERE

WR1:

SELF\representation_relationship.rep_1.context_of_items

:<>: SELF\representation_relationship.rep_2.context_of_items;

END_ENTITY;

ENTITY revolved_face_solid

SUBTYPE OF (swept_face_solid);

axis  : axis1_placement;

angle : plane_angle_measure;

DERIVE

axis_line : line := representation_item('')||

geometric_representation_item()|| curve()||

line(axis.location, representation_item('')||

geometric_representation_item()||

vector(axis.z, 1.0));

END_ENTITY;

ENTITY right_angular_wedge

SUBTYPE OF (geometric_representation_item);

position : axis2_placement_3d;

x        : positive_length_measure;

y        : positive_length_measure;

z        : positive_length_measure;

ltx      : length_measure;

WHERE

WR1: ((0.0 <= ltx) AND (ltx < x));

END_ENTITY;

ENTITY right_circular_cone

SUBTYPE OF (geometric_representation_item);

position   : axis1_placement;

height     : positive_length_measure;

radius     : length_measure;

semi_angle : plane_angle_measure;

WHERE

WR1: radius >= 0.0;

END_ENTITY;

ENTITY right_circular_cylinder

SUBTYPE OF (geometric_representation_item);

position   : axis1_placement;

height     : positive_length_measure;

radius     : positive_length_measure;

END_ENTITY;

ENTITY role_association;

role : object_role;

item_with_role : role_select;

END_ENTITY;

ENTITY roundness_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY runout_zone_definition

SUBTYPE OF (tolerance_zone_definition);

orientation  : runout_zone_orientation;

END_ENTITY;

ENTITY runout_zone_orientation;

angle : measure_with_unit;

END_ENTITY;

ENTITY runout_zone_orientation_reference_direction

SUBTYPE OF (runout_zone_orientation);

orientation_defining_relationship: shape_aspect_relationship;

END_ENTITY;

ENTITY seam_curve

SUBTYPE OF (surface_curve);

WHERE

WR1: SIZEOF(SELF\surface_curve.associated_geometry) = 2;

WR2: associated_surface(SELF\surface_curve.associated_geometry[1]) =

associated_surface(SELF\surface_curve.associated_geometry[2]);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN

TYPEOF(SELF\surface_curve.associated_geometry[1]);

WR4: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN

TYPEOF(SELF\surface_curve.associated_geometry[2]);

END_ENTITY;

ENTITY security_classification;

name : label;

purpose : text;

security_level : security_classification_level;

END_ENTITY;

ENTITY security_classification_assignment

ABSTRACT SUPERTYPE;

assigned_security_classification : security_classification;

DERIVE

role : object_role := get_role (SELF);

WHERE

WR1: SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.ITEM_WITH_ROLE')) <= 1;

END_ENTITY;

ENTITY security_classification_level;

name : label;

END_ENTITY;

ENTITY serial_numbered_effectivity

SUBTYPE OF (effectivity);

effectivity_start_id : identifier;

effectivity_end_id : OPTIONAL identifier;

END_ENTITY;

ENTITY shape_aspect;

name : label;

description : OPTIONAL text;

of_shape : product_definition_shape;

product_definitional : LOGICAL;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY shape_aspect_associativity

SUBTYPE OF (shape_aspect_relationship);

WHERE

WR1:  SELF.relating_shape_aspect.product_definitional;

WR2:  NOT (SELF.related_shape_aspect.product_definitional);

WR3:  SIZEOF (QUERY (pd <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PROPERTY_DEFINITION.DEFINITION') |

NOT (SIZEOF (QUERY (sdr <* QUERY (pdr <* USEDIN (pd,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PROPERTY_DEFINITION_REPRESENTATION.DEFINITION') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_DEFINITION_REPRESENTATION'

IN TYPEOF (pdr))) |

NOT (SIZEOF (QUERY (it <* sdr.used_representation.items |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF(it))

AND

(SIZEOF (QUERY (aco <* USEDIN (it,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STYLED_ITEM.ITEM') |

SIZEOF (TYPEOF (aco) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_CURVE']) = 1)) +

SIZEOF (USEDIN (it, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'ANNOTATION_FILL_AREA.BOUNDARIES')) >= 1)

)) = 1)

)) = 0)

)) = 0;

WR4:  SIZEOF (QUERY (pd <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PROPERTY_DEFINITION.DEFINITION') |

NOT (SIZEOF (QUERY (sdr <* QUERY (pdr <* USEDIN (pd,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PROPERTY_DEFINITION_REPRESENTATION.DEFINITION') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_DEFINITION_REPRESENTATION'

IN TYPEOF (pdr))) |

NOT (check_associative_shape_aspects(sdr))

)) = 0)

)) = 0;

END_ENTITY;

ENTITY shape_aspect_deriving_relationship

SUBTYPE OF (shape_aspect_relationship);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DERIVED_SHAPE_ASPECT' IN

TYPEOF

(SELF\SHAPE_ASPECT_RELATIONSHIP.RELATING_SHAPE_ASPECT);

END_ENTITY;

ENTITY shape_aspect_relationship;

name : label;

description : OPTIONAL text;

relating_shape_aspect : shape_aspect;

related_shape_aspect : shape_aspect;

DERIVE

id : identifier := get_id_value (SELF);

WHERE

WR1: SIZEOF (USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.IDENTIFIED_ITEM')) <= 1;

END_ENTITY;

ENTITY shape_definition_representation

SUBTYPE OF (property_definition_representation);

WHERE

WR1: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION_SHAPE' IN TYPEOF (SELF.definition)) OR ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_DEFINITION' IN TYPEOF (SELF.definition.definition));

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION' IN TYPEOF(SELF.used_representation);

END_ENTITY;

ENTITY shape_dimension_representation

SUBTYPE OF (shape_representation);

WHERE

WR1: SIZEOF (QUERY (temp <* SELF\representation.items |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM'

IN TYPEOF (temp)))) = 0;

WR2: SIZEOF (SELF\representation.items) <= 3;

WR3: SIZEOF (QUERY (pos_mri <* QUERY (real_mri <*

SELF\representation.items | 'REAL' IN TYPEOF

(real_mri\measure_with_unit.value_component) ) |

NOT  (pos_mri\measure_with_unit.value_component > 0.0 ))) = 0;

END_ENTITY;

ENTITY shape_representation

SUBTYPE OF (representation);

END_ENTITY;

ENTITY shape_representation_relationship

SUBTYPE OF (representation_relationship);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION' IN (TYPEOF(SELF\representation_relationship.rep_1) + TYPEOF(SELF\representation_relationship.rep_2));

END_ENTITY;

ENTITY shape_representation_with_parameters

SUBTYPE OF (shape_representation);

WHERE

WR1: SIZEOF( QUERY( i <* SELF.items | SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLACEMENT', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DESCRIPTIVE_REPRESENTATION_ITEM'] * TYPEOF(i)) = 1 )) = SIZEOF(SELF.items);

END_ENTITY;

ENTITY shell_based_surface_model

SUBTYPE OF (geometric_representation_item);

sbsm_boundary  : SET [1:?] OF shell;

WHERE

WR1: constraints_geometry_shell_based_surface_model(SELF);

END_ENTITY;

ENTITY shell_based_wireframe_model

SUBTYPE OF (geometric_representation_item);

sbwm_boundary  : SET [1:?] OF shell;

WHERE

WR1: constraints_geometry_shell_based_wireframe_model(SELF);

END_ENTITY;

ENTITY shell_based_wireframe_shape_representation

SUBTYPE OF ( shape_representation );

WHERE

WR1 :

SIZEOF (

QUERY ( it <* SELF.items| NOT ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT_3D' ] * TYPEOF (it)) = 1) )) = 0;

WR2 :

SIZEOF (

QUERY ( it <* SELF.items| ( SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' ] * TYPEOF (it)) = 1) )) >= 1;

WR3 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( eloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (wsb)) )| NOT ( SIZEOF (

QUERY ( el <* eloop\path.edge_list| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_CURVE' IN TYPEOF (el.edge_element)) )) = 0) )) = 0) )) = 0) )) = 0;

WR4 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( eloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (wsb)) )| NOT ( SIZEOF (

QUERY ( pline_el <*

QUERY ( el <* eloop\path.edge_list| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF (el.edge_element\edge_curve.edge_geometry)) )| NOT ( SIZEOF (pline_el.edge_element\edge_curve.edge_geometry\polyline.points) > 2) )) = 0) )) = 0) )) = 0) )) = 0;

WR5 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( eloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (wsb)) )| NOT ( SIZEOF (

QUERY ( el <* eloop\path.edge_list| NOT valid_wireframe_edge_curve(el.edge_element\edge_curve.edge_geometry) )) = 0) )) = 0) )) = 0) )) = 0;

WR6 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( eloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (wsb)) )| NOT ( SIZEOF (

QUERY ( el <* eloop\path.edge_list| NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (el.edge_element.edge_start)) AND ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (el.edge_element.edge_end))) )) = 0) )) = 0) )) = 0) )) = 0;

WR7 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( eloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE_LOOP' IN TYPEOF (wsb)) )| NOT ( SIZEOF (

QUERY ( el <* eloop\path.edge_list| NOT (valid_wireframe_vertex_point(el.edge_element.edge_start\vertex_point.vertex_geometry) AND valid_wireframe_vertex_point(el.edge_element.edge_end\vertex_point.vertex_geometry)) )) = 0) )) = 0) )) = 0) )) = 0;

WR8 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( vloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP' IN TYPEOF (wsb)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (vloop\vertex_loop.loop_vertex)) )) = 0) )) = 0) )) = 0;

WR9 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( ws <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN TYPEOF (sb)) )| NOT ( SIZEOF (

QUERY ( vloop <*

QUERY ( wsb <* ws\wire_shell.wire_shell_extent| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_LOOP' IN TYPEOF (wsb)) )| NOT valid_wireframe_vertex_point(vloop\vertex_loop.loop_vertex\vertex_point.vertex_geometry) )) = 0) )) = 0) )) = 0;

WR10 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( vs <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_SHELL' IN TYPEOF (sb)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_POINT' IN TYPEOF (vs\vertex_shell.vertex_shell_extent.loop_vertex)) )) = 0) )) = 0;

WR11 :

SIZEOF (

QUERY ( sbwm <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL_BASED_WIREFRAME_MODEL' IN TYPEOF (it)) )| NOT ( SIZEOF (

QUERY ( vs <*

QUERY ( sb <* sbwm\shell_based_wireframe_model.sbwm_boundary| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_SHELL' IN TYPEOF (sb)) )| NOT valid_wireframe_vertex_point(vs\vertex_shell.vertex_shell_extent.loop_vertex\vertex_point.vertex_geometry) )) = 0) )) = 0;

WR12 :

SIZEOF (

QUERY ( mi <*

QUERY ( it <* SELF.items| ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (it)) )| NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'SHELL_BASED_WIREFRAME_SHAPE_REPRESENTATION' IN TYPEOF (mi\mapped_item.mapping_source.mapped_representation)) )) = 0;

WR13 : SELF.context_of_items\geometric_representation_context.coordinate_space_dimension = 3;

END_ENTITY;

ENTITY si_unit

SUBTYPE OF (named_unit);

prefix : OPTIONAL si_prefix;

name : si_unit_name;

DERIVE

SELF\named_unit.dimensions : dimensional_exponents := dimensions_for_si_unit (name);

END_ENTITY;

ENTITY solid_angle_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SOLID_ANGLE_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY solid_angle_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY solid_model

SUPERTYPE OF (ONEOF (

CSG_SOLID,

MANIFOLD_SOLID_BREP,

SWEPT_FACE_SOLID,

SOLID_REPLICA))

SUBTYPE OF (geometric_representation_item);

END_ENTITY;

ENTITY solid_replica

SUBTYPE OF (solid_model);

parent_solid   : solid_model;

transformation : cartesian_transformation_operator_3d;

WHERE

WR1: acyclic_solid_replica(SELF, parent_solid);

WR2: parent_solid\geometric_representation_item.dim = 3;

END_ENTITY;

ENTITY specified_higher_usage_occurrence

SUBTYPE OF (assembly_component_usage);

upper_usage   : assembly_component_usage;

next_usage    : next_assembly_usage_occurrence;

UNIQUE

UR1: upper_usage, next_usage;

WHERE

WR1: SELF :<>: upper_usage;

WR2: SELF\product_definition_relationship.relating_product_definition

:=: upper_usage.relating_product_definition;

WR3: SELF\product_definition_relationship.related_product_definition

:=: next_usage.related_product_definition;

WR4: (upper_usage.related_product_definition :=:

next_usage.relating_product_definition) OR

(SIZEOF (QUERY (pdr <* USEDIN (upper_usage.related_product_definition,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRODUCT_DEFINITION_RELATIONSHIP.' +

'RELATED_PRODUCT_DEFINITION') |

pdr.relating_product_definition :=:

next_usage.relating_product_definition)) = 1);

WR5: SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.NEXT_ASSEMBLY_USAGE_OCCURRENCE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SPECIFIED_HIGHER_USAGE_OCCURRENCE']

* TYPEOF(upper_usage)) = 1;

END_ENTITY;

ENTITY sphere

SUBTYPE OF (geometric_representation_item);

radius : positive_length_measure;

centre : point;

END_ENTITY;

ENTITY spherical_surface

SUBTYPE OF (elementary_surface);

radius   : positive_length_measure;

END_ENTITY;

ENTITY standard_uncertainty

SUBTYPE OF (uncertainty_qualifier);

uncertainty_value : REAL;

END_ENTITY;

ENTITY start_request

SUBTYPE OF (action_request_assignment);

items : SET[1:?] OF change_request_item;

END_ENTITY;

ENTITY start_work

SUBTYPE OF (action_assignment);

items : SET[1:?] OF work_item;

END_ENTITY;

ENTITY straightness_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF));

END_ENTITY;

ENTITY structured_dimension_callout

SUBTYPE OF (draughting_callout);

WHERE

WR1: SIZEOF (TYPEOF (SELF) *

['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM_FEATURE_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DATUM_TARGET_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GEOMETRICAL_TOLERANCE_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LEADER_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROJECTION_DIRECTED_CALLOUT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIMENSION_CURVE_DIRECTED_CALLOUT']) = 0;

WR2: SIZEOF (QUERY (ato <* QUERY (con <* SELF.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (con))) |

NOT (ato.name IN

['dimension value', 'tolerance value', 'unit text',

'prefix text', 'suffix text']))) = 0;

WR3: SIZEOF (QUERY (ato <* QUERY (con <* SELF.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (con))) |

(ato.name = 'dimension value')

)) >= 1;

WR4: SIZEOF (QUERY (dcr <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT_RELATIONSHIP.' +

'RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_COMPONENT_RELATIONSHIP' IN TYPEOF (dcr)) AND

(dcr.name = 'prefix') )) <= 1;

WR5: SIZEOF (QUERY (dcr <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT_RELATIONSHIP.' +

'RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_COMPONENT_RELATIONSHIP' IN TYPEOF (dcr)) AND

(dcr.name = 'suffix') )) <= 1;

WR6: NOT((SIZEOF (QUERY (ato <* QUERY (con <* SELF.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(con)) ) |

(ato.name = 'prefix text')

)) > 0)) OR

(SIZEOF (QUERY (dcr <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT_RELATIONSHIP.' +

'RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_COMPONENT_RELATIONSHIP' IN TYPEOF (dcr)) AND

(dcr.name = 'prefix') )) = 1);

WR7: NOT(SIZEOF (QUERY (ato <* QUERY (con <* SELF.contents |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF(con))) |

(ato.name = 'suffix text')

)) > 0) OR

(SIZEOF (QUERY (dcr <* USEDIN (SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DRAUGHTING_CALLOUT_RELATIONSHIP.' +

'RELATING_DRAUGHTING_CALLOUT') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'DIMENSION_CALLOUT_COMPONENT_RELATIONSHIP' IN TYPEOF (dcr)) AND

(dcr.name = 'suffix') )) = 1);

END_ENTITY;

ENTITY styled_item

SUBTYPE OF (representation_item);

styles :  SET [1:?] OF presentation_style_assignment;

item   :  representation_item;

WHERE

WR1: (SIZEOF(SELF.styles) = 1)

XOR

(SIZEOF(QUERY(pres_style <* SELF.styles |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'PRESENTATION_STYLE_BY_CONTEXT' IN

TYPEOF(pres_style))

)) = 0);

END_ENTITY;

ENTITY supplied_part_relationship

SUBTYPE OF (product_definition_relationship);

END_ENTITY;

ENTITY surface

SUPERTYPE OF (ONEOF (

ELEMENTARY_SURFACE,

SWEPT_SURFACE,

BOUNDED_SURFACE,

OFFSET_SURFACE,

SURFACE_REPLICA))

SUBTYPE OF (geometric_representation_item);

END_ENTITY;

ENTITY surface_curve

SUPERTYPE OF (ONEOF (

INTERSECTION_CURVE,

SEAM_CURVE)

ANDOR

BOUNDED_SURFACE_CURVE)

SUBTYPE OF (curve);

curve_3d              : curve;

associated_geometry   : LIST[1:2] OF pcurve_or_surface;

master_representation : preferred_surface_curve_representation;

DERIVE

basis_surface         : SET[1:2] OF surface

:= get_basis_surface(SELF);

WHERE

WR1: curve_3d.dim = 3;

WR2: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(associated_geometry[1])) OR

(master_representation <> pcurve_s1);

WR3: ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(associated_geometry[2])) OR

(master_representation <> pcurve_s2);

WR4: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(curve_3d));

END_ENTITY;

ENTITY surface_of_linear_extrusion

SUBTYPE OF (swept_surface);

extrusion_axis      : vector;

END_ENTITY;

ENTITY surface_of_revolution

SUBTYPE OF (swept_surface);

axis_position       : axis1_placement;

DERIVE

axis_line : line := representation_item('')||

geometric_representation_item()|| curve()||

line(axis_position.location, representation_item('')||

geometric_representation_item()||

vector(axis_position.z, 1.0));

END_ENTITY;

ENTITY surface_patch

SUBTYPE OF (founded_item);

parent_surface : bounded_surface;

u_transition   : transition_code;

v_transition   : transition_code;

u_sense        : BOOLEAN;

v_sense        : BOOLEAN;

INVERSE

using_surfaces : BAG[1:?] OF rectangular_composite_surface FOR segments;

WHERE

WR1: (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_BOUNDED_SURFACE'

IN TYPEOF(parent_surface)));

END_ENTITY;

ENTITY surface_profile_tolerance

SUBTYPE OF ( geometric_tolerance );

WHERE

WR1 : NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'GEOMETRIC_TOLERANCE_WITH_DATUM_REFERENCE' IN TYPEOF (SELF)) OR ( SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3);

END_ENTITY;

ENTITY surface_replica

SUBTYPE OF (surface);

parent_surface : surface;

transformation : cartesian_transformation_operator_3d;

WHERE

WR1: acyclic_surface_replica(SELF, parent_surface);

END_ENTITY;

ENTITY surface_side_style;

name   : label;

styles : SET [1:7] OF surface_style_element_select;

WHERE

WR1: SIZEOF(QUERY( style1 <* SELF.styles |

SIZEOF(QUERY( style2 <* SELF.styles - style1 |

TYPEOF(style1) = TYPEOF(style2)

)) > 0

)) = 0;

END_ENTITY;

ENTITY surface_style_boundary;

style_of_boundary : curve_or_render;

END_ENTITY;

ENTITY surface_style_control_grid;

style_of_control_grid : curve_or_render;

END_ENTITY;

ENTITY surface_style_fill_area;

fill_area : fill_area_style;

END_ENTITY;

ENTITY surface_style_parameter_line;

style_of_parameter_lines : curve_or_render;

direction_counts         : SET [1:2] OF direction_count_select;

WHERE

WR1: (HIINDEX(SELF.direction_counts) = 1)

XOR

(TYPEOF(SELF.direction_counts[1]) <>

TYPEOF(SELF.direction_counts[2]));

END_ENTITY;

ENTITY surface_style_segmentation_curve;

style_of_segmentation_curve : curve_or_render;

END_ENTITY;

ENTITY surface_style_silhouette;

style_of_silhouette : curve_or_render;

END_ENTITY;

ENTITY surface_style_usage;

side  : surface_side;

style : surface_side_style_select;

END_ENTITY;

ENTITY swept_face_solid

SUPERTYPE OF (ONEOF (

EXTRUDED_FACE_SOLID,

REVOLVED_FACE_SOLID))

SUBTYPE OF (solid_model);

swept_face :  face_surface;

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLANE' IN TYPEOF(swept_face.face_geometry);

END_ENTITY;

ENTITY swept_surface

SUPERTYPE OF (ONEOF (

SURFACE_OF_LINEAR_EXTRUSION,

SURFACE_OF_REVOLUTION))

SUBTYPE OF (surface);

swept_curve : curve;

END_ENTITY;

ENTITY symbol_colour;

colour_of_symbol : colour;

END_ENTITY;

ENTITY symbol_representation

SUBTYPE OF (representation);

END_ENTITY;

ENTITY symbol_representation_map

SUBTYPE OF (representation_map);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_REPRESENTATION' IN

TYPEOF (SELF\representation_map.mapped_representation);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT' IN

TYPEOF (SELF\representation_map.mapping_origin);

END_ENTITY;

ENTITY symbol_representation_relationship

SUBTYPE OF (representation_relationship_with_transformation);

WHERE

WR1: acyclic_symbol_representation_relationship (SELF,

[SELF\representation_relationship.

rep_2]);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_1);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMBOL_REPRESENTATION'IN

TYPEOF (SELF\representation_relationship.rep_2);

END_ENTITY;

ENTITY symbol_representation_with_blanking_box

SUBTYPE OF (symbol_representation);

blanking : planar_box;

WHERE

WR1: item_in_context (SELF.blanking, SELF\representation.context_of_items);

END_ENTITY;

ENTITY symbol_style;

name            : label;

style_of_symbol : symbol_style_select;

END_ENTITY;

ENTITY symbol_target

SUBTYPE OF (geometric_representation_item);

placement         : axis2_placement;

x_scale           : positive_ratio_measure;

y_scale           : positive_ratio_measure;

END_ENTITY;

ENTITY symmetric_shape_aspect

SUBTYPE OF (shape_aspect);

INVERSE

basis_relationships : SET [1:?] OF shape_aspect_relationship

FOR relating_shape_aspect;

WHERE

WR1: SIZEOF (QUERY (x<*SELF\symmetric_shape_aspect.basis_relationships |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CENTRE_OF_SYMMETRY' IN TYPEOF

(x\shape_aspect_relationship.related_shape_aspect)))>=1;

END_ENTITY;

ENTITY symmetry_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 3;

END_ENTITY;

ENTITY table_record_field_representation

SUBTYPE OF (symbol_representation);

WHERE

WR1: (SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_RELATIONSHIP.REP_2')) > 0)

OR

(SIZEOF(QUERY( map_item <* USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_MAP.'+

'MAPPED_REPRESENTATION') |

SIZEOF(QUERY( mi <* USEDIN(map_item, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'MAPPED_ITEM.'+

'MAPPING_SOURCE') |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'TABLE_RECORD_REPRESENTATION' IN

TYPEOF (using_representations (mi)) )) > 0))

> 0);

END_ENTITY;

ENTITY table_record_field_representation_with_clipping_box

SUBTYPE OF (table_record_field_representation);

clipping_box : planar_box;

WHERE

WR1: item_in_context (SELF.clipping_box,

SELF\representation.context_of_items);

END_ENTITY;

ENTITY table_record_representation

SUBTYPE OF (symbol_representation);

WHERE

WR1: (SIZEOF(USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_RELATIONSHIP.REP_2')) > 0)

OR

(SIZEOF(QUERY( map_item <* USEDIN(SELF, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_MAP.'+

'MAPPED_REPRESENTATION') |

SIZEOF(QUERY( mi <* USEDIN(map_item, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'MAPPED_ITEM.'+

'MAPPING_SOURCE') |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'TABLE_REPRESENTATION' IN

TYPEOF (using_representations (mi)) )) > 0))

> 0);

END_ENTITY;

ENTITY table_representation

SUBTYPE OF (symbol_representation);

END_ENTITY;

ENTITY table_representation_relationship

SUBTYPE OF (symbol_representation_relationship);

WHERE

WR1: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_RECORD_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_1))

XOR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_RECORD_FIELD_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_2));

WR2: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_1))

XOR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_RECORD_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_2));

WR3: NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_RECORD_FIELD_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_1))

XOR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TABLE_RECORD_FIELD_REPRESENTATION' IN

TYPEOF (SELF\representation_relationship.rep_2));

END_ENTITY;

ENTITY table_text_relationship

SUBTYPE OF (annotation_occurrence_relationship);

field : table_record_field_representation;

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TABLE_OCCURRENCE'

IN TYPEOF (SELF\annotation_occurrence_relationship.

relating_annotation_occurrence);

WR2: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TABLE'

IN TYPEOF (SELF\annotation_occurrence_relationship.

relating_annotation_occurrence\styled_item.item);

WR3: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_OCCURRENCE'

IN TYPEOF (SELF\annotation_occurrence_relationship.

related_annotation_occurrence);

WR4: field_in_table (SELF.field,

SELF\annotation_occurrence_relationship.

relating_annotation_occurrence);

END_ENTITY;

ENTITY tangent

SUBTYPE OF (derived_shape_aspect);

WHERE

WR1: SIZEOF (SELF\derived_shape_aspect.deriving_relationships)= 1;

END_ENTITY;

ENTITY terminator_symbol

SUBTYPE OF (annotation_symbol_occurrence);

annotated_curve : annotation_curve_occurrence;

END_ENTITY;

ENTITY text_literal

SUBTYPE OF (geometric_representation_item);

literal   : presentable_text;

placement : axis2_placement;

alignment : text_alignment;

path      : text_path;

font      : font_select;

END_ENTITY;

ENTITY text_literal_with_associated_curves

SUBTYPE OF (text_literal);

associated_curves : SET[1:?] of curve;

END_ENTITY;

ENTITY text_literal_with_blanking_box

SUBTYPE OF (text_literal);

blanking : planar_box;

END_ENTITY;

ENTITY text_literal_with_delineation

SUBTYPE OF (text_literal);

delineation : text_delineation;

END_ENTITY;

ENTITY text_literal_with_extent

SUBTYPE OF (text_literal);

extent : planar_extent;

END_ENTITY;

ENTITY text_string_representation

SUBTYPE OF (representation);

WHERE

WR1: SIZEOF (

QUERY (item <* SELF\representation.items |

SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_CHARACTER',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEFINED_CHARACTER_GLYPH',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT'] * TYPEOF (item)) = 0

)) = 0;

WR2: SIZEOF (

QUERY (item <* SELF\representation.items |

NOT (SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT_CHARACTER',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEFINED_CHARACTER_GLYPH',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'] *

TYPEOF (item)) = 0)

)) >= 1;

WR3: SIZEOF (

QUERY (a2p <*

QUERY (item <* SELF\representation.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AXIS2_PLACEMENT' IN TYPEOF (item)) |

NOT ((SIZEOF (

QUERY (at <*

QUERY (item <* SELF\representation.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'ANNOTATION_TEXT' IN TYPEOF (item)) |

(at\mapped_item.mapping_target :=: a2p))) >= 1) OR

(SIZEOF (

QUERY (atc <*

QUERY (item <* SELF\representation.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'ANNOTATION_TEXT_CHARACTER' IN TYPEOF (item)) |

(atc\mapped_item.mapping_target :=: a2p))) >= 1)

))) = 0;

END_ENTITY;

ENTITY text_style;

name                 : label;

character_appearance : character_style_select;

END_ENTITY;

ENTITY text_style_for_defined_font;

text_colour : colour;

END_ENTITY;

ENTITY text_style_with_box_characteristics

SUBTYPE OF (text_style);

characteristics : SET [1:4] OF box_characteristic_select;

WHERE

WR1: SIZEOF( QUERY( c1 <* SELF.characteristics |

SIZEOF( QUERY( c2 <* SELF.characteristics - c1 |

TYPEOF (c1) = TYPEOF (c2)

)) > 0

)) = 0;

END_ENTITY;

ENTITY text_style_with_mirror

SUBTYPE OF (text_style);

mirror_placement : axis2_placement;

END_ENTITY;

ENTITY text_style_with_spacing

SUBTYPE OF (text_style);

character_spacing : character_spacing_select;

END_ENTITY;

ENTITY thermodynamic_temperature_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.THERMODYNAMIC_TEMPERATURE_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY thermodynamic_temperature_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 0.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 1.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY time_interval;

id : identifier;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY time_interval_assignment

ABSTRACT SUPERTYPE;

assigned_time_interval : time_interval;

role : time_interval_role;

END_ENTITY;

ENTITY time_interval_based_effectivity

SUBTYPE OF (effectivity);

effectivity_period : time_interval;

END_ENTITY;

ENTITY time_interval_relationship;

name : label;

description : OPTIONAL text;

relating_time_interval : time_interval;

related_time_interval : time_interval;

END_ENTITY;

ENTITY time_interval_role;

name : label;

description : OPTIONAL text;

END_ENTITY;

ENTITY time_interval_with_bounds

SUBTYPE OF (time_interval);

primary_bound : OPTIONAL date_time_or_event_occurrence;

secondary_bound : OPTIONAL date_time_or_event_occurrence;

duration : OPTIONAL time_measure_with_unit;

WHERE

WR1: NOT (EXISTS(secondary_bound) AND EXISTS(duration));

WR2: EXISTS(primary_bound) OR EXISTS(secondary_bound);

END_ENTITY;

ENTITY time_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TIME_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY time_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 0.0) AND (SELF\named_unit.dimensions.mass_exponent = 0.0) AND (SELF\named_unit.dimensions.time_exponent = 1.0) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.0) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.0) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.0) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.0);

END_ENTITY;

ENTITY tolerance_value;

lower_bound : measure_with_unit;

upper_bound : measure_with_unit;

WHERE

WR1: upper_bound\measure_with_unit.value_component >

lower_bound\measure_with_unit.value_component;

WR2: upper_bound\measure_with_unit.unit_component =

lower_bound\measure_with_unit.unit_component;

END_ENTITY;

ENTITY tolerance_zone

SUBTYPE OF (shape_aspect);

defining_tolerance : SET [1:?] OF geometric_tolerance;

form               : tolerance_zone_form;

END_ENTITY;

ENTITY tolerance_zone_definition

SUPERTYPE OF (ONEOF (

PROJECTED_ZONE_DEFINITION,

RUNOUT_ZONE_DEFINITION));

zone : tolerance_zone;

boundaries: SET [1:?] OF shape_aspect;

END_ENTITY;

ENTITY tolerance_zone_form;

name : label;

END_ENTITY;

ENTITY topological_representation_item

SUPERTYPE OF (ONEOF (

VERTEX,

EDGE,

FACE_BOUND,

FACE,

VERTEX_SHELL,

WIRE_SHELL,

CONNECTED_EDGE_SET,

CONNECTED_FACE_SET,(

LOOP

ANDOR

PATH)))

SUBTYPE OF (representation_item);

END_ENTITY;

ENTITY toroidal_surface

SUBTYPE OF (elementary_surface);

major_radius : positive_length_measure;

minor_radius : positive_length_measure;

END_ENTITY;

ENTITY torus

SUBTYPE OF (geometric_representation_item);

position     : axis1_placement;

major_radius : positive_length_measure;

minor_radius : positive_length_measure;

WHERE

WR1: major_radius > minor_radius;

END_ENTITY;

ENTITY total_runout_tolerance

SUBTYPE OF ( geometric_tolerance_with_datum_reference );

WHERE

WR1 :

SIZEOF (SELF\geometric_tolerance_with_datum_reference.datum_system) <= 2;

END_ENTITY;

ENTITY trimmed_curve

SUBTYPE OF (bounded_curve);

basis_curve           : curve;

trim_1                : SET[1:2] OF trimming_select;

trim_2                : SET[1:2] OF trimming_select;

sense_agreement       : BOOLEAN;

master_representation : trimming_preference;

WHERE

WR1: (HIINDEX(trim_1) = 1) OR (TYPEOF(trim_1[1]) <> TYPEOF(trim_1[2]));

WR2: (HIINDEX(trim_2) = 1) OR (TYPEOF(trim_2[1]) <> TYPEOF(trim_2[2]));

END_ENTITY;

ENTITY two_direction_repeat_factor

SUBTYPE OF (one_direction_repeat_factor);

second_repeat_factor : vector;

END_ENTITY;

ENTITY type_qualifier;

name : label;

END_ENTITY;

ENTITY uncertainty_assigned_representation

SUBTYPE OF (representation);

uncertainty : SET [1:?] OF uncertainty_measure_with_unit;

END_ENTITY;

ENTITY uncertainty_measure_with_unit

SUBTYPE OF (measure_with_unit);

name        : label;

description : OPTIONAL text;

WHERE

WR1: valid_measure_value (SELF\measure_with_unit.value_component);

END_ENTITY;

ENTITY uncertainty_qualifier

;

measure_name : label;

description  : text;

END_ENTITY;

ENTITY uniform_curve

SUBTYPE OF (b_spline_curve);

END_ENTITY;

ENTITY uniform_surface

SUBTYPE OF (b_spline_surface);

END_ENTITY;

ENTITY user_defined_curve_font

SUBTYPE OF (curve_style_font, mapped_item);

END_ENTITY;

ENTITY user_defined_marker

SUBTYPE OF (mapped_item, pre_defined_marker);

END_ENTITY;

ENTITY user_defined_terminator_symbol

SUBTYPE OF (mapped_item, pre_defined_symbol);

END_ENTITY;

ENTITY value_range

SUBTYPE OF (compound_representation_item);

WHERE

WR1: ( 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+ 'SET_REPRESENTATION_ITEM' IN TYPEOF ( item_element ) ) AND value_range_wr1 ( item_element );

WR2: value_range_wr2 ( item_element );

WR3: value_range_wr3 ( item_element );

END_ENTITY;

ENTITY value_representation_item

SUBTYPE OF (representation_item);

value_component : measure_value;

WHERE

WR1: SIZEOF (QUERY (rep <* using_representations (SELF) |

NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.GLOBAL_UNIT_ASSIGNED_CONTEXT'

IN TYPEOF (rep.context_of_items)

))) = 0;

END_ENTITY;

ENTITY vector

SUBTYPE OF (geometric_representation_item);

orientation : direction;

magnitude   : length_measure;

WHERE

WR1 : magnitude >= 0.0;

END_ENTITY;

ENTITY vector_style

SUBTYPE OF (curve_style, pre_defined_terminator_symbol);

END_ENTITY;

ENTITY versioned_action_request;

id : identifier;

version : label;

purpose : text;

description : OPTIONAL text;

END_ENTITY;

ENTITY vertex

SUBTYPE OF (topological_representation_item);

END_ENTITY;

ENTITY vertex_loop

SUBTYPE OF (loop);

loop_vertex : vertex;

END_ENTITY;

ENTITY vertex_point

SUBTYPE OF(vertex,geometric_representation_item);

vertex_geometry : point;

END_ENTITY;

ENTITY vertex_shell

SUBTYPE OF (topological_representation_item);

vertex_shell_extent : vertex_loop;

END_ENTITY;

ENTITY view_volume

SUBTYPE OF (founded_item);

projection_type            : central_or_parallel;

projection_point           : cartesian_point;

view_plane_distance        : length_measure;

front_plane_distance       : length_measure;

front_plane_clipping       : BOOLEAN;

back_plane_distance        : length_measure;

back_plane_clipping        : BOOLEAN;

view_volume_sides_clipping : BOOLEAN;

view_window                : planar_box;

END_ENTITY;

ENTITY volume_measure_with_unit

SUBTYPE OF (measure_with_unit);

WHERE

WR1: 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VOLUME_UNIT' IN TYPEOF (SELF\measure_with_unit.unit_component);

END_ENTITY;

ENTITY volume_unit

SUBTYPE OF (named_unit);

WHERE

WR1: (SELF\named_unit.dimensions.length_exponent = 3.000000) AND (SELF\named_unit.dimensions.mass_exponent = 0.000000) AND (SELF\named_unit.dimensions.time_exponent = 0.000000) AND (SELF\named_unit.dimensions.electric_current_exponent = 0.000000) AND (SELF\named_unit.dimensions.thermodynamic_temperature_exponent = 0.000000) AND (SELF\named_unit.dimensions.amount_of_substance_exponent = 0.000000) AND (SELF\named_unit.dimensions.luminous_intensity_exponent = 0.000000);

END_ENTITY;

ENTITY week_of_year_and_day_date

SUBTYPE OF (date);

week_component : week_in_year_number;

day_component : OPTIONAL day_in_week_number;

END_ENTITY;

ENTITY wire_shell

SUBTYPE OF (topological_representation_item);

wire_shell_extent : SET [1:?] OF loop;

WHERE

WR1: NOT mixed_loop_type_set(wire_shell_extent);

END_ENTITY;

FUNCTION acyclic_composite_text(start_composite : composite_text;

child_text : SET [1:?] OF

text_or_character) : LOGICAL;

LOCAL

i : INTEGER;

local_composite_text : SET [0:?] OF composite_text;

local_annotation_text : SET [0:?] OF annotation_text;

local_children : SET [0:?] OF text_or_character;

END_LOCAL;

local_composite_text := QUERY (child <* child_text |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'

IN TYPEOF (child)));

IF (SIZEOF (local_composite_text) > 0) THEN

REPEAT i := 1 TO HIINDEX (local_composite_text);

IF (start_composite :=: local_composite_text[i]) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

END_IF;

local_children := child_text;

IF (SIZEOF (local_composite_text)) > 0 THEN

REPEAT i := 1 TO HIINDEX (local_composite_text);

local_children := local_children +

local_composite_text[i].collected_text;

END_REPEAT;

END_IF;

local_annotation_text := QUERY (child <* child_text |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT'

IN TYPEOF (child)));

IF (SIZEOF (local_annotation_text) > 0) THEN

REPEAT i := 1 TO HIINDEX (local_annotation_text);

local_children := local_children +

QUERY (item <* local_annotation_text[i]\mapped_item.

mapping_source.mapped_representation.items |

SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANNOTATION_TEXT',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_TEXT'] *

TYPEOF(item)) > 0);

END_REPEAT;

END_IF;

IF (local_children :<>: child_text) THEN

RETURN (acyclic_composite_text (start_composite, local_children));

ELSE

RETURN (TRUE);

END_IF;

END_FUNCTION;

FUNCTION acyclic_curve_replica(rep : curve_replica; parent : curve)

: BOOLEAN;

IF NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA') IN TYPEOF(parent)) THEN

RETURN (TRUE);

END_IF;

(* Return TRUE if the parent is not of type curve_replica *)

IF (parent :=: rep) THEN

RETURN (FALSE);

(* Return FALSE if the parent is the same curve_replica, otherwise,

call function again with the parents own parent_curve.     *)

ELSE

RETURN(acyclic_curve_replica(rep,

parent\curve_replica.parent_curve));

END_IF;

END_FUNCTION;

FUNCTION acyclic_mapped_item_usage (rep: representation) : BOOLEAN;

-- returns TRUE if the representation contains one or more mapped_items

-- that are a mapping of the representation itself

LOCAL

items : SET OF representation_item;

END_LOCAL;

items := QUERY (item <* rep.items |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN TYPEOF (item));

IF SIZEOF (items) = 0

THEN

RETURN (FALSE);

ELSE

REPEAT i := 1 TO HIINDEX (items);

IF items[i]\mapped_item.mapping_source.mapped_representation :=: rep

THEN

RETURN (TRUE);

ELSE

RETURN (acyclic_mapped_item_usage(items[i]\

mapped_item.mapping_source.mapped_representation));

END_IF;

END_REPEAT;

RETURN (FALSE);

END_IF;

END_FUNCTION;

FUNCTION acyclic_mapped_representation

(parent_set   : SET OF representation;

children_set : SET OF representation_item) : BOOLEAN;

LOCAL

x,y : SET OF representation_item;

END_LOCAL;

-- Determine the subset of children_set that are mapped_items

x := QUERY(z <* children_set | 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM'

IN TYPEOF(z));

-- Determine that the subset has elements

IF SIZEOF(x) > 0 THEN

-- Check each element of the set

REPEAT i := 1 TO HIINDEX(x);

-- If the selected element maps a representation in the

-- parent_set, then return false

IF x[i]\mapped_item.mapping_source.mapped_representation

IN parent_set THEN

RETURN (FALSE);

END_IF;

-- Recursive check of the items of mapped_representation

IF NOT acyclic_mapped_representation

(parent_set +

x[i]\mapped_item.mapping_source.mapped_representation,

x[i]\mapped_item.mapping_source.mapped_representation.items) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

END_IF;

-- Determine the subset of children_set that are not

-- mapped_items

x := children_set - x;

-- Determine that the subset has elements

IF SIZEOF(x) > 0 THEN

-- For each element of the set:

REPEAT i := 1 TO HIINDEX(x);

-- Determine the set of representation_items referenced

y := QUERY(z <* bag_to_set( USEDIN(x[i], '')) |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION_ITEM' IN TYPEOF(z));

-- Recursively check for an offending mapped_item

-- Return false for any errors encountered

IF NOT acyclic_mapped_representation(parent_set, y) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

END_IF;

-- Return true when all elements are checked and

-- no error conditions found

RETURN (TRUE);

END_FUNCTION;

FUNCTION acyclic_point_replica(rep : point_replica; parent : point)

: BOOLEAN;

IF NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_REPLICA') IN TYPEOF(parent)) THEN

RETURN (TRUE);

END_IF;

(* Return TRUE if the parent is not of type point_replica *)

IF (parent :=: rep) THEN

RETURN (FALSE);

(* Return FALSE if the parent is the same point_replica, otherwise,

call function again with the parents own parent_pt.     *)

ELSE RETURN(acyclic_point_replica(rep, parent\point_replica.parent_pt));

END_IF;

END_FUNCTION;

FUNCTION acyclic_product_category_relationship

(relation : product_category_relationship; children : SET OF product_category) : BOOLEAN;

LOCAL

x : SET OF product_category_relationship;

local_children : SET OF product_category;

END_LOCAL;

REPEAT i := 1 TO HIINDEX(children);

IF relation.category :=: children[i] THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

x := bag_to_set(USEDIN(relation.category, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'PRODUCT_CATEGORY_RELATIONSHIP.SUB_CATEGORY'));

local_children := children + relation.category;

IF SIZEOF(x) > 0 THEN

REPEAT i := 1 TO HIINDEX(x);

IF NOT acyclic_product_category_relationship(x[i], local_children) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

END_IF;

RETURN (TRUE);

END_FUNCTION;

FUNCTION acyclic_product_definition_relationship

(relation : product_definition_relationship; relatives : SET[1:?] OF product_definition; specific_relation : STRING) : BOOLEAN;

LOCAL

x : SET OF product_definition_relationship;

END_LOCAL;

IF relation.relating_product_definition IN relatives THEN

RETURN (FALSE);

END_IF;

x := QUERY(pd <* bag_to_set(USEDIN(relation.relating_product_definition, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'PRODUCT_DEFINITION_RELATIONSHIP.' + 'RELATED_PRODUCT_DEFINITION')) | specific_relation IN TYPEOF(pd));

REPEAT i := 1 TO HIINDEX(x);

IF NOT acyclic_product_definition_relationship(x[i], relatives + relation.relating_product_definition, specific_relation) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

RETURN (TRUE);

END_FUNCTION;

FUNCTION acyclic_solid_replica(rep : solid_replica; parent :

solid_model) : BOOLEAN;

IF NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SOLID_REPLICA') IN TYPEOF(parent)) THEN

RETURN (TRUE);

END_IF;

(* Return TRUE if the parent is not of type solid_replica. *)

IF (parent :=: rep) THEN

RETURN (FALSE);

(* Return FALSE if the parent is the same solid_replica, otherwise,

call function again with the parents own parent_solid.     *)

ELSE RETURN(acyclic_solid_replica(rep,

parent\solid_replica.parent_solid));

END_IF;

END_FUNCTION;

FUNCTION acyclic_surface_replica(rep : surface_replica; parent : surface)

: BOOLEAN;

IF NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_REPLICA') IN TYPEOF(parent)) THEN

RETURN (TRUE);

END_IF;

(* Return TRUE if the parent is not of type surface_replica *)

IF (parent :=: rep) THEN

RETURN (FALSE);

(* Return FALSE if the parent is the same surface_replica, otherwise,

call function again with the parents own parent_surface.     *)

ELSE RETURN(acyclic_surface_replica(rep,

parent\surface_replica.parent_surface));

END_IF;

END_FUNCTION;

FUNCTION acyclic_symbol_representation_relationship

(relation : symbol_representation_relationship;

children : SET OF symbol_representation ) : BOOLEAN;

LOCAL

x : SET OF symbol_representation_relationship;

local_children : SET OF symbol_representation;

END_LOCAL;

REPEAT i:=1 TO HIINDEX(children);

IF relation\representation_relationship.rep_1 :=: children[i] THEN

RETURN(FALSE);

END_IF;

END_REPEAT;

x := bag_to_set (USEDIN ( relation\representation_relationship.rep_1,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_RELATIONSHIP.'+ 'REP_2'));

local_children := children + relation\representation_relationship.rep_1;

IF SIZEOF (x) > 0 THEN

REPEAT i:=1 TO HIINDEX (x);

IF NOT acyclic_symbol_representation_relationship(x[i] ,

local_children) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

END_IF;

RETURN (TRUE);

END_FUNCTION;

FUNCTION aspect_ratio (p : planar_box) : positive_ratio_measure;

(* if the dimensions of the planar_box are greater than zero,

compute the aspect ratio and return the resulting value. *)

IF (p.size_in_x > 0.) AND (p.size_in_y > 0.) THEN

RETURN (p.size_in_x / p.size_in_y);

ELSE

RETURN (?);

END_IF;

END_FUNCTION;

FUNCTION associated_surface(arg : pcurve_or_surface) : surface;

LOCAL

surf : surface;

END_LOCAL;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(arg) THEN

surf := arg.basis_surface;

ELSE

surf := arg;

END_IF;

RETURN(surf);

END_FUNCTION;

FUNCTION bag_to_set (the_bag : BAG OF GENERIC:intype):SET OF GENERIC:intype;

LOCAL

the_set : SET OF GENERIC:intype := [];

END_LOCAL;

IF SIZEOF(the_bag) > 0 THEN

REPEAT i := 1 TO HIINDEX(the_bag);

the_set := the_set + the_bag[i];

END_REPEAT;

END_IF;

RETURN (the_set);

END_FUNCTION;

FUNCTION base_axis(dim : INTEGER; axis1, axis2, axis3 : direction) :

LIST [2:3] OF

direction;

LOCAL

u      : LIST [2:3] OF direction;

factor : REAL;

d1, d2 : direction;

END_LOCAL;

IF (dim = 3) THEN

d1 := NVL(normalise(axis3),  dummy_gri || direction([0.0,0.0,1.0]));

d2 := first_proj_axis(d1,axis1);

u := [d2, second_proj_axis(d1,d2,axis2), d1];

ELSE

IF EXISTS(axis1) THEN

d1 := normalise(axis1);

u := [d1, orthogonal_complement(d1)];

IF EXISTS(axis2) THEN

factor := dot_product(axis2,u[2]);

IF (factor < 0.0) THEN

u[2].direction_ratios[1] := -u[2].direction_ratios[1];

u[2].direction_ratios[2] := -u[2].direction_ratios[2];

END_IF;

END_IF;

ELSE

IF EXISTS(axis2) THEN

d1 := normalise(axis2);

u := [orthogonal_complement(d1), d1];

u[1].direction_ratios[1] := -u[1].direction_ratios[1];

u[1].direction_ratios[2] := -u[1].direction_ratios[2];

ELSE

u := [dummy_gri || direction([1.0, 0.0]), dummy_gri ||

direction([0.0, 1.0])];

END_IF;

END_IF;

END_IF;

RETURN(u);

END_FUNCTION;

FUNCTION boolean_choose (b : boolean;

choice1, choice2 : generic : item)  : generic : item;

IF b THEN

RETURN (choice1);

ELSE

RETURN (choice2);

END_IF;

END_FUNCTION;

FUNCTION build_2axes(ref_direction : direction) : LIST [2:2] OF direction;

LOCAL

d : direction := NVL(normalise(ref_direction),

dummy_gri || direction([1.0,0.0]));

END_LOCAL;

RETURN([d, orthogonal_complement(d)]);

END_FUNCTION;

FUNCTION build_axes(axis, ref_direction : direction) :

LIST [3:3] OF direction;

LOCAL

d1, d2 : direction;

END_LOCAL;

d1 := NVL(normalise(axis), dummy_gri || direction([0.0,0.0,1.0]));

d2 := first_proj_axis(d1, ref_direction);

RETURN([d2, normalise(cross_product(d1,d2)).orientation, d1]);

END_FUNCTION;

FUNCTION cc_design_person_and_organization_correlation

(e : cc_design_person_and_organization_assignment) : BOOLEAN;

LOCAL

po_role : STRING;

END_LOCAL;

po_role := e\person_and_organization_assignment.role.name;

CASE po_role OF

'request_recipient'      : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

SIZEOF(['CONFIG_CONTROL_DESIGN.' +

'CHANGE_REQUEST',

'CONFIG_CONTROL_DESIGN.' +

'START_REQUEST'] *

TYPEOF (x)) = 1))

THEN RETURN(FALSE);

END_IF;

'initiator'              : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

SIZEOF(['CONFIG_CONTROL_DESIGN.' +

'CHANGE_REQUEST',

'CONFIG_CONTROL_DESIGN.' +

'START_REQUEST',

'CONFIG_CONTROL_DESIGN.' +

'START_WORK',

'CONFIG_CONTROL_DESIGN.' +

'CHANGE'] *

TYPEOF (x)) = 1))

THEN RETURN(FALSE);

END_IF;

'creator'                : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

SIZEOF (['CONFIG_CONTROL_DESIGN.' +

'PRODUCT_DEFINITION_FORMATION',

'CONFIG_CONTROL_DESIGN.' +

'PRODUCT_DEFINITION'] *

TYPEOF (x)) = 1))

THEN RETURN (FALSE);

END_IF;

'part_supplier'          : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

'CONFIG_CONTROL_DESIGN.' +

'PRODUCT_DEFINITION_FORMATION'

IN TYPEOF (x)))

THEN RETURN(FALSE);

END_IF;

'design_supplier'        : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

'CONFIG_CONTROL_DESIGN.' +

'PRODUCT_DEFINITION_FORMATION'

IN TYPEOF (x)))

THEN RETURN(FALSE);

END_IF;

'design_owner'           : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

'CONFIG_CONTROL_DESIGN.PRODUCT'

IN TYPEOF (x)))

THEN RETURN(FALSE);

END_IF;

'configuration_manager'  : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

'CONFIG_CONTROL_DESIGN.' +

'CONFIGURATION_ITEM'

IN TYPEOF (x)))

THEN RETURN(FALSE);

END_IF;

'contractor'             : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

'CONFIG_CONTROL_DESIGN.CONTRACT'

IN TYPEOF (x)))

THEN RETURN(FALSE);

END_IF;

'classification_officer' : IF SIZEOF (e.items) <>

SIZEOF (QUERY (x <* e.items |

'CONFIG_CONTROL_DESIGN.' +

'SECURITY_CLASSIFICATION'

IN TYPEOF (x))) THEN

RETURN(FALSE);

END_IF;

OTHERWISE : RETURN(TRUE);

END_CASE;

RETURN (TRUE);

END_FUNCTION;

FUNCTION check_associative_shape_aspects

(sdr : shape_definition_representation) : BOOLEAN;

LOCAL

sr1, sr2 : SET OF representation;

dm, pv   : SET OF representation;

END_LOCAL;

-- Check if the representation contains only two items

IF (SIZEOF (sdr.used_representation.items) <> 2) THEN

RETURN (FALSE);

END_IF;

-- Find the representations that use each item

sr1 := using_representations(sdr.used_representation.items[1]);

sr2 := using_representations(sdr.used_representation.items[2]);

-- Find the representations in which item 1 representations are mapped

REPEAT i := 1 TO HIINDEX(sr1);

dm := representations_mapped_into(sr1[i]);

REPEAT j := 1 TO HIINDEX(dm);

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_MODEL' IN TYPEOF(dm[j]))

THEN

IF (dm[j] IN sr2) THEN RETURN (TRUE);

END_IF;

-- Find the views that the draughting model is mapped into

pv := representations_mapped_into(dm[j]);

REPEAT k := 1 TO HIINDEX(pv);

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_VIEW' IN TYPEOF(pv[k]))

THEN

IF (pv[k] IN sr2) THEN RETURN (TRUE);

END_IF;

END_IF;

END_REPEAT;

END_IF;

END_REPEAT;

END_REPEAT;

-- Find the representations in which item 2 representations are mapped

REPEAT i := 1 TO HIINDEX(sr2);

dm := representations_mapped_into(sr2[i]);

REPEAT j := 1 TO HIINDEX(dm);

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DRAUGHTING_MODEL' IN TYPEOF(dm[j]))

THEN

IF (dm[j] IN sr1) THEN RETURN (TRUE);

END_IF;

-- Find the views that the draughting model is mapped into

pv := representations_mapped_into(dm[j]);

REPEAT k := 1 TO HIINDEX(pv);

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PRESENTATION_VIEW' IN TYPEOF(pv[k]))

THEN

IF (pv[k] IN sr1) THEN RETURN (TRUE);

END_IF;

END_IF;

END_REPEAT;

END_IF;

END_REPEAT;

END_REPEAT;

RETURN(FALSE);

END_FUNCTION;

FUNCTION check_text_alignment (ct : composite_text) : BOOLEAN;

LOCAL

a : SET OF text_alignment := [];

END_LOCAL;

-- create a set of all the alignments

REPEAT i := 1 TO HIINDEX (ct.collected_text);

a := a + [ct.collected_text[i]\text_literal.alignment];

END_REPEAT;

-- if there is more than one element in the set

-- then not all alignments were the same

RETURN (SIZEOF(a) = 1);

END_FUNCTION;

FUNCTION check_text_font (ct : composite_text) : BOOLEAN;

LOCAL

f : SET OF font_select := [];

END_LOCAL;

-- build a set of all the fonts

REPEAT i := 1 TO HIINDEX (ct.collected_text);

f := f + [ct.collected_text[i]\text_literal.font];

END_REPEAT;

-- if there is more than one element in the set

-- then not all fonts were the same

RETURN (SIZEOF(f) <= 1);

END_FUNCTION;

FUNCTION closed_shell_reversed (a_shell : closed_shell) :

oriented_closed_shell;

LOCAL

the_reverse : oriented_closed_shell;

END_LOCAL;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_CLOSED_SHELL' IN TYPEOF (a_shell) ) THEN

the_reverse := dummy_tri ||

connected_face_set (

a_shell\connected_face_set.cfs_faces) ||

closed_shell () || oriented_closed_shell(

a_shell\oriented_closed_shell.closed_shell_element,

NOT(a_shell\oriented_closed_shell.orientation));

ELSE

the_reverse := dummy_tri ||

connected_face_set (

a_shell\connected_face_set.cfs_faces) ||

closed_shell () || oriented_closed_shell (a_shell, FALSE);

END_IF;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION conditional_reverse (p       : BOOLEAN;

an_item : reversible_topology)

: reversible_topology;

IF p THEN

RETURN (an_item);

ELSE

RETURN (topology_reversed (an_item));

END_IF;

END_FUNCTION;

FUNCTION constraints_composite_curve_on_surface

(c: composite_curve_on_surface) : BOOLEAN;

LOCAL

n_segments : INTEGER := SIZEOF(c.segments);

END_LOCAL;

REPEAT k := 1 TO n_segments;

IF (NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN

TYPEOF(c\composite_curve.segments[k].parent_curve))) AND

(NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE' IN

TYPEOF(c\composite_curve.segments[k].parent_curve))) AND

(NOT('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_CURVE_ON_SURFACE' IN

TYPEOF(c\composite_curve.segments[k].parent_curve)))  THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

RETURN(TRUE);

END_FUNCTION;

FUNCTION constraints_geometry_shell_based_surface_model

(m: shell_based_surface_model): BOOLEAN;

LOCAL

result : BOOLEAN := TRUE;

END_LOCAL;

REPEAT j := 1 TO SIZEOF(m.sbsm_boundary);

IF (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OPEN_SHELL' IN

TYPEOF(m.sbsm_boundary[j])) AND

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CLOSED_SHELL' IN

TYPEOF(m.sbsm_boundary[j]))))

THEN

result := FALSE;

RETURN(result);

(* A surface model is composed of OPEN_ and CLOSED_SHELLs. *)

END_IF;

END_REPEAT;

RETURN(result);

END_FUNCTION;

FUNCTION constraints_geometry_shell_based_wireframe_model

(m : shell_based_wireframe_model) : BOOLEAN;

LOCAL

result : BOOLEAN := TRUE;

END_LOCAL;

REPEAT j := 1 TO SIZEOF(m.sbwm_boundary);

IF (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.WIRE_SHELL' IN

TYPEOF(m.sbwm_boundary[j])) AND

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VERTEX_SHELL' IN

TYPEOF(m.sbwm_boundary[j]))))

THEN

result := FALSE;

RETURN(result);

(* A wireframe model is composed of WIRE_ and VERTEX_SHELLs *)

END_IF;

END_REPEAT;

RETURN(result);

END_FUNCTION;

FUNCTION constraints_param_b_spline(degree, up_knots, up_cp : INTEGER;

knot_mult : LIST OF INTEGER;

knots : LIST OF parameter_value) : BOOLEAN;

LOCAL

result  : BOOLEAN := TRUE;

k, sum  : INTEGER;

END_LOCAL;

(* Find sum of knot multiplicities. *)

sum := knot_mult[1];

REPEAT i := 2 TO up_knots;

sum := sum + knot_mult[i];

END_REPEAT;

(* Check limits holding for all B-spline parametrisations *)

IF (degree < 1) OR (up_knots < 2) OR (up_cp < degree) OR

(sum <> (degree + up_cp + 2)) THEN

result := FALSE;

RETURN(result);

END_IF;

k := knot_mult[1];

IF (k < 1) OR (k > degree + 1) THEN

result := FALSE;

RETURN(result);

END_IF;

REPEAT i := 2 TO up_knots;

IF (knot_mult[i] < 1) OR (knots[i] <= knots[i-1]) THEN

result := FALSE;

RETURN(result);

END_IF;

k := knot_mult[i];

IF (i < up_knots) AND (k > degree) THEN

result := FALSE;

RETURN(result);

END_IF;

IF (i = up_knots) AND (k > degree + 1) THEN

result := FALSE;

RETURN(result);

END_IF;

END_REPEAT;

RETURN(result);

END_FUNCTION;

FUNCTION constraints_rectangular_composite_surface

(s : rectangular_composite_surface) : BOOLEAN;

(* Check the surface types *)

REPEAT i := 1 TO s.n_u;

REPEAT j := 1 TO s.n_v;

IF NOT (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_SURFACE' IN TYPEOF

(s.segments[i][j].parent_surface)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RECTANGULAR_TRIMMED_SURFACE' IN TYPEOF

(s.segments[i][j].parent_surface))) THEN

RETURN(FALSE);

END_IF;

END_REPEAT;

END_REPEAT;

(* Check the transition codes, omitting the last row or column *)

REPEAT i := 1 TO s.n_u-1;

REPEAT j := 1 TO s.n_v;

IF s.segments[i][j].u_transition = discontinuous THEN

RETURN(FALSE);

END_IF;

END_REPEAT;

END_REPEAT;

REPEAT i := 1 TO s.n_u;

REPEAT j := 1 TO s.n_v-1;

IF s.segments[i][j].v_transition = discontinuous THEN

RETURN(FALSE);

END_IF;

END_REPEAT;

END_REPEAT;

RETURN(TRUE);

END_FUNCTION;

FUNCTION cross_product (arg1, arg2 : direction) : vector;

LOCAL

mag    : REAL;

res    : direction;

v1,v2  : LIST[3:3] OF REAL;

result : vector;

END_LOCAL;

IF ( NOT EXISTS (arg1) OR (arg1.dim = 2)) OR

( NOT EXISTS (arg2) OR (arg2.dim = 2)) THEN

RETURN(?);

ELSE

BEGIN

v1  := normalise(arg1).direction_ratios;

v2  := normalise(arg2).direction_ratios;

res := dummy_gri || direction([(v1[2]*v2[3] - v1[3]*v2[2]),

(v1[3]*v2[1] - v1[1]*v2[3]), (v1[1]*v2[2] - v1[2]*v2[1])]);

mag := 0.0;

REPEAT i := 1 TO 3;

mag := mag + res.direction_ratios[i]*res.direction_ratios[i];

END_REPEAT;

IF (mag > 0.0) THEN

result := dummy_gri || vector(res, SQRT(mag));

ELSE

result := dummy_gri || vector(arg1, 0.0);

END_IF;

RETURN(result);

END;

END_IF;

END_FUNCTION;

FUNCTION curve_weights_positive(b: rational_b_spline_curve) : BOOLEAN;

LOCAL

result : BOOLEAN := TRUE;

END_LOCAL;

REPEAT i := 0 TO b.upper_index_on_control_points;

IF b.weights[i] <= 0.0  THEN

result := FALSE;

RETURN(result);

END_IF;

END_REPEAT;

RETURN(result);

END_FUNCTION;

FUNCTION default_tolerance_table_cell_wr2

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF SIZEOF(agg) <= 5 THEN

RETURN(TRUE);

ELSE

RETURN(FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION default_tolerance_table_cell_wr3

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF (SIZEOF(QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF(i))

AND (i\representation_item.name = 'significant number of digits')) )) = 1) OR

((SIZEOF(QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF(i)) AND

(i\representation_item.name = 'lower limit')) )) = 1) AND

(SIZEOF( QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF(i)) AND

(i\representation_item.name = 'upper limit')) )) = 1)) THEN

RETURN(TRUE);

ELSE

RETURN(FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION default_tolerance_table_cell_wr4

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF (SIZEOF(QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF(i)) AND

(i\representation_item.name = 'plus minus tolerance value')) )) = 1) OR

((SIZEOF(QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF(i)) AND (

i\representation_item.name = 'lower tolerance value')) )) = 1) AND

(SIZEOF( QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF(i)) AND (

i\representation_item.name = 'upper tolerance value')) )) = 1)) THEN

RETURN(TRUE);

ELSE

RETURN(FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION default_tolerance_table_cell_wr5

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF (SIZEOF(QUERY ( i <* agg | ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DESCRIPTIVE_REPRESENTATION_ITEM' IN TYPEOF(i)) )) <= 1) AND

(SIZEOF(QUERY ( i <* agg | ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DESCRIPTIVE_REPRESENTATION_ITEM' IN TYPEOF(i)) )) =

SIZEOF(QUERY ( i <* agg | (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DESCRIPTIVE_REPRESENTATION_ITEM' IN TYPEOF(i)) AND

(i\representation_item.name = 'cell description'))) ))

THEN

RETURN(TRUE);

ELSE

RETURN(FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION derive_dimensional_exponents

(x : unit) : dimensional_exponents;

LOCAL

result : dimensional_exponents := dimensional_exponents(0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0);

END_LOCAL;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DERIVED_UNIT' IN TYPEOF(x) THEN

REPEAT i := LOINDEX(x.elements) TO HIINDEX(x.elements);

result.length_exponent := result.length_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.length_exponent);

result.mass_exponent := result.mass_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.mass_exponent);

result.time_exponent := result.time_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.time_exponent);

result.electric_current_exponent := result.electric_current_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.electric_current_exponent);

result.thermodynamic_temperature_exponent := result.thermodynamic_temperature_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.thermodynamic_temperature_exponent);

result.amount_of_substance_exponent := result.amount_of_substance_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.amount_of_substance_exponent);

result.luminous_intensity_exponent := result.luminous_intensity_exponent + (x.elements[i].exponent * x.elements[i].unit.dimensions.luminous_intensity_exponent);

END_REPEAT;

ELSE

result := x.dimensions;

END_IF;

RETURN (result);

END_FUNCTION;

FUNCTION dimension_of(item : geometric_representation_item) :

dimension_count;

LOCAL

x   : SET OF representation;

y   : representation_context;

dim : dimension_count;

END_LOCAL;

-- For cartesian_point, direction, or vector dimension is determined by

-- counting components.

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF(item) THEN

dim := SIZEOF(item\cartesian_point.coordinates);

RETURN(dim);

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DIRECTION' IN TYPEOF(item) THEN

dim := SIZEOF(item\direction.direction_ratios);

RETURN(dim);

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VECTOR' IN TYPEOF(item) THEN

dim := SIZEOF(item\vector.orientation\direction.direction_ratios);

RETURN(dim);

END_IF;

-- For all other types of geometric_representation_item dim is obtained

-- via context.

-- Find the set of representation in which the item is used.

x := using_representations(item);

-- Determines the dimension_count of the

-- geometric_representation_context. Note that the

-- RULE compatible_dimension ensures that the context_of_items

-- is of type geometric_representation_context and has

-- the same dimension_count for all values of x.

-- The SET x is non-empty since this is required by WR1 of

-- representation_item.

y := x[1].context_of_items;

dim := y\geometric_representation_context.coordinate_space_dimension;

RETURN (dim);

END_FUNCTION;

FUNCTION dimensions_for_si_unit

(n : si_unit_name) : dimensional_exponents;

CASE n OF

metre          : RETURN (dimensional_exponents

(1.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0));

gram           : RETURN (dimensional_exponents

(0.0, 1.0, 0.0, 0.0, 0.0, 0.0, 0.0));

second         : RETURN (dimensional_exponents

(0.0, 0.0, 1.0, 0.0, 0.0, 0.0, 0.0));

ampere         : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 1.0, 0.0, 0.0, 0.0));

kelvin         : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0));

mole           : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 0.0, 1.0, 0.0));

candela        : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 1.0));

radian         : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0));

steradian      : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0));

hertz          : RETURN (dimensional_exponents

(0.0, 0.0, -1.0, 0.0, 0.0, 0.0, 0.0));

newton         : RETURN (dimensional_exponents

(1.0, 1.0, -2.0, 0.0, 0.0, 0.0, 0.0));

pascal         : RETURN (dimensional_exponents

(-1.0, 1.0, -2.0, 0.0, 0.0, 0.0, 0.0));

joule          : RETURN (dimensional_exponents

(2.0, 1.0, -2.0, 0.0, 0.0, 0.0, 0.0));

watt           : RETURN (dimensional_exponents

(2.0, 1.0, -3.0, 0.0, 0.0, 0.0, 0.0));

coulomb        : RETURN (dimensional_exponents

(0.0, 0.0, 1.0, 1.0, 0.0, 0.0, 0.0));

volt           : RETURN (dimensional_exponents

(2.0, 1.0, -3.0, -1.0, 0.0, 0.0, 0.0));

farad          : RETURN (dimensional_exponents

(-2.0, -1.0, 4.0, 1.0, 0.0, 0.0, 0.0));

ohm            : RETURN (dimensional_exponents

(2.0, 1.0, -3.0, -2.0, 0.0, 0.0, 0.0));

siemens        : RETURN (dimensional_exponents

(-2.0, -1.0, 3.0, 2.0, 0.0, 0.0, 0.0));

weber          : RETURN (dimensional_exponents

(2.0, 1.0, -2.0, -1.0, 0.0, 0.0, 0.0));

tesla          : RETURN (dimensional_exponents

(0.0, 1.0, -2.0, -1.0, 0.0, 0.0, 0.0));

henry          : RETURN (dimensional_exponents

(2.0, 1.0, -2.0, -2.0, 0.0, 0.0, 0.0));

degree_Celsius : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0));

lumen          : RETURN (dimensional_exponents

(0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 1.0));

lux            : RETURN (dimensional_exponents

(-2.0, 0.0, 0.0, 0.0, 0.0, 0.0, 1.0));

becquerel      : RETURN (dimensional_exponents

(0.0, 0.0, -1.0, 0.0, 0.0, 0.0, 0.0));

gray           : RETURN (dimensional_exponents

(2.0, 0.0, -2.0, 0.0, 0.0, 0.0, 0.0));

sievert        : RETURN (dimensional_exponents

(2.0, 0.0, -2.0, 0.0, 0.0, 0.0, 0.0));

OTHERWISE      : RETURN (?);

END_CASE;

END_FUNCTION;

FUNCTION dot_product(arg1, arg2 : direction) : REAL;

LOCAL

scalar : REAL;

vec1, vec2: direction;

ndim : INTEGER;

END_LOCAL;

IF NOT EXISTS (arg1) OR NOT EXISTS (arg2) THEN

scalar := ?;

(* When function is called with invalid data an indeterminate result

is returned *)

ELSE

IF (arg1.dim <> arg2.dim) THEN

scalar := ?;

(* When function is called with invalid data an indeterminate result

is returned *)

ELSE

BEGIN

vec1   := normalise(arg1);

vec2   := normalise(arg2);

ndim   := arg1.dim;

scalar := 0.0;

REPEAT  i := 1 TO ndim;

scalar := scalar +

vec1.direction_ratios[i]*vec2.direction_ratios[i];

END_REPEAT;

END;

END_IF;

END_IF;

RETURN (scalar);

END_FUNCTION;

FUNCTION edge_reversed (an_edge : edge) : oriented_edge;

LOCAL

the_reverse : oriented_edge;

END_LOCAL;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_EDGE' IN TYPEOF (an_edge) ) THEN

the_reverse  := dummy_tri ||

edge(an_edge.edge_end, an_edge.edge_start) ||

oriented_edge(an_edge\oriented_edge.edge_element,

NOT (an_edge\oriented_edge.orientation)) ;

ELSE

the_reverse := dummy_tri ||

edge(an_edge.edge_end, an_edge.edge_start) ||

oriented_edge(an_edge, FALSE);

END_IF;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION face_bound_reversed (a_face_bound : face_bound) : face_bound;

LOCAL

the_reverse : face_bound ;

END_LOCAL;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_OUTER_BOUND' IN TYPEOF (a_face_bound) ) THEN

the_reverse := dummy_tri ||

face_bound(a_face_bound\face_bound.bound,

NOT (a_face_bound\face_bound.orientation))

|| face_outer_bound() ;

ELSE

the_reverse := dummy_tri ||

face_bound(a_face_bound.bound, NOT(a_face_bound.orientation));

END_IF;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION face_reversed (a_face : face) : oriented_face;

LOCAL

the_reverse : oriented_face ;

END_LOCAL;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_FACE' IN TYPEOF (a_face) ) THEN

the_reverse := dummy_tri ||

face(set_of_topology_reversed(a_face.bounds)) ||

oriented_face(a_face\oriented_face.face_element,

NOT (a_face\oriented_face.orientation)) ;

ELSE

the_reverse := dummy_tri ||

face(set_of_topology_reversed(a_face.bounds)) ||

oriented_face(a_face, FALSE) ;

END_IF;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION field_in_table (field : table_record_field_representation;

table : annotation_table_occurrence): BOOLEAN;

LOCAL

table_rep : table_representation;

symbol_rep_rel_set : SET OF symbol_representation_relationship;

mapped_item_set : SET OF mapped_item;

table_record_rep_set : SET OF table_record_representation := [];

END_LOCAL;

table_rep := table\styled_item.item\mapped_item.mapping_source.

mapped_representation;

mapped_item_set := QUERY(item <* table_rep.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN

TYPEOF(item))

AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'TABLE_RECORD_REPRESENTATION' IN

TYPEOF(item\mapped_item.mapping_source.

mapped_representation ))

);

REPEAT i := 1 TO HIINDEX(mapped_item_set);

table_record_rep_set := table_record_rep_set +

mapped_item_set[i].mapping_source.mapped_representation;

END_REPEAT;

symbol_rep_rel_set := bag_to_set (USEDIN(table_rep,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_RELATIONSHIP.REP_1'));

REPEAT i := 1 TO HIINDEX(symbol_rep_rel_set);

table_record_rep_set := table_record_rep_set +

symbol_rep_rel_set[i]\representation_relationship.rep_2;

END_REPEAT;

IF SIZEOF(QUERY( table_record_rep <* table_record_rep_set |

--              (SIZEOF(QUERY( symbol_rep_rel <* USEDIN(table_record_rep,

--                            'PRESENTATION_DEFINITION_SCHEMA.'+

--                            'SYMBOL_REPRESENTATION_RELATIONSHIP.REP_1') |

--                       symbol_rep_rel\representation_relationship.rep_2 :=: field

(SIZEOF(QUERY( rep_rel <* USEDIN(table_record_rep,

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.'+

'REPRESENTATION_RELATIONSHIP.REP_1') |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'SYMBOL_REPRESENTATION_RELATIONSHIP' IN TYPEOF(rep_rel)) AND

(rep_rel.rep_2 :=: field)

)) > 0)

OR

(SIZEOF(QUERY(item <* table_record_rep.items |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MAPPED_ITEM' IN

TYPEOF(item))

AND

(field :=: item\mapped_item.mapping_source.

mapped_representation )

)) > 0)

)) = 0 THEN

RETURN(FALSE);

END_IF;

RETURN(TRUE);

END_FUNCTION;

FUNCTION first_proj_axis(z_axis, arg : direction) : direction;

LOCAL

x_axis : direction;

v      : direction;

z      : direction;

x_vec  : vector;

END_LOCAL;

IF (NOT EXISTS(z_axis)) THEN

RETURN (?) ;

ELSE

z := normalise(z_axis);

IF NOT EXISTS(arg) THEN

IF ((z.direction_ratios <> [1.0,0.0,0.0]) AND

(z.direction_ratios <> [-1.0,0.0,0.0]))  THEN

v :=  dummy_gri || direction([1.0,0.0,0.0]);

ELSE

v := dummy_gri || direction([0.0,1.0,0.0]);

END_IF;

ELSE

IF  (arg.dim <> 3) THEN

RETURN (?) ;

END_IF;

IF ((cross_product(arg,z).magnitude) = 0.0) THEN

RETURN (?);

ELSE

v := normalise(arg);

END_IF;

END_IF;

x_vec := scalar_times_vector(dot_product(v, z), z);

x_axis := vector_difference(v, x_vec).orientation;

x_axis := normalise(x_axis);

END_IF;

RETURN(x_axis);

END_FUNCTION;

FUNCTION gbsf_check_curve

(cv : representation_item) : BOOLEAN;

IF SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOUNDED_CURVE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D'] * TYPEOF(cv)) > 1 THEN

RETURN (FALSE);

END_IF;

IF SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CIRCLE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELLIPSE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TRIMMED_CURVE'] * TYPEOF(cv)) = 1 THEN

RETURN (TRUE);

ELSE

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE' IN TYPEOF(cv)) AND (cv\b_spline_curve.self_intersect = FALSE) OR (cv\b_spline_curve.self_intersect = UNKNOWN)) THEN

RETURN (TRUE);

ELSE

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_CURVE' IN TYPEOF(cv)) AND (cv\composite_curve.self_intersect = FALSE) OR (cv\composite_curve.self_intersect = UNKNOWN)) THEN

RETURN (SIZEOF(QUERY(seg <* cv\composite_curve.segments | NOT (gbsf_check_curve(seg.parent_curve)))) = 0);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA' IN TYPEOF(cv) THEN

RETURN (gbsf_check_curve(cv\curve_replica.parent_curve));

ELSE

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D' IN TYPEOF(cv)) AND ((cv\offset_curve_3d.self_intersect = FALSE) OR (cv\offset_curve_3d.self_intersect = UNKNOWN)) AND (NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF(cv\offset_curve_3d.basis_curve)))) THEN

RETURN (gbsf_check_curve(cv\offset_curve_3d.basis_curve));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(cv) THEN

RETURN ((gbsf_check_curve(cv\pcurve.reference_to_curve\representation.items[1])) AND (gbsf_check_surface(cv\pcurve.basis_surface)));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF(cv) THEN

IF (SIZEOF(cv\polyline.points) >= 3) THEN

RETURN (TRUE);

END_IF;

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE' IN TYPEOF(cv) THEN

IF gbsf_check_curve(cv\surface_curve.curve_3d) THEN

REPEAT i := 1 TO SIZEOF(cv\surface_curve.associated_geometry);

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE' IN TYPEOF(cv\surface_curve.associated_geometry[i]) THEN

IF NOT gbsf_check_surface(cv\surface_curve.associated_geometry[i]) THEN

RETURN (FALSE);

END_IF;

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(cv\surface_curve.associated_geometry[i]) THEN

IF NOT gbsf_check_curve(cv\surface_curve.associated_geometry[i]) THEN

RETURN (FALSE);

END_IF;

END_IF;

END_IF;

END_REPEAT;

RETURN (TRUE);

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

RETURN (FALSE);

END_FUNCTION;

FUNCTION gbsf_check_point

(pnt : point) : BOOLEAN;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF(pnt) THEN

RETURN (TRUE);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_CURVE' IN TYPEOF(pnt) THEN

RETURN (gbsf_check_curve(pnt\point_on_curve.basis_curve));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_SURFACE' IN TYPEOF(pnt) THEN

RETURN (gbsf_check_surface(pnt\point_on_surface.basis_surface));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.DEGENERATE_PCURVE' IN TYPEOF(pnt) THEN

RETURN ((gbsf_check_curve(pnt\degenerate_pcurve.reference_to_curve\representation.items[1])) AND (gbsf_check_surface(pnt\degenerate_pcurve.basis_surface)));

END_IF;

END_IF;

END_IF;

END_IF;

RETURN (FALSE);

END_FUNCTION;

FUNCTION gbsf_check_surface

(sf : surface) : BOOLEAN;

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_SURFACE' IN TYPEOF(sf)) AND (sf\b_spline_surface.self_intersect = FALSE) OR (sf\b_spline_surface.self_intersect = UNKNOWN)) THEN

RETURN (TRUE);

ELSE

IF SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SPHERICAL_SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TOROIDAL_SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_BOUNDED_SURFACE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RECTANGULAR_TRIMMED_SURFACE'] * TYPEOF(sf)) = 1 THEN

RETURN (TRUE);

ELSE

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_SURFACE' IN TYPEOF(sf)) AND (sf\offset_surface.self_intersect = FALSE) OR (sf\offset_surface.self_intersect = UNKNOWN)) THEN

RETURN (gbsf_check_surface(sf\offset_surface.basis_surface));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RECTANGULAR_COMPOSITE_SURFACE' IN TYPEOF(sf) THEN

REPEAT i := 1 TO SIZEOF(sf\rectangular_composite_surface.segments);

REPEAT j := 1 TO SIZEOF(sf\rectangular_composite_surface.segments[i]);

IF NOT (gbsf_check_surface(sf\rectangular_composite_surface.segments[i][j].parent_surface)) THEN

RETURN (FALSE);

END_IF;

END_REPEAT;

END_REPEAT;

RETURN (TRUE);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_REPLICA' IN TYPEOF(sf) THEN

RETURN (gbsf_check_surface(sf\surface_replica.parent_surface));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_OF_REVOLUTION' IN TYPEOF(sf) THEN

RETURN (gbsf_check_curve(sf\swept_surface.swept_curve));

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

RETURN (FALSE);

END_FUNCTION;

FUNCTION get_basis_surface (c : curve_on_surface) : SET[0:2] OF surface;

LOCAL

surfs  : SET[0:2] OF surface;

n      : INTEGER;

END_LOCAL;

surfs := [];

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF (c) THEN

surfs := [c\pcurve.basis_surface];

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE' IN TYPEOF (c) THEN

n := SIZEOF(c\surface_curve.associated_geometry);

REPEAT i := 1 TO n;

surfs := surfs +

associated_surface(c\surface_curve.associated_geometry[i]);

END_REPEAT;

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_CURVE_ON_SURFACE' IN TYPEOF (c) THEN

(* For a composite_curve_on_surface the basis_surface is the intersection

of the basis_surfaces of all the segments. *)

n := SIZEOF(c\composite_curve.segments);

surfs := get_basis_surface(

c\composite_curve.segments[1].parent_curve);

IF n > 1 THEN

REPEAT i := 2 TO n;

surfs := surfs * get_basis_surface(

c\composite_curve.segments[i].parent_curve);

END_REPEAT;

END_IF;

END_IF;

RETURN(surfs);

END_FUNCTION;

FUNCTION get_description_value

(obj : description_attribute_select) : text;

LOCAL

description_bag : BAG OF description_attribute := (USEDIN(obj, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'DESCRIPTION_ATTRIBUTE.' + 'DESCRIBED_ITEM'));

END_LOCAL;

IF SIZEOF(description_bag) = 1 THEN

RETURN (description_bag[1].attribute_value);

ELSE

RETURN (?);

END_IF;

END_FUNCTION;

FUNCTION get_id_value

(obj : id_attribute_select) : identifier;

LOCAL

id_bag : BAG OF id_attribute := (USEDIN(obj, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ID_ATTRIBUTE.' + 'IDENTIFIED_ITEM'));

END_LOCAL;

IF SIZEOF(id_bag) = 1 THEN

RETURN (id_bag[1].attribute_value);

ELSE

RETURN (?);

END_IF;

END_FUNCTION;

FUNCTION get_name_value

(obj : name_attribute_select) : label;

LOCAL

name_bag : BAG OF name_attribute := (USEDIN(obj, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'NAME_ATTRIBUTE.' + 'NAMED_ITEM'));

END_LOCAL;

IF SIZEOF(name_bag) = 1 THEN

RETURN (name_bag[1].attribute_value);

ELSE

RETURN (?);

END_IF;

END_FUNCTION;

FUNCTION get_role

(obj : role_select) : object_role;

LOCAL

role_bag : BAG OF role_association := (USEDIN(obj, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'ROLE_ASSOCIATION.' + 'ITEM_WITH_ROLE'));

END_LOCAL;

IF SIZEOF(role_bag) = 1 THEN

RETURN (role_bag[1].role);

ELSE

RETURN (?);

END_IF;

END_FUNCTION;

FUNCTION get_shape_aspect_property_definition_representations

(s_a_instance : shape_aspect) : SET OF property_definition_representation;

LOCAL

pd_set : SET OF property_definition := [];

pdr_set : SET OF property_definition_representation := [] ;

END_LOCAL;

pd_set := bag_to_set(USEDIN(s_a_instance, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PROPERTY_DEFINITION.DEFINITION'));

IF (SIZEOF(pd_set) < 1) THEN

RETURN (pdr_set);

END_IF;

REPEAT i := 1 TO HIINDEX(pd_set);

pdr_set := pdr_set + (QUERY(pdr <* USEDIN(pd_set[i], 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' + 'PROPERTY_DEFINITION_REPRESENTATION.' + 'DEFINITION') |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_DEFINITION_REPRESENTATION' IN TYPEOF(pdr)));

END_REPEAT;

RETURN (pdr_set);

END_FUNCTION;

FUNCTION item_in_context

(item  : representation_item;

cntxt : representation_context) : BOOLEAN;

LOCAL

y : BAG OF representation_item;

END_LOCAL;

-- If there is one or more representation using both the item

-- and cntxt return true.

IF SIZEOF(USEDIN(item,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION.ITEMS')

* cntxt.representations_in_context) > 0 THEN

RETURN (TRUE);

-- Determine the bag of representation_items that reference

-- item

ELSE y := QUERY(z <* USEDIN (item , '') |

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION_ITEM' IN TYPEOF(z));

-- Ensure that the bag is not empty

IF SIZEOF(y) > 0 THEN

-- For each element in the bag

REPEAT i := 1 TO HIINDEX(y);

-- Check to see it is an item in the input cntxt.

IF item_in_context(y[i], cntxt) THEN

RETURN (TRUE);

END_IF;

END_REPEAT;

END_IF;

END_IF;

-- Return false when all possible branches have been checked

-- with no success.

RETURN (FALSE);

END_FUNCTION;

FUNCTION leap_year

(year : year_number) : BOOLEAN;

IF ((((year MOD 4) = 0) AND ((year MOD 100) <> 0)) OR ((year MOD 400) = 0)) THEN

RETURN (TRUE);

ELSE

RETURN (FALSE);

END_IF;

END_FUNCTION;

FUNCTION list_face_loops(f: face) : LIST[0:?] OF loop;

LOCAL

loops : LIST[0:?] OF loop := [];

END_LOCAL;

REPEAT i := 1 TO SIZEOF(f.bounds);

loops := loops +(f.bounds[i].bound);

END_REPEAT;

RETURN(loops);

END_FUNCTION;

FUNCTION list_of_topology_reversed (a_list

: list_of_reversible_topology_item)

: list_of_reversible_topology_item;

LOCAL

the_reverse : list_of_reversible_topology_item;

END_LOCAL;

the_reverse := [];

REPEAT i := 1 TO SIZEOF (a_list);

the_reverse := topology_reversed (a_list [i]) + the_reverse;

END_REPEAT;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION list_to_array(lis : LIST [0:?] OF GENERIC : T;

low,u : INTEGER) : ARRAY [low:u] OF GENERIC : T;

LOCAL

n   : INTEGER;

res : ARRAY [low:u] OF GENERIC : T;

END_LOCAL;

n := SIZEOF(lis);

IF (n <> (u-low +1)) THEN

RETURN(?);

ELSE

res := [lis[1] : n];

REPEAT i := 2 TO n;

res[low+i-1] := lis[i];

END_REPEAT;

RETURN(res);

END_IF;

END_FUNCTION;

FUNCTION list_to_set(l : LIST [0:?] OF GENERIC:T) : SET OF GENERIC:T;

LOCAL

s : SET OF GENERIC:T := [];

END_LOCAL;

REPEAT i := 1 TO SIZEOF(l);

s := s + l[i];

END_REPEAT;

RETURN(s);

END_FUNCTION;

FUNCTION make_array_of_array(lis : LIST[1:?] OF LIST [1:?] OF GENERIC : T;

low1, u1, low2, u2 : INTEGER):

ARRAY [low1:u1] OF ARRAY [low2:u2] OF GENERIC : T;

LOCAL

res   : ARRAY[low1:u1] OF ARRAY [low2:u2] OF GENERIC : T;

END_LOCAL;

(* Check input dimensions for consistency *)

IF (u1-low1+1) <> SIZEOF(lis) THEN

RETURN (?);

END_IF;

IF (u2 - low2 + 1 ) <> SIZEOF(lis[1]) THEN

RETURN (?) ;

END_IF;

(* Initialise res with values from lis[1] *)

res := [list_to_array(lis[1], low2, u2) : (u1-low1 + 1)];

REPEAT i := 2 TO HIINDEX(lis);

IF (u2-low2+1) <> SIZEOF(lis[i]) THEN

RETURN (?);

END_IF;

res[low1+i-1] := list_to_array(lis[i], low2, u2);

END_REPEAT;

RETURN (res);

END_FUNCTION;

FUNCTION mixed_loop_type_set(l: SET[0:?] OF loop): LOGICAL;

LOCAL

poly_loop_type: LOGICAL;

END_LOCAL;

IF(SIZEOF(l) <= 1) THEN

RETURN(FALSE);

END_IF;

poly_loop_type := ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLY_LOOP' IN TYPEOF(l[1]));

REPEAT i := 2 TO SIZEOF(l);

IF(('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLY_LOOP' IN TYPEOF(l[i])) <> poly_loop_type)

THEN

RETURN(TRUE);

END_IF;

END_REPEAT;

RETURN(FALSE);

END_FUNCTION;

FUNCTION msb_shells (brep: manifold_solid_brep) :

SET [1:?] OF  closed_shell;

IF SIZEOF (QUERY (msbtype <* TYPEOF (brep) |

msbtype LIKE '*BREP_WITH_VOIDS')) >= 1 THEN

RETURN (brep\brep_with_voids.voids + brep.outer);

ELSE

RETURN([brep.outer]);

END_IF;

END_FUNCTION;

FUNCTION msf_curve_check (cv : representation_item) : BOOLEAN;

(* This function varifies the validity of a curve in the context of a

manifold surface model. Representation_items are

valid input, however, they are supposed to be curves; otherwise

this function will return false.

*)

(* complex subtypes of curve that are both bounded_curve and

oneof conic, curve_replica, line, or offset_curve_3d are not

valid

*)

IF SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.BOUNDED_CURVE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D'] * TYPEOF(cv)) > 1 THEN

RETURN(FALSE);

END_IF;

(* b_spline_curves shall not self-intersect

*)

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE' IN TYPEOF (cv)) AND

(cv\b_spline_curve.self_intersect = FALSE)OR

(cv\b_spline_curve.self_intersect = UNKNOWN)) THEN

RETURN(TRUE);

ELSE

(* conics and lines are valid curve types

*)

IF SIZEOF (['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE']

* TYPEOF (cv)) = 1 THEN

RETURN(TRUE);

ELSE

(* a curve_replica shall reference a valid curve

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA' IN TYPEOF(cv) THEN

RETURN (msf_curve_check(cv\curve_replica.parent_curve));

ELSE

(* an offset_curve_3d shall not self-intersect and

shall reference a valid curve; a polyline is not a

valid basis_curve

*)

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D' IN TYPEOF (cv))

AND

((cv\offset_curve_3d.self_intersect = FALSE) OR

(cv\offset_curve_3d.self_intersect = UNKNOWN))

AND

(NOT ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF

(cv\offset_curve_3d.basis_curve)))) THEN

RETURN (msf_curve_check(cv\offset_curve_3d.basis_curve));

ELSE

(* a pcurve shall reference a valid curve and a valid

basis_surface

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF(cv) THEN

RETURN ((msf_curve_check

(cv\pcurve.reference_to_curve\representation.items[1])) AND

(msf_surface_check(cv\pcurve.basis_surface)));

ELSE

(* a surface_curve references a curve_3d and one or

two pcurves or one or two surfaces or one of

each; all of these references shall be valid

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_CURVE' IN TYPEOF(cv) THEN

(* if the curve reference is correct, check also the rest

*)

IF msf_curve_check(cv\surface_curve.curve_3d) THEN

REPEAT i := 1 TO SIZEOF

(cv\surface_curve.associated_geometry);

(* do for one or two associated_geometrys:

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE' IN

TYPEOF (cv\surface_curve.associated_geometry[i]) THEN

IF NOT msf_surface_check

(cv\surface_curve.associated_geometry[i]) THEN

RETURN(FALSE);

END_IF;

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PCURVE' IN TYPEOF

(cv\surface_curve.associated_geometry[i]) THEN

IF NOT msf_curve_check

(cv\surface_curve.associated_geometry[i]) THEN

RETURN(FALSE);

END_IF;

END_IF;

END_IF;

END_REPEAT;

RETURN(TRUE);

END_IF;

ELSE

(* a polyline shall have at least 3 points

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' IN TYPEOF(cv) THEN

IF (SIZEOF (cv\polyline.points) >= 3) THEN RETURN (TRUE);

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

(* FALSE is returned if the input parameter cv is not a valid curve.

*)

RETURN (FALSE);

END_FUNCTION;

FUNCTION msf_surface_check (surf : surface) : BOOLEAN;

(* This function varifies the validity of a surface in the

context of a manifold surface model.

*)

(* elementary_surfaces are valid surface types

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELEMENTARY_SURFACE' IN TYPEOF(surf) THEN

RETURN(TRUE);

ELSE

(* a swept_surface shall have a valid sweeping curve

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SWEPT_SURFACE' IN TYPEOF (surf) THEN

RETURN (msf_curve_check(surf\swept_surface.swept_curve));

ELSE

(* an offset_surface shall not self-intersect and shall

reference a valid surface

*)

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_SURFACE' IN TYPEOF (surf)) AND

(surf\offset_surface.self_intersect = FALSE) OR

(surf\offset_surface.self_intersect = UNKNOWN)) THEN

RETURN (msf_surface_check(surf\offset_surface.basis_surface));

ELSE

(* a surface_replica shall have a valid parent surface

*)

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_REPLICA' IN TYPEOF(surf) THEN

RETURN(msf_surface_check(surf\surface_replica.parent_surface));

ELSE

(* a b_spline_surface shall not self-intersect

*)

IF (('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_SURFACE' IN TYPEOF(surf)) AND

(surf\b_spline_surface.self_intersect = FALSE) OR

(surf\b_spline_surface.self_intersect = UNKNOWN)) THEN

RETURN(TRUE);

END_IF;

END_IF;

END_IF;

END_IF;

END_IF;

RETURN(FALSE);

END_FUNCTION;

FUNCTION normalise (arg : vector_or_direction) : vector_or_direction;

LOCAL

ndim   : INTEGER;

v      : direction;

result : vector_or_direction;

vec    : vector;

mag    : REAL;

END_LOCAL;

IF NOT EXISTS (arg) THEN

result := ?;

(* When function is called with invalid data a NULL result is returned *)

ELSE

ndim := arg.dim;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VECTOR' IN TYPEOF(arg) THEN

BEGIN

v := dummy_gri || direction(arg.orientation.direction_ratios);

IF arg.magnitude = 0.0 THEN

RETURN(?);

ELSE

vec := dummy_gri || vector (v, 1.0);

END_IF;

END;

ELSE

v := dummy_gri || direction (arg.direction_ratios);

END_IF;

mag := 0.0;

REPEAT  i := 1 TO ndim;

mag := mag + v.direction_ratios[i]*v.direction_ratios[i];

END_REPEAT;

IF mag > 0.0 THEN

mag := SQRT(mag);

REPEAT  i := 1 TO ndim;

v.direction_ratios[i] := v.direction_ratios[i]/mag;

END_REPEAT;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VECTOR' IN TYPEOF(arg) THEN

vec.orientation := v;

result := vec;

ELSE

result := v;

END_IF;

ELSE

RETURN(?);

END_IF;

END_IF;

RETURN (result);

END_FUNCTION;

FUNCTION open_shell_reversed ( a_shell : open_shell) :

oriented_open_shell;

LOCAL

the_reverse : oriented_open_shell;

END_LOCAL;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_OPEN_SHELL' IN TYPEOF (a_shell) ) THEN

the_reverse := dummy_tri ||

connected_face_set (

a_shell\connected_face_set.cfs_faces) ||

open_shell () || oriented_open_shell(

a_shell\oriented_open_shell.open_shell_element,

(NOT (a_shell\oriented_open_shell.orientation)));

ELSE

the_reverse := dummy_tri ||

connected_face_set (

a_shell\connected_face_set.cfs_faces) ||

open_shell () ||  oriented_open_shell (a_shell, FALSE);

END_IF;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION orthogonal_complement(vec : direction) : direction;

LOCAL

result :  direction ;

END_LOCAL;

IF (vec.dim <> 2) OR NOT EXISTS (vec) THEN

RETURN(?);

ELSE

result := dummy_gri || direction([-vec.direction_ratios[2],

vec.direction_ratios[1]]);

RETURN(result);

END_IF;

END_FUNCTION;

FUNCTION path_head_to_tail(a_path : path) : LOGICAL;

LOCAL

n : INTEGER;

p : LOGICAL := TRUE;

END_LOCAL;

n := SIZEOF (a_path.edge_list);

REPEAT i := 2 TO n;

p := p AND (a_path.edge_list[i-1].edge_end :=:

a_path.edge_list[i].edge_start);

END_REPEAT;

RETURN (p);

END_FUNCTION;

FUNCTION path_reversed (a_path : path) : oriented_path;

LOCAL

the_reverse : oriented_path ;

END_LOCAL;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ORIENTED_PATH' IN TYPEOF (a_path) ) THEN

the_reverse := dummy_tri ||

path(list_of_topology_reversed (a_path.edge_list)) ||

oriented_path(a_path\oriented_path.path_element,

NOT(a_path\oriented_path.orientation)) ;

ELSE

the_reverse := dummy_tri ||

path(list_of_topology_reversed (a_path.edge_list)) ||

oriented_path(a_path, FALSE);

END_IF;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION representations_mapped_into

(rep : representation) : SET of representation;

LOCAL

results : SET OF representation := [];

rm      : SET OF representation_map;

mi      : SET OF mapped_item := [];

END_LOCAL;

-- Find set of representation_maps which specify the representation

rm := bag_to_set(USEDIN(rep, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'REPRESENTATION_MAP.MAPPED_REPRESENTATION'));

-- Find the set of mapped_items that use each representation_map

REPEAT i := 1 TO HIINDEX(rm);

mi := mi + rm[i].map_usage;

END_REPEAT;

-- Find the set of representations that use each mapped_item

REPEAT j := 1 TO HIINDEX(mi);

results := results + USEDIN(mi[j],'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.' +

'REPRESENTATION.ITEMS');

END_REPEAT;

RETURN(results);

END_FUNCTION;

FUNCTION scalar_times_vector (scalar : REAL; vec : vector_or_direction)

: vector;

LOCAL

v      : direction;

mag    : REAL;

result : vector;

END_LOCAL;

IF NOT EXISTS (scalar) OR NOT EXISTS (vec) THEN

RETURN (?) ;

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VECTOR' IN TYPEOF (vec) THEN

v   := dummy_gri || direction(vec.orientation.direction_ratios);

mag := scalar * vec.magnitude;

ELSE

v   := dummy_gri || direction(vec.direction_ratios);

mag := scalar;

END_IF;

IF (mag < 0.0 ) THEN

REPEAT i := 1 TO SIZEOF(v.direction_ratios);

v.direction_ratios[i] := -v.direction_ratios[i];

END_REPEAT;

mag := -mag;

END_IF;

result := dummy_gri || vector(normalise(v), mag);

END_IF;

RETURN (result);

END_FUNCTION;

FUNCTION second_proj_axis(z_axis, x_axis, arg: direction) : direction;

LOCAL

y_axis : vector;

v      : direction;

temp   : vector;

END_LOCAL;

IF NOT EXISTS(arg) THEN

v := dummy_gri || direction([0.0,1.0,0.0]);

ELSE

v := arg;

END_IF;

temp   := scalar_times_vector(dot_product(v, z_axis), z_axis);

y_axis := vector_difference(v, temp);

temp   := scalar_times_vector(dot_product(v, x_axis), x_axis);

y_axis := vector_difference(y_axis, temp);

y_axis := normalise(y_axis);

RETURN(y_axis.orientation);

END_FUNCTION;

FUNCTION set_of_topology_reversed (a_set : set_of_reversible_topology_item)

: set_of_reversible_topology_item;

LOCAL

the_reverse : set_of_reversible_topology_item;

END_LOCAL;

the_reverse := [];

REPEAT i := 1 TO SIZEOF (a_set);

the_reverse := the_reverse + topology_reversed (a_set [i]);

END_REPEAT;

RETURN (the_reverse);

END_FUNCTION;

FUNCTION shell_reversed (a_shell : shell) : shell;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OPEN_SHELL' IN TYPEOF (a_shell) ) THEN

RETURN (open_shell_reversed (a_shell));

ELSE

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CLOSED_SHELL' IN TYPEOF (a_shell) ) THEN

RETURN (closed_shell_reversed (a_shell));

ELSE

RETURN (?);

END_IF;

END_IF;

END_FUNCTION;

FUNCTION surface_weights_positive(b: rational_b_spline_surface) : BOOLEAN;

LOCAL

result        : BOOLEAN := TRUE;

END_LOCAL;

REPEAT i := 0 TO b.u_upper;

REPEAT j := 0 TO b.v_upper;

IF (b.weights[i][j] <= 0.0)  THEN

result := FALSE;

RETURN(result);

END_IF;

END_REPEAT;

END_REPEAT;

RETURN(result);

END_FUNCTION;

FUNCTION topology_reversed (an_item : reversible_topology)

: reversible_topology;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.EDGE' IN TYPEOF (an_item)) THEN

RETURN (edge_reversed (an_item));

END_IF;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PATH' IN TYPEOF (an_item)) THEN

RETURN (path_reversed (an_item));

END_IF;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE_BOUND' IN TYPEOF (an_item)) THEN

RETURN (face_bound_reversed (an_item));

END_IF;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FACE' IN TYPEOF (an_item)) THEN

RETURN (face_reversed (an_item));

END_IF;

IF ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHELL' IN TYPEOF (an_item)) THEN

RETURN (shell_reversed (an_item));

END_IF;

IF ('SET' IN TYPEOF (an_item)) THEN

RETURN (set_of_topology_reversed (an_item));

END_IF;

IF ('LIST' IN TYPEOF (an_item)) THEN

RETURN (list_of_topology_reversed (an_item));

END_IF;

RETURN (?);

END_FUNCTION;

FUNCTION type_check_function

(the_type : GENERIC; sub_names : SET OF STRING; criterion : INTEGER) : LOGICAL;

IF (( NOT EXISTS ( the_type ) ) OR (NOT ({0<= criterion <=3})) OR

(SIZEOF ( sub_names ) = 0 ) ) THEN RETURN (UNKNOWN);

ELSE

CASE criterion OF

0: RETURN (SIZEOF ( sub_names * TYPEOF (the_type) ) > 0);

1: RETURN (SIZEOF ( sub_names * TYPEOF (the_type) ) = 0);

2: RETURN (SIZEOF ( sub_names * TYPEOF (the_type) ) = 1);

3: RETURN (SIZEOF ( sub_names * TYPEOF (the_type) ) <= 1);

END_CASE;

END_IF;

END_FUNCTION;

FUNCTION using_items (item : founded_item_select;

checked_items: SET OF founded_item_select)

: SET OF founded_item_select;

LOCAL

new_check_items    : SET OF founded_item_select;

result_items       : SET OF founded_item_select;

next_items         : SET OF founded_item_select;

END_LOCAL;

result_items := [];

new_check_items := checked_items + item;

-- Find the set of representation_items or founded_items

-- in which item is used directly.

next_items := QUERY(z <* bag_to_set( USEDIN(item , '')) |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION_ITEM' IN TYPEOF(z)) OR

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FOUNDED_ITEM'        IN TYPEOF(z)));

-- If the set of next_items is not empty;

IF SIZEOF(next_items) > 0 THEN

-- For each element in the set, find the using_items recursively

REPEAT i := 1 TO HIINDEX(next_items);

-- Check for loop in data model, i.e. one of the next_items

-- occurred earlier in the set of check_items;

IF NOT(next_items[i] IN new_check_items) THEN

result_items := result_items + next_items[i] +

using_items(next_items[i],new_check_items);

END_IF;

END_REPEAT;

END_IF;

-- return the set of representation_items or founded_items

-- in which the input item is used directly and indirectly.

RETURN (result_items);

END_FUNCTION;

FUNCTION using_representations (item : founded_item_select)

: SET OF representation;

LOCAL

results            : SET OF representation;

result_bag         : BAG OF representation;

intermediate_items : SET OF founded_item_select;

END_LOCAL;

-- Find the representations in which the item is used and add to the

-- results set.

results := [];

result_bag :=

USEDIN(item,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION.ITEMS');

IF SIZEOF(result_bag) > 0 THEN

REPEAT i := 1 TO HIINDEX(result_bag);

results := results + result_bag[i];

END_REPEAT;

END_IF;

-- Find all representation_items or founded_items

-- by which item is referenced directly or indirectly.

intermediate_items := using_items(item,[]);

-- If the set of intermediate items is not empty;

IF SIZEOF(intermediate_items) > 0 THEN

-- For each element in the set, add the

-- representations of that element.

REPEAT i := 1 TO HIINDEX(intermediate_items);

result_bag := USEDIN(intermediate_items[i],

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.REPRESENTATION.ITEMS');

IF SIZEOF(result_bag) > 0 THEN

REPEAT j := 1 TO HIINDEX(result_bag);

results := results + result_bag[j];

END_REPEAT;

END_IF;

END_REPEAT;

END_IF;

-- Return the set of representation in which the input item is

-- used directly and indirectly (through intervening

-- representation_items or founded items).

RETURN (results);

END_FUNCTION;

FUNCTION valid_calendar_date

(date : calendar_date) : LOGICAL;

CASE date.month_component OF

1  : RETURN({ 1 <= date.day_component <= 31 });

2  : BEGIN

IF (leap_year(date.year_component)) THEN

RETURN({ 1 <= date.day_component <= 29 });

ELSE

RETURN({ 1 <= date.day_component <= 28 });

END_IF;

END;

3  : RETURN({ 1 <= date.day_component <= 31 });

4  : RETURN({ 1 <= date.day_component <= 30 });

5  : RETURN({ 1 <= date.day_component <= 31 });

6  : RETURN({ 1 <= date.day_component <= 30 });

7  : RETURN({ 1 <= date.day_component <= 31 });

8  : RETURN({ 1 <= date.day_component <= 31 });

9  : RETURN({ 1 <= date.day_component <= 30 });

10 : RETURN({ 1 <= date.day_component <= 31 });

11 : RETURN({ 1 <= date.day_component <= 30 });

12 : RETURN({ 1 <= date.day_component <= 31 });

END_CASE;

RETURN (FALSE);

END_FUNCTION;

FUNCTION valid_datum_target_parameters

(pdf : placed_datum_target_feature) : BOOLEAN;

LOCAL

rep_set : SET OF representation := [] ;

parameter_representations: SET OF representation;

END_LOCAL;

REPEAT i := 1 TO HIINDEX(pdf.representation_associations);

rep_set := rep_set + pdf.representation_associations[i].used_representation;

END_REPEAT;

parameter_representations := QUERY(rep <* rep_set |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SHAPE_REPRESENTATION_WITH_PARAMETERS' IN

TYPEOF(rep)));

IF (SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF( QUERY( i <* srwp.items |

(i.name='orientation') AND

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLACEMENT' IN TYPEOF(i)))) = 1))) <> 1) THEN

RETURN(FALSE);

END_IF;

CASE pdf\shape_aspect.description OF

'point': RETURN(SIZEOF(QUERY( srwp <* parameter_representations |

(SIZEOF(srwp.items) = 1))) = 1);

'circle': RETURN((SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF(srwp.items) = 2))) = 1) AND

(SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF( QUERY( i <* srwp.items |

(i.name='target diameter') AND

(SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_MEASURE_WITH_UNIT']*TYPEOF(i)

) = 2) )) = 1))) = 1));

'line': RETURN(SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF( QUERY( i <* srwp.items |

(i.name='target length') AND

(SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_MEASURE_WITH_UNIT']*TYPEOF(i)

) = 2) )) = 1))) = 1);

'rectangle': RETURN((SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF(srwp.items)= 3))) = 1) AND

(SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF( QUERY( i <* srwp.items |

(i.name='target length') AND

(SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_MEASURE_WITH_UNIT']*TYPEOF(i)

) = 2))) = 1))) = 1) AND

(SIZEOF( QUERY( srwp <* parameter_representations |

(SIZEOF( QUERY( i <* srwp.items |

(i.name='target width') AND

(SIZEOF(['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM',

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_MEASURE_WITH_UNIT']*TYPEOF(i)

) = 2))) = 1) )) = 1));

OTHERWISE : RETURN(FALSE);

END_CASE;

END_FUNCTION;

FUNCTION valid_geometrically_bounded_wf_curve

(

crv : curve ) : BOOLEAN ;

IF SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELLIPSE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CIRCLE' ] * TYPEOF (crv)) = 1 THEN

RETURN (TRUE);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TRIMMED_CURVE' IN TYPEOF (crv) THEN

IF SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PARABOLA', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.HYPERBOLA' ] * TYPEOF (crv\trimmed_curve.basis_curve)) = 1 THEN

RETURN (TRUE);

ELSE

RETURN (valid_geometrically_bounded_wf_curve(crv\trimmed_curve.basis_curve));

END_IF ;

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D' IN TYPEOF (crv) THEN

RETURN (valid_geometrically_bounded_wf_curve(crv\offset_curve_3d.basis_curve));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA' IN TYPEOF (crv) THEN

RETURN (valid_geometrically_bounded_wf_curve(crv\curve_replica.parent_curve));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOSITE_CURVE' IN TYPEOF (crv) THEN

RETURN ( SIZEOF (

QUERY ( ccs <* crv\composite_curve.segments| NOT valid_geometrically_bounded_wf_curve(ccs.parent_curve) )) = 0);

END_IF ;

END_IF ;

END_IF ;

END_IF ;

END_IF ;

RETURN (FALSE);

END_FUNCTION;

FUNCTION valid_geometrically_bounded_wf_point

(

pnt : point ) : BOOLEAN ;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF (pnt) THEN

RETURN (TRUE);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_ON_CURVE' IN TYPEOF (pnt) THEN

RETURN (valid_geometrically_bounded_wf_curve(pnt\point_on_curve.basis_curve));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_REPLICA' IN TYPEOF (pnt) THEN

RETURN (valid_geometrically_bounded_wf_point(pnt\point_replica.parent_pt));

END_IF ;

END_IF ;

END_IF ;

RETURN (FALSE);

END_FUNCTION;

FUNCTION valid_measure_value

(m : measure_value) : BOOLEAN;

IF ('REAL' IN TYPEOF (m)) THEN

RETURN (m > 0.0);

ELSE

IF ('INTEGER' IN TYPEOF (m)) THEN

RETURN (m > 0);

ELSE

RETURN (TRUE);

END_IF;

END_IF;

END_FUNCTION;

FUNCTION valid_time

(time : local_time) : BOOLEAN;

IF EXISTS(time.second_component) THEN

RETURN (EXISTS(time.minute_component));

ELSE

RETURN (TRUE);

END_IF;

END_FUNCTION;

FUNCTION valid_units

(m : measure_with_unit) : BOOLEAN;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LENGTH_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 1.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MASS_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 1.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TIME_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 1.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ELECTRIC_CURRENT_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 1.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.THERMODYNAMIC_TEMPERATURE_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CELSIUS_TEMPERATURE_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AMOUNT_OF_SUBSTANCE_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 0.0, 1.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LUMINOUS_INTENSITY_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 1.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PLANE_ANGLE_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SOLID_ANGLE_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.AREA_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 2.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VOLUME_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 3.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.RATIO_MEASURE' IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POSITIVE_LENGTH_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 1.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POSITIVE_PLANE_ANGLE_MEASURE'

IN TYPEOF ( m.value_component ) THEN

IF derive_dimensional_exponents ( m.unit_component ) <>

dimensional_exponents ( 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0 ) THEN

RETURN (FALSE);

END_IF;

END_IF;

RETURN (TRUE);

END_FUNCTION;

FUNCTION valid_wireframe_edge_curve

(

crv : curve ) : BOOLEAN ;

IF SIZEOF ([ 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONIC', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.B_SPLINE_CURVE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POLYLINE' ] * TYPEOF (crv)) = 1 THEN

RETURN (TRUE);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_REPLICA' IN TYPEOF (crv) THEN

RETURN (valid_wireframe_edge_curve(crv\curve_replica.parent_curve));

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.OFFSET_CURVE_3D' IN TYPEOF (crv) THEN

RETURN (valid_wireframe_edge_curve(crv\offset_curve_3d.basis_curve));

END_IF ;

END_IF ;

END_IF ;

RETURN (FALSE);

END_FUNCTION;

FUNCTION valid_wireframe_vertex_point

(

pnt : point ) : BOOLEAN ;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CARTESIAN_POINT' IN TYPEOF (pnt) THEN

RETURN (TRUE);

ELSE

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POINT_REPLICA' IN TYPEOF (pnt) THEN

RETURN (valid_wireframe_vertex_point(pnt\point_replica.parent_pt));

END_IF ;

END_IF ;

RETURN (FALSE);

END_FUNCTION;

FUNCTION value_range_wr1

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF (SIZEOF(agg) = 2) AND ((SIZEOF(QUERY (i1 <* agg | (

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF

(i1)))) = 2) OR

(SIZEOF(QUERY (i2 <* agg | (

'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VALUE_REPRESENTATION_ITEM' IN TYPEOF

(i2)))) = 2)) THEN

RETURN(TRUE);

ELSE

RETURN(FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION value_range_wr2

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF (SIZEOF(QUERY (i <* agg | (i.name = 'upper limit'))) = 1)

AND (SIZEOF(QUERY (i <* agg | (i.name = 'lower limit'))) = 1)

THEN

RETURN(TRUE);

ELSE

RETURN(FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION value_range_wr3

(agg : compound_item_definition) : BOOLEAN;

BEGIN

IF (SIZEOF(QUERY(i1 <* agg |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF (i1)) AND

(SIZEOF (QUERY (i2 <* agg |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM' IN TYPEOF (i2)) AND

(i1 :<>: i2) AND (i1\measure_with_unit.unit_component :=: i2\measure_with_unit.unit_component))) = 1))) = 2)

THEN

RETURN (TRUE);

ELSE

RETURN (FALSE);

END_IF;

END;

END_FUNCTION;

FUNCTION vector_difference(arg1, arg2 : vector_or_direction) : vector;

LOCAL

result          : vector;

res, vec1, vec2 : direction;

mag, mag1, mag2 : REAL;

ndim            : INTEGER;

END_LOCAL;

IF ((NOT EXISTS (arg1)) OR (NOT EXISTS (arg2))) OR (arg1.dim <> arg2.dim)

THEN

RETURN (?) ;

ELSE

BEGIN

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VECTOR' IN TYPEOF(arg1) THEN

mag1 := arg1.magnitude;

vec1 := arg1.orientation;

ELSE

mag1 := 1.0;

vec1 := arg1;

END_IF;

IF 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VECTOR' IN TYPEOF(arg2) THEN

mag2 := arg2.magnitude;

vec2 := arg2.orientation;

ELSE

mag2 := 1.0;

vec2 := arg2;

END_IF;

vec1 := normalise (vec1);

vec2 := normalise (vec2);

ndim := SIZEOF(vec1.direction_ratios);

mag := 0.0;

res := dummy_gri || direction(vec1.direction_ratios);

REPEAT i := 1 TO ndim;

res.direction_ratios[i] := mag1*vec1.direction_ratios[i] +

mag2*vec2.direction_ratios[i];

mag := mag + (res.direction_ratios[i]*res.direction_ratios[i]);

END_REPEAT;

IF (mag > 0.0 ) THEN

result := dummy_gri || vector( res, SQRT(mag));

ELSE

result := dummy_gri || vector( vec1,  0.0);

END_IF;

END;

END_IF;

RETURN (result);

END_FUNCTION;

RULE compatible_dimension FOR

(cartesian_point,

direction,

representation_context,

geometric_representation_context);

WHERE

-- ensure that the count of coordinates of each cartesian_point

-- matches the coordinate_space_dimension of each geometric_context in

-- which it is geometrically founded

WR1: SIZEOF(QUERY(x <* cartesian_point| SIZEOF(QUERY

(y <* geometric_representation_context | item_in_context(x,y) AND

(HIINDEX(x.coordinates) <> y.coordinate_space_dimension))) > 0 )) =0;

-- ensure that the count of direction_ratios of each direction

-- matches the coordinate_space_dimension of each geometric_context in

-- which it is geometrically founded

WR2: SIZEOF(QUERY(x <* direction | SIZEOF( QUERY

(y <* geometric_representation_context | item_in_context(x,y) AND

(HIINDEX(x.direction_ratios) <> y.coordinate_space_dimension)))

> 0 )) = 0;

END_RULE;

RULE consistent_uncertainty

FOR (global_uncertainty_assigned_context,

qualified_representation_item,

uncertainty_assigned_representation);

WHERE

WR1: SIZEOF ( QUERY ( guac <* global_uncertainty_assigned_context |

SIZEOF ( QUERY ( u1 <* guac.uncertainty |

SIZEOF ( QUERY ( u2 <* guac.uncertainty | u2.name =  u1.name ) ) >1 ) ) >0 ) ) =  0 ;

WR2: SIZEOF ( QUERY ( uar <* uncertainty_assigned_representation |

SIZEOF ( QUERY ( u1<* uar.uncertainty |

SIZEOF ( QUERY ( u2 <* uar.uncertainty | u2.name =  u1.name ) ) >1 ) ) >0 ) ) =  0;

WR3: SIZEOF ( QUERY ( qri <* qualified_representation_item |

SIZEOF ( QUERY ( u1 <* qri.qualifiers |

('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF' + '.UNCERTAINTY_QUALIFIER' IN TYPEOF ( u1 ) ) AND

( SIZEOF ( QUERY ( u2 <* qri.qualifiers |

( 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF' + '.UNCERTAINTY_QUALIFIER' IN TYPEOF ( u2 ) ) AND

( u2\uncertainty_qualifier.measure_name =  u1\uncertainty_qualifier.measure_name ) )

) >1 ) ) ) >0 ) ) =  0;

END_RULE;

RULE restrict_language_assignment_per_attribute FOR (attribute_language_assignment);

WHERE

WR1: SIZEOF ( QUERY ( ala1 <* attribute_language_assignment |

SIZEOF(QUERY( it <* ala1.items |

SIZEOF ( QUERY ( ala2 <* USEDIN ( it ,'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ATTRIBUTE_LANGUAGE_ASSIGNMENT.ITEMS' ) |

( ala1\attribute_classification_assignment.attribute_name = ala2\attribute_classification_assignment.attribute_name ) AND

( ala1\attribute_classification_assignment.assigned_class :=: ala2\attribute_classification_assignment.assigned_class )

)) >1

)) >0

)) =0;

END_RULE;

RULE styled_curve FOR

(styled_item);

WHERE

WR1: SIZEOF( QUERY( si <* styled_item | ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE' IN TYPEOF (si.item)) AND (SIZEOF (QUERY (psa <* si.styles | (SIZEOF (QUERY (cs <* psa.styles | ('CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CURVE_STYLE' IN TYPEOF (cs)) )) > 0) )) <> 1) )) = 0;

END_RULE;

RULE subtype_exclusiveness_geometric_tolerance FOR

(geometric_tolerance);

WHERE

WR1: SIZEOF(QUERY (gt <* geometric_tolerance | NOT (type_check_function(gt, ['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANGULARITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CIRCULAR_RUNOUT_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COAXIALITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONCENTRICITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CYLINDRICITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FLATNESS_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE_PROFILE_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PARALLELISM_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PERPENDICULARITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POSITION_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ROUNDNESS_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STRAIGHTNESS_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_PROFILE_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMMETRY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TOTAL_RUNOUT_TOLERANCE'] , 3)))) = 0;

END_RULE;

RULE subtype_exclusiveness_representation_item FOR

(representation_item);

WHERE

WR1: SIZEOF(QUERY (cri <* representation_item | NOT (type_check_function(cri,['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.MEASURE_REPRESENTATION_ITEM','CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.VALUE_REPRESENTATION_ITEM','CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COMPOUND_REPRESENTATION_ITEM'] , 3)))) = 0;

END_RULE;

RULE subtype_mandatory_geometric_tolerance FOR

(geometric_tolerance);

WHERE

WR1: SIZEOF(QUERY (gt <* geometric_tolerance | NOT (type_check_function(gt, ['CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ANGULARITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CIRCULAR_RUNOUT_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.COAXIALITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CONCENTRICITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.CYLINDRICITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.FLATNESS_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.LINE_PROFILE_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PARALLELISM_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.PERPENDICULARITY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.POSITION_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.ROUNDNESS_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.STRAIGHTNESS_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SURFACE_PROFILE_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.SYMMETRY_TOLERANCE', 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TOTAL_RUNOUT_TOLERANCE'] , 0)))) = 0;

END_RULE;

RULE text_font_usage FOR

(externally_defined_text_font,pre_defined_text_font);

WHERE

WR1: SIZEOF (QUERY (pdtf <* pre_defined_text_font | SIZEOF (USEDIN (pdtf, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL.FONT')) = 0 )) = 0;

WR2: SIZEOF (QUERY (edtf <* externally_defined_text_font | SIZEOF (USEDIN (edtf, 'CONFIGURATION_CONTROL_3D_DESIGN_ED2_MIM_LF.TEXT_LITERAL.FONT')) = 0 )) = 0;

END_RULE;

(*** 2003=>1994 conversion: insert a rule to control if instances are legal according to USE/REF clauses ***)

RULE validate_dependently_instantiable_entity_data_types FOR

(application_context_element,area_in_set,attribute_value_role,bounded_curve,bounded_surface,camera_image,camera_model_d3,cartesian_transformation_operator,classification_role,connected_edge_set,contract_type,document_type,document_usage_constraint,event_occurrence_role,local_time,loop,one_direction_repeat_factor,oriented_face,oriented_open_shell,oriented_path,planar_box,pre_defined_item,presentation_set,product_definition_context_role,product_definition_effectivity,runout_zone_orientation,solid_model,swept_face_solid,tolerance_zone_form,two_direction_repeat_factor,vertex,view_volume --<list this first and all subsequent relevant referencedentity data types here>

);

LOCAL

number_of_input_instances : INTEGER;

previous_in_chain : LIST OF GENERIC := [];

set_of_input_types : SET OF STRING := [];

all_instances : SET OF GENERIC := [];

END_LOCAL;

all_instances := application_context_element + area_in_set + attribute_value_role + bounded_curve + bounded_surface + camera_image + camera_model_d3 + cartesian_transformation_operator + classification_role + connected_edge_set + contract_type + document_type + document_usage_constraint + event_occurrence_role + local_time + loop + one_direction_repeat_factor + oriented_face + oriented_open_shell + oriented_path + planar_box + pre_defined_item + presentation_set + product_definition_context_role + product_definition_effectivity + runout_zone_orientation + solid_model + swept_face_solid + tolerance_zone_form + two_direction_repeat_factor + vertex + view_volume;--<make a union of all implicit populations of the FOR-clause>

number_of_input_instances := SIZEOF(all_instances);

(* Collect all type strings of all FOR instances into one set. *)

REPEAT i:=1 TO number_of_input_instances;

set_of_input_types := set_of_input_types + TYPEOF(all_instances[i]);

END_REPEAT;

WHERE

WR1: dependently_instantiated(all_instances, set_of_input_types,

previous_in_chain);

END_RULE;

FUNCTION dependently_instantiated(

set_of_input_instances : SET OF GENERIC:igen;

set_of_input_types     : SET OF STRING;

previous_in_chain      : LIST OF GENERIC:cgen): BOOLEAN;

(*'dependently_instantiated' To test whether all instances in the

input set_of_input_instances are referenced by independently

instantiable instances. If so, this function returns true.

Set_of_input_types includes the type strings for all input instances.

The instances in previous_in_chain are used to detect cyclic

references during recursive calls to this function. The parameter

lists already tested instances in a chain of references.

*)

LOCAL

number_of_input_instances     : INTEGER;

number_of_referring_instances : INTEGER;

bag_of_referring_instances    : BAG OF GENERIC:igen := [];

dependently_instantiated_flag : BOOLEAN;

previous_in_chain_plus        : LIST OF GENERIC:cgen := [];

result                        : BOOLEAN := true;

set_of_types                  : SET OF STRING := [];

END_LOCAL;

IF EXISTS(set_of_input_instances) THEN

number_of_input_instances := SIZEOF(set_of_input_instances);

(* Add the declared type of bag_of_referring_instances to the set of

types of the REFERENCEd instances for the subset comparison later.

*)

set_of_input_types := set_of_input_types + 'GENERIC';

REPEAT i:=1 TO number_of_input_instances;

(* Determine all references to the current input instance. *)

bag_of_referring_instances := USEDIN (set_of_input_instances[i] , '');

IF EXISTS(bag_of_referring_instances) THEN

number_of_referring_instances := SIZEOF(bag_of_referring_instances);

dependently_instantiated_flag := false;

REPEAT j:=1 TO number_of_referring_instances;

(* Determine the type strings of the current referencing instance.

*)

set_of_types := TYPEOF(bag_of_referring_instances[j]);

(* If the referencing instance is of one of the types of the

only dependently instantiable select items, the current input

instance may still be invalidly instantiated.

Otherwise it is OK, and the next input instance is tested.

*)

IF set_of_types <= set_of_input_types THEN -- subset operator

(* The referring instance is of one of the restricted types.

However, it may itself be referred to by a valid instance;

then also the current instance would be valid.

Thus, call this function recursively with the referring

instance as input.

To avoid an infinite loop in case a set of instances

reference each other in a closed loop, test first whether

the current referencing instance is in the list of

previously processed chain members.

*)

IF NOT (bag_of_referring_instances[j] IN previous_in_chain) THEN

previous_in_chain_plus := previous_in_chain +

set_of_input_instances[i];

IF dependently_instantiated([bag_of_referring_instances[j]],

set_of_input_types,

previous_in_chain_plus) THEN

dependently_instantiated_flag := true;

ESCAPE; -- dependently instantiated; next input instance

ELSE

(* Not dependently instantiated: go to next referring

instance. *)

SKIP;

END_IF;

END_IF;

ELSE

dependently_instantiated_flag := true;

ESCAPE; -- dependently instantiated; take next input instance

END_IF;

END_REPEAT;

IF NOT dependently_instantiated_flag THEN

RETURN(false);

END_IF;

ELSE

RETURN(false); -- not referenced at all => invalidly instantiated

END_IF;

END_REPEAT;

ELSE

RETURN(false); -- no input

END_IF;

RETURN(true);

END_FUNCTION; -- end dependently_instantiated

END_SCHEMA;

# Comments

Do we really need a composite  shape aspect for cases of multiple geometric elements representing the feature? Can't we just use itemize them in the shape aspect? Also, what shape representation to use, open shell or solid b-rep? Should face sets be connected via LK's shape rep or just a collection of faces without order?